|  | United Nations | ECE/TRANS/WP.29/2011/29 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 21 December 2010 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

153rd session

Geneva, 8–11 March 2011

Item 4.10.13 of the provisional agenda

1958 Agreement – Consideration of draft Corrigenda

to existing Regulations submitted by GRE

Proposal for Corrigendum 1 to the 01 series of amendments to Regulation No. 98 (Headlamps with gas-discharge light sources)

Submitted by the Working Party on Lighting and Light-Signalling*

The text reproduced below was adopted by the Working Party on Lighting and Light-Signalling (GRE) at its sixty-fourth session. It is based on informal document GRE-64-19, as reproduced in Annex IX to the report. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration (ECE/TRANS/WP.29/GRE/64, para. 34).

Insert a new paragraph 13.2., to read:

"13.2.	Until 60 months after the date of entry into force of the 01 series of amendments to this Regulation with regard to the changes introduced by the 01 series of amendments concerning the photometric testing procedures involving the use of the spherical coordinate system and the specification of luminous intensity values, and in order to allow the Technical Services to update their testing equipment, no Contracting Party applying this Regulation shall refuse to grant approvals under this Regulation as amended by the 01 series of amendments where existing testing equipment is used with suitable conversion of the values, to the satisfaction of the authority responsible for type approval."

Paragraphs 13.2. to 13.4. (former), renumbered as paragraphs 13.3. to 13.5.

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2006–2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.