|  | United Nations | ECE/TRANS/WP.29/2011/38 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 23 December 2010 English Original: English and French |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

153rd session

Geneva, 8–11 March 2011

Item 4.8.6 of the provisional agenda

1958 Agreement – Consideration of draft amendments
to existing Regulations submitted by GRSG

Proposal for Supplement 5 to Regulation No. 121 (Identification of controls, tell-tales and indicators)

Submitted by the Working Party on General Safety Provisions*

The text reproduced below was adopted by the Working Party on General Safety Provisions (GRSG) at its ninety-ninth session to introduce a symbol for the electronic stability control, improve the references to the braking regulations and update the reference to ISO 2575. It is based on ECE/TRANS/WP.29/GRSG/2010/28, as amended by paragraph 29 of the report (ECE/TRANS/WP.29/GRSG/78, para. 29). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

Table 1, amend to read:

"

| No. | Column 1 | Column 2 | Column 3 | Column 4 | Column 5 |
| --- | --- | --- | --- | --- | --- |
|  | Item | Symbol 2/ | Function | Illumination | Colour |
| …. | … | … | … | … | … |
| 25. | Brake system malfunction | 8/ | Tell-tale | Yes | see Regulations Nos. 13-H and 13 as appropriate |
| …. | … | … | … | … | … |
| 43. | Electronic stability control (including malfunction) | or ESC 17/ | Tell-tale | Yes | see Regulations Nos. 13-H and 13 as appropriate |
| …. | … | … | … | … | … |

1/	…

17/	The vehicle outline shown is not intended to be restrictive, but is the recommended outline.  Alternative vehicle outlines may be used in order to better represent the actual outline of a given vehicle.

18/	Symbol may be shown in other colours than specified in column 5 in order to convey different meanings according to the general colour coding as proposed in paragraph 5 of ISO 2575-2004.

19/	… lowercase letters."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2006–2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.