|  | United Nations | ECE/TRANS/WP.29/2011/94/Amend.1 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 28 September 2011 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

155th session

Geneva, 15–18 November 2011

Item 4.10.1 of the provisional agenda

1958 Agreement – Consideration of amendments to draft Regulations submitted by GRRF

Proposal for amendments to draft Supplement 9 to the 11 series of amendments to Regulation No. 13 (Heavy vehicles braking) *

Submitted by the Working Party on Brakes and Running Gear **

The text reproduced below was adopted by the Working Party on Brakes and Running Gear (GRRF) at its seventy-first session to update the cross references impacted by ECE/TRANS/WP.29/2011/94. It is based on GRRF-71-03 and is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

Annex 11 – Appendix 2

Paragraph 2.2.2.2., amend to read:

"2.2.2.2.	The brake input … to produce diagram 2 of Annex 19-Part 1."

Paragraph 3.5.1., amend to read:

"3.5.1. 	Supplementary cold performance test

The preparation of … with paragraph 4.4.2. of Annex 19-Part 1 of this Regulation.

In the case, … according to paragraph 4.4.3. of Annex 19-Part 1 of this Regulation, …verification according to paragraph 4.4.3. of Annex 19-Part 1.

It is permissible to carry out … in accordance with paragraph 4. of Annex 19-Part 1 of this Regulation.

It is also … one after the other.

Some brake applications according to Annex 19-Part 1, paragraph 4.4.2.6. may be … by the brake manufacturer."

Paragraph 3.8., the second table, row (f), amend to read:

"

| (f) Declared threshold torque C0,dec | It shall be checked that the brake performance remains within the corridors of Diagram 2 of Annex 19-Part1. |
| --- | --- |

"

Paragraph 3.9.1., amend to read:

"3.9.1.	Test report number

The test report … a dot or slash.

The base part … (according to paragraph 4. of Annex 19-Part 1 to this Regulation)."

Paragraph 4.3.1.1., amend to read:

"4.3.1.1.	The predicted actuator … the procedure defined in item paragraph 2. of Annex 19-Part 1 to this Regulation … Appendix 1 of Annex 19."

Annex 11 – Appendix 3

Paragraph 2.3.3., amend to read:

"2.3.3.	This item … defined in paragraph 4. of Annex 19-Part 1 to this Regulation to … brake factor (BF)."

Paragraph 4., amend to read:

"4.	This test … where appropriate paragraph 4. of Annex 19-Part 1 to Regulation No. 13 … amendments."

Annex 19

Paragraph 4.4.2.9., amend to read:

"4.4.2.9.	If the manufacturer …

… The results of at least 3 tests in accordance with paragraph 4.4.3.4. of Annex 19-Part 1 conducted under the conditions of the laden Type-0 test…"

Annex 19 – Appendix 1

Paragraph 3.3.1., amend to read:

"3.3.1.	Pressure range over which the above effective stroke is valid: (see paragraph 2.3.4. of Annex 19-Part 1)."

Annex 20

Paragraph 7.3.1.4., amend to read:

"7.3.1.4.	With the brakes … in accordance with paragraph 5.4.1.2.4.2. of Annex 19-Part 1 to this Regulation, the energy storage …"

Paragraph 7.4.2.1., amend to read

"7.4.2.1.	The relationship of … referred to in paragraph 5.2. of Annex 19-Part 1 to this Regulation."

Paragraph 7.4.8.1., amend to read

"7.4.8.1.	Any installation limitations … referred to in paragraph 5.2. of Annex 19-Part 1 to this Regulation shall apply."

# Footnotes

*	This document has been submitted late in order to include information on the latest progress in this work.

**	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.