|  | United Nations | ECE/TRANS/WP.29/GRE/2010/18 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 14 January 2011 Original: English English and French only |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on Lighting and Light-Signalling

Sixty-fifth session

Geneva, 28–31 March 2011

Item 3 of the provisional agenda

Regulation No. 37 (Filament lamps)

Proposal for Supplement 38 to the 03 series of amendments

Submitted by the expert from the Working Party "Brussels 1952"*

The text reproduced below was prepared by the expert from the Working Party "Brussels 1952" (GTB) in order to phase out some light source categories from Regulation No. 37. The modifications to the existing text of Regulation No. 37, including draft Supplement 37 to the 03 series of amendments (ECE/TRANS/WP.29/2011/10), are marked in bold for new or strikethrough for deleted characters.

Paragraphs 8.3. and 8.4., amend to read:

"8.3.	No filament lamps … the table below:

| Category | Types | Supplement | Period |
| --- | --- | --- | --- |
| C5W | 6V | 38 | 12 months |
| C21W | all | 28 | 12 months |
| H1 | 6 V | 38 | 12 months |
| H3 | 6 V | 38 | 12 months |
| H14 | all | 38 | 12 months |
| HS1 | 6 V | 38 | 12 months |
| HS2 | 6 V | 38 | 12 months |
| P19W | all | 37 | 60 months |
| P21W | 6 V | 38 | 12 months |
| P21/5W | 6 V | 38 | 12 months |
| PC16W | all | 37 | 60 months |
| PCR16W | all | 37 | 12 months |
| PCY16W | all | 37 | 60 months |
| PR19W | all | 37 | 12 months |
| PR24W | all | 37 | 12 months |
| PSR19W | all | 37 | 12 months |
| PSR24W | all | 37 | 12 months |
| PY19W | all | 37 | 60 months |
| R2 | all | 28 | 12 months |
| R5W | 6 V | 38 | 12 months |
| R10W | 6 V | 38 | 12 months |
| RR5W | 6 V | 38 | 12 months |
| RR10W | 6 V | 38 | 12 months |
| RY10W | 6 V | 38 | 12 months |
| S1 | all | 28 | 12 months |
| S2 | all | 38 | 12 months |
| S3 | all | 38 | 12 months |
| T4W | 6 V | 38 | 12 months |
| W3W | 6 V | 38 | 12 months |
| W5W | 6 V | 38 | 12 months |
| W10W | 6 V | 38 | 12 months |
| WY10W | 6 V | 38 | 12 months |

8.4.		However, Contracting Parties … as indicated below:

| Category | Types | Supplement | Period |
| --- | --- | --- | --- |
| C5W | 6V | 38 | unlimited |
| C21W | all | 28 | unlimited |
| H1 | 6 V | 38 | unlimited |
| H3 | 6 V | 38 | unlimited |
| H14 | all | 38 | unlimited |
| HS1 | 6 V | 38 | unlimited |
| HS2 | 6 V | 38 | unlimited |
| P19W | all | 37 | unlimited |
| P21W | 6 V | 38 | unlimited |
| P21/5W | 6 V | 38 | unlimited |
| PC16W | all | 37 | unlimited |
| PCR16W | all | 37 | unlimited |
| PCY16W | all | 37 | unlimited |
| PR19W | all | 37 | unlimited |
| PR24W | all | 37 | unlimited |
| PSR19W | all | 37 | unlimited |
| PSR24W | all | 37 | unlimited |
| PY19W | all | 37 | unlimited |
| R2 | all | 28 | unlimited |
| R5W | 6 V | 38 | unlimited |
| R10W | 6 V | 38 | unlimited |
| RR5W | 6 V | 38 | unlimited |
| RR10W | 6 V | 38 | unlimited |
| RY10W | 6 V | 38 | unlimited |
| S1 | all | 28 | unlimited |
| S2 | all | 38 | unlimited |
| S3 | all | 38 | unlimited |
| T4W | 6 V | 38 | unlimited |
| W3W | 6 V | 38 | unlimited |
| W5W | 6 V | 38 | unlimited |
| W10W | 6 V | 38 | unlimited |
| WY10W | 6 V | 38 | unlimited |

"

Annex 1, the list of categories of filament lamps and their sheets, amend to read:

"....

Group 1

Without general restrictions:

| Category |  | Sheet number(s) |
| --- | --- | --- |
| H1 | *6 | H1/1 to 3 |
| H3 | *6 | H3/1 to 4 |
| H4 |  | H4/1 to 5 |
| H7 |  | H7/1 to 4 |
| H8 |  | H8/1 to 4 |
| H8B |  | H8/1 to 4 |
| H9 | *3 | H9/1 to 4 |
| H9B | *3 | H9/1 to 4 |
| H10 |  | H10/1 to 3 |
| H11 |  | H11/1 to 4 |
| H11B |  | H11/1 to 4 |
| H12 |  | H12/1 to 3 |
| H13 |  | H13/1 to 4 |
| H13A |  | H13/1 to 4 |
| H15 |  | H15/1 to 5 |
| H16 |  | H16/1 to 4 |
| H16B |  | H16/1 to 4 |
| H21W | *2 | H21W/1 to 2 |
| H27W/1 |  | H27W/1 to 3 |
| H27W/2 |  | H27W/1 to 3 |
| HB3 |  | HB3/1 to 4 |
| HB3A |  | HB3/1 to 4 |
| HB4 |  | HB4/1 to 4 |
| HB4A |  | HB4/1 to 4 |
| HIR1 | *3 | HIR1/1 to 3 |
| HIR2 |  | HIR2/1 to 3 |
| HS1 | *6 | HS1/1 to 5 |
| HS2 | *6 | HS2/1 to 3 |
| HS5 |  | HS5/1 to 4 |
| HS5A | *5 | HS5A/1 to 3 |
| HS6 | *4 | HS6/1 to 4 |
| PSX24W | *2 | P24W/1 to 3 |
| PSX26W | *2 | PSX26W1 to 3 |
| PX24W | *2 | P24W/1 to 3 |

Group 2

Only for use in signalling lamps, cornering lamps, reversing lamps and rear registration plate lamps:

| Category |  | Sheet number(s) |  |
| --- | --- | --- | --- |
| C5W | *6 | C5W/1 |  |
| H6W |  | H6W/1 |  |
| H10W/1 |  | H10W/1 to 2 |  |
| HY6W |  | H6W/1 |  |
| HY10W |  | H10W/1 to 2 |  |
| HY21W |  | H21W/1 to 2 |  |
| P13W |  | P13W/1 to 3 |  |
| P21W | *6 | P21W/1 to 2 |  |
| P21/4W |  | P21/4W/1 | (P21/5W/2 to 3) |
| P21/5W | *6 | P21/5W/1 to 3 |  |
| P24W |  | P24W/1 to 3 |  |
| P27W |  | P27W/1 to 2 |  |
| P27/7W |  | P27/7W/1 to 3 |  |
| PR21W |  | PR21W/1 | (P21W/2) |
| PR21/4W |  | PR21/4W/1 | (P21/5W/2 to 3) |
| PR21/5W |  | PR21/5W/1 | (P21/5W/2 to 3) |
| PR27/7W |  | PR27/7W/1 | (P27/7W/2 to 3) |
| PS19W |  | P19W/1 to 3 |  |
| PS24W |  | P24W/1 to 3 |  |
| PSY19W |  | P19W/1 to 3 |  |
| PSY24W |  | P24W/1 to 3 |  |
| PW13W |  | P13W/1 to 3 |  |
| PW16W |  | PC16W/1 to 3 |  |
| PWR16W |  | PC16W/1 to 3 |  |
| PWY16W |  | PC16W/1 to 3 |  |
| PW19W |  | P19W/1 to 3 |  |
| PWR19W |  | P19W/1 to 3 |  |
| PWY19W |  | P19W/1 to 3 |  |
| PW24W |  | P24W/1 to 3 |  |
| PWR24W |  | P24W/1 to 3 |  |
| PWY24W |  | P24W/1 to 3 |  |
| PY21W |  | PY21W/1 | (P21W/2) |
| PY24W |  | P24W/1 to 3 |  |
| PY27/7W |  | PY27/7W/1 | (P27/7W/2 to 3) |
| R5W | *6 | R5W/1 |  |
| R10W | *6 | R10W/1 |  |
| RR5W | *6 | R5W/1 |  |
| RR10W | *6 | R10W/1 |  |
| RY10W | *6 | R10W/1 |  |
| T1.4W |  | T1.4W/1 |  |
| T4W | *6 | T4W/1 |  |
| W2.3W |  | W2.3W/1 |  |
| W3W | *6 | W3W/1 |  |
| W5W | *6 | W5W/1 |  |
| W10W | *6 | W10W/1 |  |
| W15/5W |  | W15/5W/1 to 3 |  |
| W16W |  | W16W/1 |  |
| W21W |  | W21W/1 to 2 |  |
| W21/5W |  | W21/5W/1 to 3 |  |
| WP21W |  | WP21W/1 to 2 |  |
| WPY21W |  | WP21W/1 to 2 |  |
| WR5W |  | W5W/1 |  |
| WR21/5W |  | WR21/5W/1 | (W21/5W/2 to 3) |
| WY2.3W |  | WY2.3W/1 |  |
| WY5W |  | W5W/1 |  |
| WY10W | *6 | W10W/1 |  |
| WY16W |  | W16W/1 |  |
| WY21W |  | WY21W/1 to 2 |  |

Group 3

For replacement purposes only (see transitional provisions of paragraphs 8.3. and 8.4.):

| Category |  | Sheet number(s) |
| --- | --- | --- |
| C5W | *7 | C5W/1 |
| C21W |  | C21W/1 to 2 |
| H1 | *7 | H1/1 to 3 |
| H3 | *7 | H3/1 to 4 |
| H14 |  | H14/1 to 4 |
| HS1 | *7 | HS1/1 to 5 |
| HS2 | *7 | HS2/1 to 3 |
| P19W |  | P19W/1 to 3 |
| P21W | *7 | P21W/1 to 2 |
| P21/5W | *7 | P21/5W/1 to 3 |
| PC16W |  | PC16W/1 to 3 |
| PCR16W |  | PC16W/1 to 3 |
| PCY16W |  | PC16W/1 to 3 |
| PR19W |  | P19W/1 to 3 |
| PR24W |  | P24W/1 to 3 |
| PSR19W |  | P19W/1 to 3 |
| PSR24W |  | P24W/1 to 3 |
| PY19W |  | P19W/1 to 3 |
| R2 |  | R2/1 to 3 |
| R5W | *7 | R5W/1 |
| R10W | *7 | R10W/1 |
| RR5W | *7 | R5W/1 |
| RR10W | *7 | R10W/1 |
| RY10W | *7 | R10W/1 |
| S1 |  | S1/S2/1 to 2 |
| S2 |  | S1/S2/1 to 2 |
| S3 |  | S3/1 |
| T4W | *7 | T4W/1 |
| W3W | *7 | W3W/1 |
| W5W | *7 | W5W/1 |
| W10W | *7 | W10W/1 |
| WY10W | *7 | W10W/1 |

*	Tables, Electrical and Photometric characteristics:

Voltage is expressed in V;

Wattage is expressed in W;

Luminous flux is expressed in lm.

In a case that for a category of filament lamp more than one value of reference luminous flux is specified, the value at approximately 12 V for approval of a lighting device and 13.5 V for approval of a light-signalling device shall be applied unless otherwise specified by the regulation used for the approval of the device.

*2	Not for use in passing beam headlamps.

*3	Not for use in front fog lamps marked "B" as defined in Regulation No. 19.

*4	Not for use in Regulation No. 112 headlamps.

*5	Not for use in headlamps other than Regulation No. 113 class C headlamps

*6	All types except from 6 V type

*7	6 V types only "

II.	Justification

1.	With the introduction of new light source categories, GTB regularly evaluates which light source categories could be phased out based upon technological progress and our evaluation of the need to keep these categories in the regulation. This is such a proposal.

2.	The proposal is not aimed at completely deleting categories of light sources from Regulation No. 37, but at moving some categories or types of categories from group 1 and group 2 to group 3 of Annex 1. In this way, these categories of light sources can still be approved and used as replacement parts. However, they can no longer be used for type approval of new lamps, unless these lamps are intended as replacement parts for vehicles in use.

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106, ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.