| Submitted by the expert from ETRTO | Informal document No. GRRF-71-04 (71st GRRF, 13-15 September 2011 agenda item 6(d)) |
| --- | --- |

Proposal for corrigendum to document ECE/TRANS/WP.29/GRRF/2011/30 - (ETRTO) - 
Proposal for amendments to Regulation No. 117 (Tyre rolling noise and wet grip adhesion) (C3 tyres)

The changes to Regulation No. 117 indicated in bold and strikethrough characters in GRRF/2011/30 are assumed to be adopted, and the changes to document GRRF/2011/30 are shown in bold for new or strikethrough for deleted characters.

I.	Proposal

Paragraph 2.16., amend to read:

"2.16.	"Standard reference test tyre" (SRTT) means a tyre that is produced, controlled and stored in accordance with the ASTM (American Society for Testing and Materials) standards F2870 (2011) for the size 315/70R22.5

(a)	E1136-93 (2003) for the size P195/75R14

(b)	F2872 (2011) for the size 225/75 R 16 C F2871 (2011) for the size 245/70R19.5

(c)	F2870 (2011) for the size 315/70R22.5"

II.	Justification

On one hand, reference to F2872 (2011) for the size 225/75 R 16 C is incorrect as it refers to a C2 tyre. On the other hand, reference to the narrow C3 tyre (F2871 (2011) for the size 245/70R19.5) is missing.