UN/SCEGHS/24/INF.31

Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals Sub-Committee of Experts on the Globally Harmonized System of Classification and Labelling of Chemicals 12 December 2012 Twenty–fourth session Geneva, 12 – 14 December 2012 Item 2 (d) of the provisional agenda Updating of the Globally Harmonized System of Classification and Labelling of Chemicals (GHS): Annexes

Comment on ST/SG/AC.10/C.4/2012/22

Transmitted by the expert from Canada

Issue

1.	The proposals set out in ST/SG/AC.10/C.4/2012/22 were reviewed and a number of minor editorial amendments were identified as required to ensure consistency with terminology used elsewhere in the GHS and within the proposed merged annexes 1 and 2 of the GHS.

Proposal

2.	It is proposed to make amendments to A1.18, A1.19, A1.24, A1.25, A1.26, A1.28(a), A1.28(b) and A1.29 as outlined in the tables below.  Text to be deleted is struck out and text to be added is underlined.

“Annex 1

## CLASSIFICATION AND LABELLING SUMMARY TABLES

## NOTE:  	The codification of hazard statements is further explained in Annex 3 (Section 1). The hazard statement codes are intended to be used for reference purposes only. They are not part of the hazard statement text and should not be used to replace it.

A1.18		Skin corrosion/irritation (see Chapter 3.2 for classification criteria)

| Classification | Labelling |
| --- | --- |
| Hazard class | Hazard category | Pictogram | Signal word | Hazard statement | Code |
|  |  | GHS | UN Model Regulations |  |  |  |
| Skin corrosion/irritation | 1 Corrosive (including A, B and C) |  |  | Danger | Causes severe skin burns and eye damage | H314 |
|  | 2 Irritant |  | Not required | Warning | Causes skin irritation | H315 |
|  | 3a Mild irritanta | No pictogram | Not required | Warning | Causes mild skin irritation | H316 |

a	Applies to some authorities.

A1.19		Serious eye damage/eye irritation (see Chapter 3.3 for classification criteria)

| Classification | Labelling |
| --- | --- |
| Hazard class | Hazard category | Pictogram | Signal word | Hazard statement | Code |
|  |  | GHS | UN Model Regulations |  |  |  |
| Serious eye damage/eye irritation | 1 Irreversible effects |  | Not required | Danger | Causes serious eye damage | H318 |
|  | 2/2A Irritant |  | Not required | Warning | Causes serious eye irritation | H319 |
|  | 2B Mild irritant | No pictogram | Not required | Warning | Causes eye irritation | H320 |

A1.24		Toxic to reproduction Reproductive toxicity (see Chapter 3.7 for classification criteria)

| Classification | Labelling |
| --- | --- |
| Hazard class | Hazard category | Pictogram | Signal word | Hazard statement | Code |
|  |  | GHS | UN Model Regulations |  |  |  |
| Toxic to reproduction Reproductive toxicity | 1 (both 1A and 1B) |  | Not required | Danger | May damage fertility or the unborn child (state specific effect if known) (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) | H360 |
|  | 2 |  | Not required | Warning | Suspected of damaging fertility or the unborn child (state specific effect if known) (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) | H361 |
|  | Additional category for effects on or via lactation | No pictogram | Not required | No signal word | May cause harm to breast-fed children | H362 |

### A1.25		Specific target organ toxicity following - single exposure (see Chapter 3.8 for classification criteria)

| Classification | Labelling |
| --- | --- |
| Hazard class | Hazard category | Pictogram | Signal word | Hazard statement | Code |
|  |  | GHS | UN Model Regulations |  |  |  |
| Specific target organ toxicity following - single exposure | 1 |  | Not required | Danger | Causes damage to organs (or state all organs affected, if known) (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) | H370 |
|  | 2 |  | Not required | Warning | May cause damage to organs (or state all organs affected, if known) (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) | H371 |
|  | 3 |  | Not required | Warning | May cause respiratory irritation or May cause dizziness or drowsiness | H335 H336 |

### A1.26		Specific target organ toxicity following - repeated exposure (see Chapter 3.9 for classification criteria)

| Classification | Labelling |
| --- | --- |
| Hazard class | Hazard category | Pictogram | Signal word | Hazard statement | Code |
|  |  | GHS | UN Model Regulations |  |  |  |
| Specific target organ toxicity following - repeated exposure | 1 |  | Not required | Danger | Causes damage to organs (state all organs affected, if known) through prolonged or repeated exposure (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) | H372 |
|  | 2 |  | Not required | Warning | May cause damage to organs (state all organs affected, if known) through prolonged or repeated exposure(state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) | H373 |

A1.28 (a)	Short-term (acute) hazards to the aquatic environment Hazardous to the aquatic environment Short-term (acute) (see Chapter 4.1 for classification criteria)

| Classification | Labelling |
| --- | --- |
| Hazard class | Hazard category | Pictogram | Signal word | Hazard statement | Code |
|  |  | GHS | UN Model Regulationsa |  |  |  |
| Short-term (Acute) hazards to the aquatic environment Hazardous to the aquatic environment Short-term (acute) | Acute 1 |  |  | Warning | Very toxic to aquatic life | H400 |
|  | Acute 2 | No pictogram | Not required | No signal word | Toxic to aquatic life | H401 |
|  | Acute 3 | No pictogram | Not required | No signal word | Harmful to aquatic life | H402 |

a	For category 1, under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations, the pictogram is not required if the substance presents any other hazards covered by UN Model Regulations. If no other hazard is presented, this pictogram is required as a mark in addition to the UN Model Regulations Class 9 label.

# A1.28 (b)	Long-term (chronic) hazards to the aquatic environment Hazardous to the aquatic environment Long-term (chronic) (see Chapter 4.1 for classification criteria)

| Classification | Labelling |
| --- | --- |
| Hazard class | Hazard category | Pictogram | Signal word | Hazard statement | Code |
|  |  | GHS | UN Model Regulationsa |  |  |  |
| Long-term (Chronic) hazards to the aquatic environment Hazardous to the aquatic environment Long-term (chronic) | Chronic 1 |  |  | Warning | Very toxic to aquatic life with long lasting effects | H410 |
|  | Chronic 2 |  |  | No signal word | Toxic to aquatic life with long lasting effects | H411 |
|  | Chronic 3 | No pictogram | Not required | No signal word | Harmful to aquatic life with long lasting effects | H412 |
|  | Chronic 4 | No pictogram | Not required | No signal word | May cause long lasting harmful effects to aquatic life | H413 |

a	For categories 1 and 2, under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations, the pictogram is not required if the substance presents any other hazards covered by UN Model Regulations. If no other hazard is presented, this pictogram is required as a mark in addition to the UN Model Regulations Class 9 label.

A1.29 		Hazardous to the ozone layer (see Chapter 4.2 for classification criteria)

| Classification | Labelling |
| --- | --- |
| Hazard class | Hazard category | Pictogram | Signal word | Hazard statement | Code |
|  |  | GHS | UN Model Regulations |  |  |  |
| Hazardous to the ozone layer | 1 |  | Not required | Warning | Harms public health and the environment by destroying ozone in the upper atmosphere | H420 |