|  | United Nations | ECE/TRANS/WP.15/2012/6 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 15 February 2012 Original: English |

Economic Commission for Europe

Inland Transport Committee

Working Party on the Transport of Dangerous Goods

Ninety-second session

Geneva, 7–11 May 2012

Item 6 (c) of the provisional agenda

Proposals for amendments to Annexes A and B of ADR:
new proposals

Amendments to Chapter 8.5, additional requirement S1(4)(d)

Transmitted by the government of Norway

Summary

Executive summary: Proposal to solve a practical problem related to the use of the term “vehicle” in Chapter 8.5, S1 concerning loading and unloading of Class 1 explosives. Action to be taken: Replace the word “vehicles” with “transport units” in Chapter 8.5, S1(4)(d). Related documents: None.

Introduction

1.	In Chapter 8.5, S1(4)(d) deals with loading and unloading of Class 1, and reads: “When vehicles carrying substances and articles of Class 1 are obliged to stop for loading or unloading operations in a public place, a distance of at least 50 m shall be maintained between the stationary vehicles.”.

2.	A transport unit is defined as a motor vehicle without an attached trailer, or a combination consisting of a motor vehicle and an attached trailer. Presumably, it has never been the intent to require 50 metre separation between a trailer and its towing vehicle during loading and unloading. Such separation creates a practical problem in relation to efficient loading and unloading as well as effective supervision of the vehicles.

3.	The situation of having Class 1 goods on both the towing vehicle and the trailer is not uncommon. In Norway it is common practice to separate transport of Class 1 compatibility group B and D, by loading the compatibility group B only on one of the vehicles in the transport unit.

Proposal

4.	We propose to replace the word “vehicles” with “transport units” in S1(4)(d) in Chapter 8.5 as follows:

“When vehicles transport units carrying substances and articles of Class 1 are obliged to stop for loading or unloading operations in a public place, a distance of at least 50 m shall be maintained between the stationary vehicles transport units.”.

Justification

5.	The proposed new wording will solve a practical problem, and it will come into line with the wording in the subsequent subsection relating to vehicles in convoys, (see S1(5)(a) in Chapter 8.5).

# Footnotes

The present document is submitted in accordance with paragraph 1(c) of the terms of reference of the Working Party, as contained in document ECE/TRANS/WP.15/190/Add.1, which provides a mandate to “Develop and update the European Agreement concerning the International Carriage of Dangerous Goods by Road (ADR)”.