|  | United Nations | ECE/TRANS/WP.29/2012/18 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 22 December 2011 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

156th session

Geneva, 13–16 March 2012

Item 4.9.12 of the provisional agenda

1958 Agreement – Consideration of draft amendments

to existing Regulations submitted by GRE

Proposal for Supplement 1 to the 01 series of amendments to Regulation No. 119 (Cornering lamps)

Submitted by the Working Party on Lighting and Light-Signalling *

The text reproduced below was adopted by the Working Party on Lighting and Light-Signalling (GRE) at its sixty-sixth session in order to clarify Regulation No. 119. It is based on GRE-66-05, as reproduced in Annex VII to the report (ECE/TRANS/WP.29/GRE/66, para. 49). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

Existing paragraphs 8. to 8.2., delete and replace with a new paragraph 8., to read:

"8.	Colour of light emitted

The colour of the light emitted inside the field of the light distribution grid defined in paragraph 2. of Annex 3 shall be white. For testing see Annex 4 to this Regulation.  Outside this field, no sharp variations of colour shall be observed."

Annex 4, paragraph 1., amend to read:

"1. 	For checking the colorimetric characteristics, a source of light at a colour temperature of 2,856 K, corresponding to illuminant A of the international commission (CIE), shall be used.  For lamps equipped with non-replaceable light sources (filament lamps and other), or light sources (replaceable or non-replaceable) operated together with an electronic light source control gear, the colorimetric characteristics should be verified with the light sources present in the lamp, in accordance with paragraph 7 of this Regulation."

________________

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106, ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.