|  | United Nations | ECE/TRANS/WP.29/GRE/2013/3/Corr.1 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 28 January 2013 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on Lighting and Light-Signalling

Sixty-ninth session

Geneva, 8–11 April 2013

Item 10 of the provisional agenda

Regulation No. 10 (Electromagnetic compatibility)

Proposal for the 05 series of amendments to Regulation No. 10 (Electromagnetic compatibility)

Note by the Secretariat*

The text reproduced below was prepared by the Secretary to GRE, based on the document ECE/TRANS/WP.29/GRE/2013/3. It is proposing some corrections, mainly to the figures, to the original text. The modifications are marked in bold for new or strikethrough for deleted characters. In order to simply the work of the experts, some annexes and appendixes have been completely reproduced.

I.		Proposal

Paragraph 6.10.5., correct to read:

"6.10.5.	Emission of transient conducted disturbances generated by ESAs on 12/24 V supply lines

ESAs that are not switched, contain no switches or do not include inductive loead load need not be tested for transient conducted emission and shall be deemed to comply with paragraph 6.9. 6.7."

Paragraph 13.5., correct to read:

"13.3.1.	As from 28 October 2014 (36 months after the official date of entry into force of this Regulation, as amended by the 04 series of amendments,) ), Contracting Parties applying this Regulation shall grant approvals only if the vehicle type, component or separate technical unit, to be approved meets the requirements of this Regulation as amended by the 04 series of amendments."

Annex 4, Appendix, correct to read:

"Annex 4 – Appendix

# Figure 1

Clear horizontal surface free of electromagnetic reflection delimitation of the surface defined by an ellipse

# Figure 2

Position of antenna in relation to the vehicle

Figure 2a

Dipole antenna in position to measure the vertical radiation components

Figure 2b

Dipole antenna in position to measure the horizontal radiation components

# Figure 3

Vehicle in configuration "REESS charging mode" coupled to the power grid

Example of test set-up for vehicle with plug located on vehicle side 
(AC powered without communication)

# Figure 3a

Elevation

Figure 3b

Plane

Legend

1 	Vehicle under test

2 	Insulating support

3 	Charging cable

4 	Artificial Network(s) grounded

5 	Power mains socket

# Vehicle in configuration "REESS charging mode" coupled to the power grid

Example of test setup for vehicle with plug located front/rear of vehicle 
(AC powered without communication)

# Figure 3c

# Figure 3d

Legend

1 	Vehicle under test

2 	Insulating support

3 	Charging cable

4 	Artificial Network(s) grounded

5 	Power mains socket

# Vehicle in configuration "REESS charging mode" coupled to the power grid

# Example of test set-up for vehicle with plug located on vehicle side 
(AC or DC powered with communication)

Figure 3e

Figure 3f

Legend

1 	Vehicle under test

2 	Insulating support

3 	Charging / communication cable

4 	AC or DC Artificial Network(s) grounded

5 	Power mains socket

6 	Impedance Stabilization(s) grounded

7 	Charging Station

# Vehicle in configuration "REESS charging mode" coupled to the power grid

# Example of test setup for vehicle with plug located front/rear of the vehicle 
(AC or DC powered with communication)

Figure 3g

Figure 3h

Legend

1 	Vehicle under test

2 	Insulating support

3 	Charging / communication cable

4 	AC or DC Artificial Network(s) grounded

5 	Power mains socket

6 	Impedance Stabilisation(s) grounded

7 	Charging Station

Annex 6, Appendix 1, correct to read:

"Annex 6 – Appendix 1

Figure 1

Figure 2

# Figure 3

# Figure 4

Vehicle in configuration "REESS in charging mode coupled to the power grid"

Example of test set-up for vehicle with plug located on the vehicle side 
(AC power charging without communication)

Figure 4a

Figure 4b

Legend

1 	Vehicle under test

2 	Insulating support

3 	Charging cable

4 	Artificial Network(s) grounded

5 	Power mains socket

Example of test set-up for vehicle with plug located front / rear of vehicle (AC power charging without communication)

Figure 4c

Figure 4d

Legend

1 	Vehicle under test

2 	Insulating support

3 	Charging cable

4 	Artificial Network(s) grounded

5 	Power mains socket

Example of test set-up for vehicle with plug located on vehicle side (AC or DC power charging with communication)

Figure 4e

Figure 4f

Legend

1 	Vehicle under test

2 	Insulating support

3 	Charging / communication cable

4 	AC or DC Artificial Network(s) grounded

5 	Power mains socket

6 	Impedance Stabilisation(s) grounded

7 	Charging Station

Example of test set-up for vehicle with plug located front / rear of the vehicle (AC or DC power charging with communication)

Figure 4g

Figure 4h

Legend

1 	Vehicle under test

2 	Insulating support

3 	Charging / communication cable

4 	AC or DC Artificial Network(s) grounded

5 	Power mains socket

6 	Impedance Stabilisation(s) grounded

7 	Charging Station

# "

Annex 7, Appendix, new Figure 2, correct to read

"Figure 2

Test configuration for ESAs involved in "REESS charging mode coupled to the power grid" (example for biconical antenna)

| Legend: 1 ESA (grounded locally if required in test plan) 2 LV Test harness 3 LV Load simulator (placement and ground connection according to CISPR 25 paragraph 6.4.2.5) 4 Power supply (location optional) 5 LV Artificial network (AN) 6 Ground plane (bonded to shielded enclosure) 7 Low relative permittivity support (εr ≤ 1.4) 8 Biconical antenna 10 High-quality coaxial cable e.g. double-shielded (50 Ω) | 11 Bulkhead connector 12 Measuring instrument 13 RF absorber material 14 Stimulation and monitoring system 15 HV harness 16 HV load simulator 17 HV AN 18 HV power supply 19 HV feed-through 25 AC/DC charger harness 26 AC/DC load simulator (e.g. PLC) 27 50µH LISN (AC) or HVAN (DC) 28 AC/DC power supply 29 AC/DC feed-through |
| --- | --- |

"

Annex 11, Appendix 1, correct to read:

"Annex 11 – Appendix 1

Figure 1

Vehicle in configuration "REESS charging mode coupled to the power grid" – Single phase charger test set-up

Figure 2

Vehicle in configuration "REESS charging mode coupled to the power grid" – Three-phase charger test set-up

"

Annex 12, Appendix 1, correct to read:

"Annex 12 – Appendix 1

Figure 1a

Vehicle in configuration "REESS charging mode coupled to the power grid" – Single phase test set-up

Figure 1b

Vehicle in configuration "REESS charging mode coupled to the power grid" – Three phase test set-up

"

Annex 13, Appendix 1, correct to read:

"Annex 13 – Appendix 1

# Figure 1

Vehicle in configuration "REESS charging mode coupled to the power grid"

Example of test setup for vehicle with plug located on vehicle side (AC powered without communication)

Figure 1a

Figure1b

Legend

1 	Vehicle under test

2 	Insulating support

3 	Charging cable

4 	Artificial Network(s) grounded (for AC or DC power lines)

5 	Power mains socket

6 	Measuring receiver

Vehicle in configuration "REESS charging mode coupled to the power grid"

Example of test setup for vehicle with plug located front / rear of vehicle (AC powered without communication)

Figure 1c

Figure 1d

Legend

1 	Vehicle under test

2 	Insulating support

3 	Charging cable

4 	Artificial Network(s) grounded (for AC or DC power lines)

5 	Power mains socket

6 	Measuring receiver

"

Annex 14, Appendix 1, correct to read:

"Annex 14 – Appendix 1

# Figure 1

Vehicle in configuration "REESS charging mode coupled to the power grid"

Example of test setup for vehicle with plug located on vehicle side (AC or DC powered with communication)

# Figure 1a

# Figure 1b

| Legend 1 Vehicle under test 2 Insulating support 3 Charging / communication cable 4 AC or DC Artificial Network(s) grounded (for AC or DC power lines) | 5 Power mains socket 6 Impedance Stabilization(s) grounded (for communication lines) 7 Charging Station 8 Measuring receiver |
| --- | --- |

# Vehicle in configuration "REESS charging mode coupled to the power grid"

# Example of test set-up for vehicle with plug located front/rear of vehicle (AC or DC powered with communication)

Figure 1c

Figure 1d

| Legend 1 Vehicle under test 2 Insulating support 3 Charging / communication cable 4 AC or DC Artificial Network(s) grounded (for AC or DC power lines) | 5 Power mains socket 6 Impedance Stabilisation(s) grounded (for communication lines) 7 Charging Station 8 Measuring receiver |
| --- | --- |

Figure 2

Alternative measurement for vehicle in configuration "REESS charging mode coupled in the power grid"

Example of test setup for vehicle with plug located on vehicle side (AC or DC powered with communication)

Figure 2a

Figure 2b

| Legend 1 Vehicle under test 2 Insulating support 3 Charging / communication cable 4 AC or DC Artificial Network(s) grounded (for AC or DC power lines) | 5 Power mains socket 7 Charging Station 8 Current probe 9 Communication lines 10 Measuring receiver 11 Capacitive voltage probe |
| --- | --- |

Alternative measurement for vehicle in configuration "REESS charging mode coupled in the power grid"

Example of test setup for vehicle with plug located front / rear of vehicle (AC or DC powered with communication)

Figure 2c

Figure 2d

| Legend 1 Vehicle under test 2 Insulating support 3 Charging / communication cable 4 AC or DC Artificial Network(s) grounded (for AC or DC power lines) | 5 Power mains socket 7 Charging Station 8 Current probe (or capacitive voltage probe) 9 Communication lines 10 Measuring receiver 11 Capacitive voltage probe |
| --- | --- |

Annex 15, Appendix 1, correct to read:

"Annex 15 – Appendix 1

Figure 1

Vehicle in configuration "REESS charging mode" coupled to the power grid coupling on AC/DC power lines

"

Annex 16, Appendix 1, correct to read:

"Annex 16 – Appendix 1

Vehicle in configuration "REESS charging mode coupled to the power grid

# Figure 1

Vehicle in configuration "REESS charging mode coupled to the power grid" – Coupling between lines for DC or AC (single phase) power lines

# Figure 2

Vehicle in configuration "REESS charging mode coupled to the power grid" – Coupling between each line and earth for DC or AC (single phase) power lines

# Figure 3

Vehicle in configuration "REESS charging mode coupled to the power grid" – Coupling between lines for AC (three phases) power lines

Figure 4

Vehicle in configuration "REESS charging mode coupled to the power grid" – Coupling between each line and earth for AC (three phases) power lines

"

Annex 17, Appendix 1, correct to read:

"Annex 17 – Appendix 1

# Figure 1

ESA in configuration "REESS charging mode coupled to the power grid" – Single phase test set-up

# Figure 2

ESA in configuration "REESS charging mode coupled to the power grid" –Three-phase test set-up

"

Annex 18, Appendix 1, correct to read:

"Annex 18 – Appendix 1

# Figure 1a

ESA in configuration "REESS charging mode coupled to the power grid"- Single phase test set-up

# Figure 1b

ESA in configuration "REESS charging mode coupled to the power grid" - Three-phase test set-up

"

Annex 20, Appendix 1, correct to read:

"Annex 20 – Appendix 1

# Figure 1

ESA in configuration "REESS charging mode coupled to the power grid"

Legend

1 	ESA under test

2 	Insulating support

3 	Charging / communication cable

4 	AC or DC Artificial Network(s) grounded

5 	Power mains socket

6 	Impedance Stabilization(s) grounded

7 	Charging Station

"

Annex 21, Appendix 1, correct to read:

"Annex 21 –	Appendix 1

# Figure 1

ESA in configuration "REESS charging mode coupled to the power grid

"

II.	Justification

1.	Some corrections are proposed by the secretariat and OICA to clarify the proposal.

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106, ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.

# Text boxes

G

RA

jXA

RN

jXN

L1

N

M

Measurement device

Power supply with open circuit voltage G and 
(RP + j XP) impedance

Maximum length 10m

Cable shall be z-folded if longer than 10m, 100 ± 25mm above ground and at least 100mm from the car body

0.8 (+0.2 / -0) m

Maximum length 10m

Power supply with open circuit voltage G and (RP + j XP) impedance

Measurement device

Cable shall be z-folded if longer than 10m, 100 ± 25mm above ground and at least 100mm from the car body

Measurement device with input impedance ZM

Power supply of internal impedance Zs and open circuit voltage G

ESA

maximum cable

length 10m

Measurement device with input impedance ZM

Power supply of internal impedance Zs and open circuit voltage G

ESA

maximum cable

length 10m

ESA

G

RA

jXA

RN

jXN

L1

N

M

Measurement device

Power supply with open circuit voltage G and 
(RP + j XP) impedance

Measurement device

Power supply with open circuit voltage G and (RP + j XP) impedance

ESA

0.8 (+0.2 / -0) m

4

5

1

2

3

5

0.5 m max

Top view

6

7

ESA

Cable shall be z-folded if longer than 1m, 100 ± 25mm above ground and at least 100mm from the ESA body

2

0.8 (+0.2 / -0) m

4

5

1

2

3

5

0.5 m max

Top view

6

7

ESA

Cable shall be z-folded if longer than 1m, 100 ± 25mm above ground and at least 100mm from the ESA body

Ground Plane