| Transmitted by the expert from Japan | Informal document GRPE-64-05 (64th GRPE, 5-8 June 2012, agenda item 7) |
| --- | --- |

Proposal for corrigendum to global technical regulation (gtr) No. 2

(ECE/TRANS/180/Add.2/Amend.1)

I.		Proposal

Paragraph 8.1.1.4.2.	, replace the Equation 8-2 as below:

“8.1.1.4.2. Hydrocarbons

… by means of the following formula:

|  | Equation 8-2 |
| --- | --- |

…”

Paragraph 8.1.1.4.3., replace the Equation 8-4 as below:

“8.1.1.4.3.	Carbon monoxide

…by means of the following formula:

|  | Equation 8-4 |
| --- | --- |

…”

Paragraph 8.1.1.4.4., replace the Equation 8-6 as below:

“8.1.1.4.4.	Nitrogen oxides

…by means of the following formula:

|  | Equation 8-6 |
| --- | --- |

…”

Paragraph 8.1.1.4.5., replace the Equation 8-10 as below:

“8.1.1.4.5.	Carbon dioxide

… by means of the following formula:

| × 10 | Equation 8-10 |
| --- | --- |

…”

Annex 13, paragraph 1 Figure A13-1, correct the line for “acc.gear 1” in the upper figure for “gear use during acceleration phases” as shown below.

II.	Justification

1.	Paragraph 8

The equations 8-2, 8-4, 8-6, and 8-10 need to be corrected in accordance with the unit of each factor in the equation.  The calculated pollutants are shown in kg/km, while the V is in m3 and dHC in kg/m3, which means the value needs to be multiplied by 10-3 (by 10 for CO2) and the denominator needs to be corrected accordingly.

2.	Annex 13, paragraph 1 Figure A13-1

In the upper figure for “gear use during acceleration phases”, the acceleration gear 1 starts from zero, which is not correct.

# Text boxes

3

3

3