|  | United Nations | ECE/TRANS/WP.29/2013/7 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 13 December 2012 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

159th session

Geneva, 12-15 March 2013

Item 4.7.2 of the provisional agenda

1958 Agreement – Consideration of draft amendments 
to existing Regulations submitted by GRRF

Proposal for Supplement 3 to the 02 series of amendments to Regulation No. 117 (Tyres: Rolling resistance, rolling noise and wet grip)

Submitted by the Working Party on Brakes and Running Gear*

The text reproduced below was adopted by the Working Party on Brakes and Running Gear (GRRF) at its secenty-third session (ECE/TRANS/WP.29/GRRF/73, para. 28). It is based on ECE/TRANS/WP.29/GRRF/2012/18. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee AC.1 for consideration.

Annex 6, paragraph 6.2., amend to read:

"6.2.	Temperature correction

If measurements at temperatures other than 25 (C are unavoidable (only temperatures not less than 20 (C or more than 30 (C are acceptable), then a correction for temperature shall be made using the following equation, with:

is the rolling resistance at 25 (C, in Newton:

| Where: |  |  |
| --- | --- | --- |
|  |  | is the rolling resistance, in Newton, |
|  |  | is the ambient temperature, in degree Celsius, |
|  |  | is equal to: 0.008 for Class C1 tyres 0.010 for Class C2 and C3 tyres with a load index equal or lower than 121 0.006 for Class C3 tyres with a load index greater than 121" |

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.