|  | United Nations | ECE/TRANS/WP.29/2013/13 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 21 December 2012 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

159th session

Geneva, 12-15 March 2013

Item 4.9.1 of the provisional agenda

1958 Agreement – Consideration of draft amendments

to existing Regulations submitted by GRE

Proposal for Supplement 14 to the 02 series of amendments to UN Regulation No. 3 
(Retro-reflecting devices for power-driven vehicles)

Submitted by the Working Party on Lighting and Light Signalling *

The text reproduced below was adopted by the Working Party on Lighting and Light Signalling (GRE) at its sixty-eighth session (ECE/TRANS/WP.29/GRE/68, para. 23). It is based on ECE/TRANS/WP.29/GRE/2012/42, not amended. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee AC.1 for consideration.

Annex 7

Insert a new paragraph 3.2., to read:

"3.2.	However, in the case where a retro-reflecting device of Class IA, Class IB, Class IIIA or Class IIIB is intended to be installed with its H plane at a mounting height less than 750 mm above the ground, the CIL values are verified only up to an angle of 5° downwards."

Paragraph 3.2. ( former), renumber as paragraph 3.3.

Insert a new paragraph 3.4., to read:

"3.4.		However, in the case where a retro-reflecting device of Class IVA is intended to be installed with its H plane at a mounting height less than 750 mm above the ground, the CIL values are verified only up to an angle of 5° downwards."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.