|  | United Nations | ECE/TRANS/WP.29/2013/15 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 21 December 2012 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

159th session

Geneva, 12-15 March 2013

Item 4.9.3 of the provisional agenda

1958 Agreement – Consideration of draft amendments

to existing Regulations submitted by GRE

Proposal for Supplement 22 to the 02 series of amendments to Regulation No. 7 (Position, stop and end-outline lamps)

Submitted by the Working Party on Lighting and Light Signalling *

The text reproduced below was adopted by the Working Party on Lighting and Light Signalling (GRE) at its sixty-eighth session (ECE/TRANS/WP.29/GRE/68, paras. 22 and 23). It is based on ECE/TRANS/WP.29/GRE/2012/41, as amended by para. 22 of the report and ECE/TRANS/WP.29/GRE/2012/42, as amended by Annex IV (ECE/TRANS/WP.29/GRE/68, paras. 22 and 23). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee AC.1 for consideration.

Paragraphs 6.2.4. and 6.2.4.1., amend to read:

"6.2.4.		Moreover,

6.2.4.1.	Throughout the fields defined in the diagrams in Annex 1, the luminous intensity of the light emitted must be not less than 0.05 cd for front and rear position lamps and end-outline marker lamps, not less than 0.3 cd for devices of categories S1, S3 and for those of categories S2 and S4 by day; it shall not be less than 0.07 cd for devices of categories S2 and S4 by night;"

Annex 1, amend to read:

"…

In all cases, the minimum vertical angles of light distribution in space are 15° above and 15° below the horizontal for all categories of devices included in this Regulation, except:

(a)	For lamps intended to be installed with their H plane at a mounting height less than 750 mm above the ground, for which they are 15° above and 5° below the horizontal;

(b)	Optional lamps intended to be installed with their H plane at a mounting height more than 2100 mm above the ground, for which they are 5° above and 15° below the horizontal;

(c)	For category S3 or S4 stop lamp for which they are 10° above and 5° below	the horizontal."

x

Front end outline marker lamp (AM)

Rear end outline marker lamp (RM1,RM2)

Rear position lamps

"

# Stop-lamps (S1 and S2)

Stop-lamps (S3 and S4)

"

Annex 2, item 9, amend to read:

"9. 	Concise description:

9.1. 	By category of lamp:

For mounting either outside or inside or both2:

Colour of light emitted: red / white2

Number, category and kind of light source(s):

Voltage and wattage:

Light source module specific identification code: .

Only for limited mounting height of equal to or less than 750 mm above the ground: yes/no 2/

Geometrical conditions of installation and relating variations, if any: 	."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.

# Text boxes

Front position lamps,

Vehicle

Driving

direction

45°

80°

Reference axis

H plane: "horizontal plane going through the reference centre of the lamp"

20°

80°

Vehicle

Driving

direction

Reference axis

Under the H plane for front position lamps intended to be installed with this plane at a mounting height less than 750 mm above ground.

Vehicle

Vehicle

Reference axis

45°

80°

Driving
direction

Reference axis

20°

80°

Driving
direction

Under the H plane for rear position lamps intended to be installed with this plane at a mounting height less than 750 mm above ground.

Reference axis

45°

45°

Driving
direction

Reference axis

20°

45°

Driving
direction

Under the H plane for stop lamps (S1 and S2) intended to be installed with this plane at a mounting height less than 750 mm above ground.