|  | United Nations | ECE/TRANS/WP.29/2013/130 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 27 August 2013 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

161st session

Geneva, 12-15 November 2013

Item 4.11.1 of the provisional agenda

Consideration of draft corrigenda to existing Regulations submitted by the secretariat
Proposal for Corrigendum 1 to Revision 3 
to Regulation No. 54 (Tyres for commercial vehicles and their trailers)

Proposal for Corrigendum 1 to Revision 3 to Regulation No. 54 (Tyres for commercial vehicles and their trailers)

Note by the Secretariat*

The text reproduced below was prepared by the secretariat to correctly express the symbol of Regroovable tyres as adopted by the Working Party on Brakes and Running Gear (GRRF) and to correctly align the rows of the second column of the table of Annex 7, Appendix 2 to the Regulation.

Paragraph 3.1.9., for the existing symbol substitute

Annex 7, Appendix 2, correct to read:

"

| Pressure Index ("PSI") | Bar | kPa |
| --- | --- | --- |
| 20 | 1.4 | 140 |
| 25 | 1.7 | 170 |
| 30 | 2.1 | 210 |
| 35 | 2.4 | 240 |
| 40 | 2.8 | 280 |
| 45 | 3.1 | 310 |
| 50 | 3.4 | 340 |
| 55 | 3.8 | 380 |
| 60 | 4.1 | 410 |
| 65 | 4.5 | 450 |
| 70 | 4.8 | 480 |
| 75 | 5.2 | 520 |
| 80 | 5.5 | 550 |
| 85 | 5.9 | 590 |
| 90 | 6.2 | 620 |
| 95 | 6.6 | 660 |
| 100 | 6.9 | 690 |
| 105 | 7.2 | 720 |
| 110 | 7.6 | 760 |
| 115 | 7.9 | 790 |
| 120 | 8.3 | 830 |
| 125 | 8.6 | 860 |
| 130 | 9.0 | 900 |
| 135 | 9.3 | 930 |
| 140 | 9.7 | 970 |
| 145 | 10.0 | 1000 |
| 150 | 10.3 | 1030 |
| ... | ... | ... |

"

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.