|  | United Nations | ECE/TRANS/WP.29/GRE/2013/66 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 7 August 2013 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on Lighting and Light-Signalling

Seventieth session

Geneva, 21-23 October 2013

Item 14(d) of the provisional agenda

Other business – Other business

Proposal for Supplement 6 to the 04 series of amendments to Regulation No. 19 (Front fog lamps)

Submitted by the expert from France*

The text reproduced below was prepared by the expert from France introducing the 04 series of amendments for replacement parts in the transitional provisions. The modifications to the current text of the Regulation are marked in bold for new or strikethrough for deleted characters.

I.	Proposal

Paragraph 14.2., amend to read:

"14.2.		As from the date of entry into force of Supplement 2 to the 04 series of amendments, Contracting Parties applying this Regulation shall refuse to grant approvals for new types of Class B front fog lamps. However, Contracting Parties applying this Regulation, shall continue to issue approvals for Class B front fog lamps on the basis of the 02,and 03 and 04 series of amendments provided that these front fog lamps are only intended as replacements for fitting to vehicles in use."

II.	Justification

In the current regulation, class B front fog lamp, on the basis of the 02 and 03 series of amendments, may be approved for replacement purposes only. In the 04 series of amendments to UN Regulation No. 19, 04 B front fog lamps should be allowed in the same circumstances, as well.

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.