Comments on Document ECE/TRANS/WP.29/GRE/2013/14

Proposal for [Supplement 12 to the 04 series of amendments, Supplement 5 to the 05 series of amendments,] Supplement 3 to the 06 series of amendments to Regulation No. 48 (Installation of lighting and light-signalling devices).

I.	Proposal

Proposed modification regarding deletion of text is indicated in strike through and addition with text in italic bold in blue colour.

Insert a new paragraph 2.10.1., to read:

"2.10.1	Horizontal orientation of a direction indicator means the ratio of the length of path of the movement in horizontal direction to that in vertical direction on the apparent surface should not exceed should not be less than the value of [10:6]."

II.	Justification

Minimum ratio of the length of path of the movement in horizontal direction to that in vertical direction on the apparent surface is to be maintained to ensure horizontal orientation of a direction indicator.

_________________