Proposal for amendments to Regulation No. 48

I.	PROPOSAL

Paragraph 6.1.2. shall read:

"6.1.2.	Number

Two or four, type approved according to Regulations Nos. 31, 98, or 112, excluding Class A headlamp.

For vehicles of the category N3: Two extra main-beam headlamps may be installed.

Where a vehicle is fitted with four concealable headlamps the installation of two additional headlamps shall only be authorized for the purpose of light-signalling, consisting of intermittent illumination, at short intervals (see paragraph 5.12.) in daylight."

Paragraph 6.2.2. shall read:

"6.2.2.	Number

Two, type approved according to Regulations Nos. 31, 98, or 112, excluding Class A headlamp."

II.	JUSTIFICATION

After discussion of item 5(f) of the agenda for 69th GRE Session, proposal to “freeze” ECE Regulations N. 5 and 31 from GTB (see document ECE/TRANS/WP29/GRE/2013/5) was approved.

Consequently Italy requested whether the deletion of references to Regulation N. 31 presently existing in paragraphs 6.1.2. and 6.2.2. of Regulation N. 48 should be deleted or not.

GRE agreed on the deletion of these references and requested Italy to prepare an informal document specifying the text of the proposed changes.

The present document is the Italian proposal for deletion of the above indicated references, to avoid confusion and possible incorrect application of the requirements containing these references.

___________________