Proposal for an amendment to ECE/TRANS/WP.29/GRPE/2013/6

Submitted by the chairman of the informal working group on Retrofit Emission Control devices (REC)

The text reproduced below was prepared by the chairman of the informal working group on Retrofit Emission Control devices (REC) as a result of the discussion of the informal group on retrofit emission control devices (REC) regarding a proposal for a new Regulation on REC.

Modifications to the original text of ECE/TRANS/WP.29/GRPE/2013/6 are marked in track changes.

- Proposal

Paragraph 8.2.3., delete:

""

Paragraph 8.4.2., amend to read:

"8.4.2.	For a Class II REC, the NO2 incremental increase shall not be more than 30 percentage points greater than the level recorded when no REC is fitted (baseline). As an example, if baseline NO2 is 10 per cent of NOX, the maximum permitted NO2 emission with the REC is 40 percent of NOX measured as defined in Annex 5."

Annex 8, amend to read:

"Annex 8

Test sequences

1.	Test sequence for particulate reduction REC

2.	Test sequence for NOX reduction REC

3.	Test sequence for particulate and NOX reduction REC

"