|  | United Nations | ECE/TRANS/WP.29/2014/35 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 28 March 2014 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

163rd session

Geneva, 24-27 June 2014

Item 4.6.2 of the provisional agenda

1958 Agreement – Consideration of draft amendments
to existing Regulations submitted by GRSP

Proposal for Supplement 2 to the 03 series of amendments to Regulation No. 29 (Cabs of commercial vehicles)

Submitted by the Working Party on Passive Safety *

The text reproduced below was adopted by the Working Party on Passive Safety (GRPE) at its fifty-fourth session (ECE/TRANS/WP.29/GRSP/54, para. 20). It is based on ECE/TRANS/WP.29/GRSP/2013/19, not amended. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee AC.1 for consideration.

Paragraph 1., amend to read:

"1.	This Regulation applies to vehicles of category N with regard to the protection of the occupants of the cab."

Insert new paragraphs 2.13. and 2.14., to read:

"2.13.	"Vehicles of category N1 derived from M1" means those vehicles of N1 category which, forward of the A-pillars, have the same general structure and shape as a pre-existing M1 category vehicle."

2.14.	"Separate cab" means a cab attached to the vehicle’s frame by specific links and which has no common part with the cargo area."

Paragraph 5.1.2., amend to read:

"5.1.2.	Vehicles of categories N1 and vehicles of categories N2 with a gross vehicle mass not exceeding 7.5 t shall be subjected to the tests A and C, as described in Annex 3, paragraphs 5. and 7..

However a vehicle type which meets the frontal impact requirements of Regulation No. 12 or Regulation No. 33 or Regulation No. 94, and vehicles of category N1, derived from M1 approved to Regulation No. 94, may be considered to have satisfied the requirements on frontal impact (test A).

Test C shall only be conducted on vehicles which have a separate cab."

Paragraph 5.1.3., amend to read:

"5.1.3.	Vehicles of categories N3 and vehicles of categories N2 with a gross vehicle mass exceeding 7.5 t shall be subjected to the tests A, B, and C, as described in Annex 3, paragraphs 5., 6., and 7.

Test C shall only be conducted on vehicles which have a separate cab."

Annex 3,

paragraph 7.3.3., amend to read:

"7.3.3.	The impactor and/or the cab shall be so positioned that, at the moment of impact:"

paragraph 7.3.4., amend to read:

"7.3.4.	The impactor  shall strike the upper side of the cab such that at the time of the impact the prescriptions of paragraph 7.3.3. above are satisfied. The direction of impact shall be perpendicular to the surface of the impactor and perpendicular to the median longitudinal line of the cab. Either the impactor or the cab may be moving, as long as the positioning requirements are satisfied at the moment of impact."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2012–2016 (ECE/TRANS/224, para. 94 and ECE/TRANS/2012/12, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.

As defined in the Consolidated Resolution on the Construction of Vehicles (R.E.3.), document ECE/TRANS/WP.29/78/Rev.2, para. 2. - www.unece.org/trans/main/wp29/wp29wgs/wp29gen/wp29resolutions.html