|  | United Nations | ECE/TRANS/WP.29/2014/48 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 28 March 2014 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

163rd session

Geneva, 24-27 June 2014

Item 4.9.4 of the provisional agenda

1958 Agreement – Consideration of draft amendments
to existing Regulations submitted by GRRF

Proposal for Supplement 14 to Regulation No. 75 (Tyres for motorcycles/mopeds)

Submitted by the Working Party on Brakes and Running Gear *

The text reproduced below was adopted by the Working Party on Brakes and Running Gear (GRRF) at its seventy-fifth session (ECE/TRANS/WP.29/GRRF/75, para. 33). It is based on ECE/TRANS/WP.29/GRRF/2013/21, not amended. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee AC.1 for consideration.

Annex 7

Paragraph 2.5.2., amend to read:

"2.5.2.		Initial tests speed: 30 km/h less than the speed corresponding to the speed category symbol marked on the tyre (see paragraph 2.28.2. of this Regulation) if a 2.0 m diameter test drum is used, or 40 km/h less if a 1.7 m diameter test drum is used."

Paragraph 2.5.2.1., amend to read:

"2.5.2.1.		The initial test speed for the second test in case of tyres suitable for speeds above 240 km/h for tyres identified by means of letter code "V" within the size designation (or 270 km/h for tyres identified by means of letter code "Z" within the size designation) is 30 km/h less than the maximum speed specified by the tyre manufacturer (see paragraph 4.1.15.) if a 2.0 m diameter test drum is used, or 40 km/h less if a 1.7 m diameter test drum is used."

Insert a new paragraph 2.5.6.1. to read:

"2.5.6.1.		The maximum test speed for the second test in case of tyres suitable for speeds above 240 km/h for tyres identified by means of letter code "V" within the size designation (or 270 km/h for tyres identified by means of letter code "Z" within the size designation) is the maximum speed specified by the tyre manufacturer (see paragraph 4.1.15.) if a 2.0 m diameter test drum is used, or 10 km/h less if a 1.7 m diameter test drum is used."

Paragraph 2.6.1., amend to read:

"2.6.1.		Twenty minutes to build up from zero to the initial test speed as specified in paragraph 2.5.2.1."

Paragraph 2.6.3., amend to read:

"2.6.3. 		Ten minutes to build up to the maximum test speed as specified in paragraph 2.5.6.1."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2012–2016 (ECE/TRANS/224, para. 94 and ECE/TRANS/2012/12, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.