Adopted amendments to ECE/TRANS/WP.29/GRRF/2013/20

I.	Proposal

Paragraph 2.1.3., amend to read:

"2.1.3.	… moped, all terrain (AT)."

Add new paragraph 2.16.4.

"2.16.4.	The prefix "AT" for all terrain (AT) tyres (e.g. AT 18x11-8)"

Add new paragraph 2.34.

"2.3.4.		AT (all terrain) tyre:  means a low pressure tyre designed primarily for the equipment of categories L6 and L7. "

Add new paragraph 3.1.15.

"3.1.15.	For all terrain (AT) tyres, the symbol identifying the reference inflation pressure as follows:

| Symbol | Reference Inflation Pressure (kPa) |
| --- | --- |
|  | 25 |
|  | 35 |
|  | 45 |

"

Add new paragraph 4.1.16.

"4.1.16.	For all terrain (AT) tyres, the symbol identifying the reference inflation pressure (see paragraph 3.1.15.)."

Annex 1, paragraph 5.2., amend to read:

"5.2.		… moped, all terrain (AT) 2/"

Annex 1, add a new paragraph 5.6

"5.6.		For all terrain (AT) tyres, the symbol (stars) identifying the reference inflation pressure."

Annex 5, add a new table

"Table 8: Tyres for all terrain vehicles (AT).

Table 8 (1 of 3)

Tyres for all terrain vehicles (AT)

| Tyre size (1) | Measuring rim width code | Section width (mm) | Overall diameter (mm) | Maximum overall width (mm) |
| --- | --- | --- | --- | --- |
|  |  |  | Dmin | D | Dmax |  |
| AT16x6-8 | 5 | 154 | 394 | 406 | 418 | 168 |
| AT16x7-7 | 5.5 | 177 | 392 | 406 | 420 | 193 |
| AT16x8-7 | 6.5 | 204 | 392 | 406 | 420 | 222 |
| AT18x7-7 | 5.5 | 177 | 440 | 457 | 474 | 193 |
| AT18x7-8 | 5.5 | 177 | 442 | 457 | 472 | 193 |
| AT18x8-7 | 6.5 | 204 | 440 | 457 | 474 | 222 |
| AT18x9-8 | 7 | 227 | 442 | 457 | 472 | 247 |
| AT18x9.5-8 | 7.5 | 240 | 442 | 457 | 472 | 262 |
| AT18x10-10 | 8 | 254 | 445 | 457 | 469 | 277 |
| AT18x10-8 | 8 | 254 | 442 | 457 | 472 | 277 |
| AT18x11-10 | 9 | 281 | 445 | 457 | 469 | 306 |
| AT18x11-8 | 9 | 281 | 442 | 457 | 472 | 306 |
| AT18x11-9 | 9 | 281 | 443 | 457 | 471 | 306 |
| AT19x6-10 | 5 | 154 | 469 | 483 | 497 | 168 |
| AT19x7-8 | 5.5 | 177 | 466 | 483 | 500 | 193 |
| AT19x8-8 | 6.5 | 204 | 466 | 483 | 500 | 222 |
| AT19x9-8 | 7 | 227 | 466 | 483 | 500 | 247 |
| AT19x10-9 | 8 | 254 | 468 | 483 | 498 | 277 |
| AT20x7-10 | 5.5 | 177 | 493 | 508 | 523 | 193 |
| AT20x7-8 | 5.5 | 177 | 490 | 508 | 526 | 193 |
| AT20x7-9 | 5.5 | 177 | 491 | 508 | 525 | 193 |
| AT20x8-10 | 6.5 | 204 | 493 | 508 | 523 | 222 |
| AT20x10-10 | 8 | 254 | 493 | 508 | 523 | 277 |
| AT20x10-8 | 8 | 254 | 490 | 508 | 526 | 277 |
| AT20x10-9 | 8 | 254 | 491 | 508 | 525 | 277 |
| AT20x11-10 | 9 | 281 | 493 | 508 | 523 | 306 |
| AT20x11-8 | 9 | 281 | 490 | 508 | 526 | 306 |
| AT20x11-9 | 9 | 281 | 491 | 508 | 525 | 306 |
| AT21x7-10 | 5.5 | 177 | 516 | 533 | 550 | 193 |
| AT21x8-9 | 6.5 | 204 | 515 | 533 | 551 | 222 |
| AT21x10-10 | 8 | 254 | 516 | 533 | 550 | 277 |
| AT21x10-8 | 8 | 254 | 513 | 533 | 553 | 277 |
| AT21x11-8 | 9 | 281 | 513 | 533 | 553 | 306 |
| AT21x11-9 | 9 | 281 | 515 | 533 | 551 | 306 |
| AT21x12-8 | 9.5 | 304 | 513 | 533 | 553 | 331 |
| AT22x7-10 | 5.5 | 177 | 541 | 559 | 577 | 193 |
| AT22x7-11 | 5.5 | 177 | 542 | 559 | 576 | 193 |
| AT22x7-12 | 5.5 | 177 | 544 | 559 | 574 | 193 |
| AT22x7-9 | 5.5 | 177 | 539 | 559 | 579 | 193 |
| AT22x8-10 | 6.5 | 204 | 541 | 559 | 577 | 222 |
| AT22x9-10 | 7 | 227 | 541 | 559 | 577 | 247 |

Table 8 (2 of 3)

Tyres for all terrain vehicles (AT tyres)

| Tyre size (1) | Measuring rim width code | Section width (mm) | Overall diameter (mm) | Maximum overall width (mm) |
| --- | --- | --- | --- | --- |
|  |  |  | Dmin | D | Dmax |  |
| AT22x9-11 | 7 | 227 | 542 | 559 | 576 | 247 |
| AT22x9-8 | 7 | 227 | 538 | 559 | 580 | 247 |
| AT22x10-10 | 8 | 254 | 541 | 559 | 577 | 277 |
| AT22x10-8 | 8 | 254 | 538 | 559 | 580 | 277 |
| AT22x10-9 | 8 | 254 | 539 | 559 | 579 | 277 |
| AT22x11-10 | 9 | 281 | 541 | 559 | 577 | 306 |
| AT22x11-8 | 9 | 281 | 538 | 559 | 580 | 306 |
| AT22x11-9 | 9 | 281 | 539 | 559 | 579 | 306 |
| AT22x12-8 | 9,5 | 304 | 538 | 559 | 580 | 331 |
| AT22.5x10-8 | 8 | 254 | 550 | 572 | 594 | 277 |
| AT23x7-10 | 5.5 | 177 | 564 | 584 | 604 | 193 |
| AT23x8-10 | 6.5 | 204 | 564 | 584 | 604 | 222 |
| AT23x8-11 | 6.5 | 204 | 566 | 584 | 602 | 222 |
| AT23x8-12 | 6.5 | 204 | 567 | 584 | 601 | 222 |
| AT23x10-10 | 8 | 254 | 564 | 584 | 604 | 277 |
| AT23x10-12 | 8 | 254 | 567 | 584 | 601 | 277 |
| AT23x10-8 | 8 | 254 | 561 | 584 | 607 | 277 |
| AT23x11-9 | 9 | 281 | 563 | 584 | 605 | 306 |
| AT23x12-9 | 9,5 | 304 | 563 | 584 | 605 | 331 |
| AT24x8-11 | 6.5 | 204 | 590 | 610 | 630 | 222 |
| AT24x8-12 | 6.5 | 204 | 592 | 610 | 628 | 222 |
| AT24x9-11 | 7 | 227 | 590 | 610 | 630 | 247 |
| AT24x9-12 | 7 | 227 | 592 | 610 | 628 | 247 |
| AT24x10-11 | 8 | 254 | 590 | 610 | 630 | 277 |
| AT24x11-10 | 9 | 281 | 589 | 610 | 631 | 306 |
| AT24x11.5-10 | 9 | 290 | 589 | 610 | 631 | 316 |
| AT24x12-10 | 9,5 | 304 | 589 | 610 | 631 | 331 |
| AT24x13-9 | 10.5 | 330 | 587 | 610 | 633 | 360 |
| AT25x8-10 | 6.5 | 204 | 612 | 635 | 658 | 222 |
| AT25x8-12 | 6.5 | 204 | 615 | 635 | 655 | 222 |
| AT25x8-13 | 6.5 | 204 | 617 | 635 | 653 | 222 |
| AT25x10-10 | 8 | 254 | 612 | 635 | 658 | 277 |
| AT25x10-12 | 8 | 254 | 615 | 635 | 655 | 277 |
| AT25x11-10 | 9 | 281 | 612 | 635 | 658 | 306 |
| AT25x11-12 | 9 | 281 | 615 | 635 | 655 | 306 |
| AT25x11-9 | 9 | 281 | 611 | 635 | 659 | 306 |
| AT25x11.5-9 | 9 | 290 | 611 | 635 | 659 | 316 |
| AT25x12-10 | 9,5 | 304 | 612 | 635 | 658 | 331 |
| AT25x12-9 | 9,5 | 304 | 611 | 635 | 659 | 331 |
| AT25x13-9 | 10.5 | 330 | 611 | 635 | 659 | 360 |

Table 8 (3 of 3)

Tyres for all terrain vehicles (AT tyres)

| Tyre size (1) | Measuring rim width code | Section width (mm) | Overall diameter (mm) | Maximum overall width (mm) |
| --- | --- | --- | --- | --- |
|  |  |  | Dmin | D | Dmax |  |
| AT26x9-12 | 7 | 227 | 639 | 660 | 681 | 247 |
| AT26x10-12 | 8 | 254 | 639 | 660 | 681 | 277 |
| AT26x10.5-12 | 8.5 | 268 | 639 | 660 | 681 | 292 |
| AT26x12-10 | 9.5 | 304 | 636 | 660 | 684 | 331 |
| AT26x12-12 | 9.5 | 304 | 639 | 660 | 681 | 331 |
| AT26x12-14 | 9.5 | 304 | 642 | 660 | 678 | 331 |
| AT27x9-12 | 7 | 227 | 663 | 686 | 709 | 247 |
| AT27x11-12 | 9 | 281 | 663 | 686 | 709 | 306 |
| AT27x12-10 | 9.5 | 304 | 660 | 686 | 712 | 331 |
| AT27x12-12 | 9.5 | 304 | 663 | 686 | 709 | 331 |

(1)	Tyres in Radial construction are identified by the letter "R" in place of "-" (e.g. AT16x6 R 8). In case of Tyre Size designations not included in this table, refer to any edition of one of the following International Tyre Standards for the relevant dimensional data:

(a)	The European Tyre and Rim Technical Organisation (ETRTO) 'Standards Manual';

(b)	The Tire and Rim Association Inc. (TRA) 'Year Book';

(c)	The Japan Automobile Tire Manufacturers Association (JATMA) 'Year Book';

(d)	The Scandinavian Tyre and Rim Organisation (STRO) 'Data Book'.

In that case the nominated International Tyre Standard, to which the tyre conforms, shall be specified in the application for approval.

"

Annex 6, paragraph 1. and Annex 7, paragraph 1.2, add to the table:

"

|  | Tyre version | Speed Category | Pressure (bar) | Pressure (kPa) |
| --- | --- | --- | --- | --- |
| all terrain (ATV) |  | all | 0.25 | 25 |
|  |  | all | 0.35 | 35 |
|  |  | all | 0.45 | 45 |

"

Annex 8, add a new table for all terrain (AT) tyres with speed symbol "F":

"

| Speed (km/h) | Variation in Load Carrying Capacity (%) |
| --- | --- |
| 50 and below | + 12 |
| 60 | + 7 |
| 70 | + 3 |
| 80 | 0 |
| 90 | - 5 |
| 100 | - 10 |
| 110 | - 15 |
| 120 | - 20 |
| 130 | - 25 |

"

II.	Justification

The addition of AT tyres into UN Regulation No. 75 would permit the type approval of tyres designed to equip quadricycle covered by the new Regulation (EU) No. 168/2013 of the European Parliament and of the Council of 15 January 2013 on the approval and market surveillance of two- or three-wheel vehicles and quadricycles 
(L category vehicles). These tyres may also equip some agricultural tractors (SbS vehicles) covered by the new EU Regulation.

________________