|  |  | INF.9 |
| --- | --- | --- |

Economic Commission for Europe

Inland Transport Committee

Working Party on the Transport of Dangerous Goods

Ninety-eighth session

Geneva, 4-7 May 2015											20 April 2015

Item 6 (b) of the provisional agenda

Proposals for amendments to annexes A and B of ADR:
miscellaneous proposals

Corrections to ADR 2015 – Part 9, Chapters 9.1 and 9.2

Transmitted by the Government of Romania

Introduction

1.	Some inconsistencies with regard to the references to ECE Regulations in Part 9 have been noticed during the transposition of ADR 2015 into Romanian. As a consequence we propose the following corrections:

Corrections

1.	Chapter 9.1, paragraph 9.1.1.1

It is necessary to delete the wording “Annex 7 of”, because in the current version of R.E.3, vehicles are not defined in Annex 7.

Chapter 9.1, 9.1.1.1, first sentence: Delete the wording “Annex 7 of”.

2.	Chapter 9.2, paragraph 9.2.4.7.1

It is necessary to modify the title of ECE Regulation No. 122, because it differs from the current title of the Regulation.

Chapter 9.2, 9.2.4.7.1, footnote 4: Amend the text to read as follows:

4	ECE Regulation No. 122 (Uniform provisions concerning the approval of vehicles of categories M, N and O with regard to their heating systems)

3.	Chapter 9.2, paragraph 9.2.5

It is necessary to modify the title of ECE Regulation No.89, because it differs from the current title of the Regulation.

Chapter 9.2, 9.2.5, footnote 5: Amend the text to read as follows:

5	ECE Regulation No.89 (Uniform provisions concerning the approval of:

I.	Vehicles with regard to limitation of their maximum speed or their adjustable speed limitation function

II.	Vehicles with regard to the installation of a speed limiting device (SLD) or adjustable speed limitation device (ASLD) of an approved type

III.	Speed limitation devices (SLD) and adjustable speed limitation device (ASLD))