## Slide 1: A new EU Regulation for engines in non-road mobile machinery (NRMM)
GRPE session, June 2016
European Commission
Unit C.4 - Automotive and Mobility Industries
DG for Internal Market, Industry, Entrepreneurship and SMEs
Informal document GRPE-73-06
73rd GRPE, 6-10 June 2016, agenda item 6(a)

## Slide 2: DIRECTIVE 97/68/EC OF THE EP AND OF THE COUNCIL of 16 December 1997 on the approximation of the laws of the Member States relating to measures against the emission of gaseous and particulate pollutants from internal combustion engines to be installed in non-road mobile machinery (NRMM)
Directive 97/68/EC
It´s about
  Engines – not vehicles or machinery!
  Pollutant emissions – gaseous (CO, NOx, HC) & particulate (PM)!
  Emission limits & type-approval procedures

## Slide 3
Pathways for revision of
Directive 97/68/EC
Scope extension
New emission limits
Enhancing provisions
Guiding principles for
revising EU legislation
  Strive alignment with (higher) US EPA standards, where appropriate
  Address health-damaging evidence of ultrafine particulate matter
  Catch up with on-road technology trends
  Harmonise requirements across EU
  Simplification & closing loopholes in legislation

## Slide 4
New scope of application
New NRMM Regulation
SI 19-56kW
CI 0-8kW
CI 19-37kW
56-130kW
130-560kW
>0kW
>0kW
>0kW
>560kW
CI 37-56kW
>0kW
300-1000kW
≥1000kW
37-75kW
75-130kW
130-300kW
Rail - Locomotives
Rail - Railcars
Inland Waterway Vessels (IWV)
Snowmobiles
All Terrain & Side-by-Side Vehicles
Land-based NRMM
SI 0-19kW
Gen-Sets >560kW
Auxiliaries ≥1000kW
CI 8-19kW
Auxiliaries 560-1000kW
SI – Spark-ignited (gasoline)
CI – Compression-ignited (diesel)
Scope of Directive 97/68/EC
Scope extensions new NRMM Regulation

## Slide 5
Some key features
of the new Regulation
Regulation
Enhanced market-surveillance provisions
Simplification of administrative procedures
New transition scheme, with staggered introduction dates
Monitoring of emissions from in-service engines
Type-approval also for gas-fuelled engines (partial/mono)
Eliminating "greyzones" (field testing, sep. shipment, ATEX,…)
Early type-approval for Stage V

## Slide 6
2014
TODAY
Oct
-
Dec
EP
Council
Jan
-
Dec
Adoption by Legislators
Entry into force of NRMM Regulation
2015
2016
Jan-
Mar
2017
Sep
Application of NRMM Regulation
+
Repeal of Dir 97/68/EC
Adoption process
NRMM Regulation
Co-Decision Act (CDA)
Essential elements
Recitals
Chapters & Articles
Annexes
Supplementing Regulation
on NRMM
Delegated Act (DA)
Non-Essential elements
Recitals
Chapters & Articles
Annexes
Supplementing Regulation
on NRMM
Implementing Act (IA)
Non-Essential elements
(mostly of adminstrative nature)
(Recitals)
Chapters & Articles
(Annexes)
Jan
-
Dec
Commission
Adoption by Commission

## Slide 7
Timetable - Application of
New NRMM Regulation
1.1.2016
New NRMM Regulation
Entry into force*
YEAR 1
YEAR 2
YEAR 3
YEAR 1
YEAR 2
YEAR 3
YEAR 4
YEAR 1
YEAR 2
YEAR 3
YEAR 4
YEAR 5
SI engines 19-56 kW
CI engines <19 kW
Engines >560 kW
SI engines for ATV & SBS
SI engines for snowmobiles
SI engines <19 kW
CI engines 19-56 kW
Engines 130-560 kW
Engines inland waterway vessels 19-300kW
Engines 56 -130 kW
Engines inland waterway vessels >300kW
Engines for rail
Mandatory dates of application of Stage V – Placing on the market of engines
Date of application*
(DA & IA adopted)
1.1.2017
1.1.2018
1.1.2019
1.1.2020
1.1.2021
* Floating date!
TA
TA
TA
Mandatory dates of application of Stage V – EU Type-Approval of engines

## Slide 8
Land-based NRMM
(CI <56kW & Engines >56kW)
CI 0-8kW
CI 19-37kW
56-130kW
130-560kW
>560kW
CI 37-56kW
Gen-Sets >560kW
CI 8-19kW
Scope of Directive 97/68/EC
Additional in new NRMM proposal

## Slide 9
SI 19-56kW
>0kW
>0kW
Snowmobiles
All Terrain & Side-by-Side Vehicles
SI 0-19kW
Land-based NRMM
(SI engines)
Scope of Directive 97/68/EC
Additional in new NRMM proposal

## Slide 10: UNECE Regulation 96 on Uniform provisions concerning the approval of compression ignition (C.I.) engines to be installed in agricultural and forestry tractors and in non-road mobile machinery with regard to the emissions of pollutants by the engine
UNECE Reg 96
R 96 covers part of the scope of new EU Regulation on NRMM
Need to align R 96 with new EU Regulation on NRMM

## Slide 11
Thank you
For further information
http://ec.europa.eu/growth/sectors/automotive/index_en.htm