## Slide 1: Status Report about the Investigations to the Test method For the Sun Load Impact (Working Title „Phantom effect”)
Karl Manz
Report to GRE 75
Transmitted by the expert from Germany | Informal document GRE-75-16 (75th GRE, 5 - 8 April 2016, agenda item 9(d))

## Slide 2
Background
First Results
Further Results
Conclusion
Open Point
Outline
Notes: Durchführen -- made

## Slide 3
The clear recognition of the signals is very important!
Which situations have an influence to the detection of signal lamps?
Motivation
Notes: Untersuchen -- analysed

## Slide 4
Studies have shown that
approximately 65 % of all rear end accidents and
approximately 50 % of all crossroad accidents
could be avoided if the driver has 0,5 seconds more reaction time.
Motivation
[Enke]
Notes: important

## Slide 5
First Investigation
Background
Principle Test set-up
Rear signalling lamp
Observer
Notes: Objective -- ziel
Make -- durchführen
Image
irradiate

## Slide 6
There is a good correlation between
the luminance factor and
the reaction time (delay) of the observers
Results of the first Investigation

## Slide 7
Principal Test Method
Evaluation only for signal area relevant for the signal
Procedural method
Generation of a mask from the signal area
- Pixels with luminance higher than 11 000 cd/m² = 1
- Pixels with lower luminance = 0
Materials and Methods

## Slide 8
Materials and Methods
L ...........Mean luminance of the signal
LPh ........Mean luminance of phantom by irradiation with sun light and switched off signal
FPh .......Minimum value of super elevation from the luminance of the signal L to the luminance of the phantom light LPh
Test Criterion
Notes: Calculated
Equation
divide

## Slide 9
Results
(a)
(b)
(c)
Signal turn indicator
Luminance pictures (signal indicator) (a) mask, (b) luminance of signal, (c) luminance of phantom
Notes: Example compare
Image
Pseudocolor exposure
Colour displays value of the luminance
Impression – Eindruck
Recognition -- erkennen

## Slide 10
Investigations how to measure it and is it possible to implement these test procedures into optical simulation tool by the manufactures
Signalling Lamp
Sun Simulator
Measuring Head

## Slide 11
New Investigation
Lamps
Of the
First Investigation
Lamps
Of the
Investigation about test procedures and optical simulation tool
Second Investigation
with observers to evaluate all Results

## Slide 12
Chart: relative ReactionTime
| 1.2515675593573701 | 1.03243821250693 | 1.01352680144069 | 1.07690103396479 | 1.04636463682739 | 1.0602281352910601 | 1.2863612143899099 | 1.1760764573272999

 | 0.879 | 1 | 0.9939 | 0.90308 | 0.96471 | 0.95241 | 0.86794 | 0.89861
New Investigation

## Slide 13
Proposal for Regulation No. 6 and Regulation No. 7

## Slide 17
Open point to do:
With regard to the test criterion “Mean Luminance”:
For measurements of the signal and sun load impact to determine the Factor:
Requires a more precise description;

## Slide 18
Possible Measuring procedures:
Relative measurement ;
→Simpler measurement equipment;
→ Relative difficult evaluation of the area to be measure;
b) Luminance measurement with the application of an filter;
→ More expensive measurement equipment (absolute measurements);
→ Easier evaluation of the area to be measure;
→ More precise Results:
All these methods must be seen in correlation to the results of the latest Investigation to set the threshold factor.

## Slide 19
Thank you for your attention !