| Submitted by expert from Germany | Informal document GRSP-59-09-Rev.1 (59th GRSP, 9-13 May 2016, agenda item 15) |
| --- | --- |

Proposal for Supplement 2 to the 03 series of amendments to Regulation No. 80 (Seats of large passenger vehicles and of these vehicles with regard to the strength of the seats and their anchorages)

The text reproduced below was prepared by the expert from Germany. It clarifies requirements regarding the safety device to be installed at side-facing seats. The modifications to the current text of UN Regulation No. 80 are marked in bold for new or strikethrough for deleted characters.

I.	Proposal

Paragraph 7.4.4., amend to read:

"7.4.4.	The passengers in side-facing seats shall be safeguarded by a vehicle part (e.g. partition, wall or seat back of a forward-facing seat) forward of the foremost side-facing seat. This vehicle part shall meet the requirements of Appendix 7. It shall maintain its safeguard function during testing."

II.	Justification

1.	The current text has been misunderstood with regard to the need of providing a safety device that does not break and which maintains its capability to retain a passenger’s body in the case of an accident.

2.	The proposal clarifies the requirements and introduces the necessary transitional provisions.