## Slide 1: Replacement Brake Callipers
CLEPA Presentation to GRRF 84
Submitted by CLEPA
Informal document GRRF-84-25
84th GRRF, 19–22 September 2017
Agenda item 4

## Slide 2: Market
The market for replacement brake callipers is serviced by:
  new callipers from OEM suppliers
  remanufactured* callipers from OEM suppliers
  new “copy” callipers from non - OEM suppliers
  remanufactured* callipers from non - OEM suppliers
* Common definition agreed by APRA, CLEPA, FIRM, VDA and ACEA
  “A remanufactured part fulfils a function which is at least equivalent compared to the original part[1]. It is restored from an existing part (core), using standardized industrial processes in line with specific technical specifications . A remanufactured part is given the same warranty as a new part and it clearly identifies the part as a remanufactured part and the remanufacturer ”
A remanufactured part is different from a reused, repaired, rebuilt, refurbished, reworked or reconditioned part. These categories are not subject to this definition

## Slide 3: Background
In view of the evolution of the market it has been suggested that UN Regulation No. 90-02 should be extended to cover replacement brake callipers – both new “copy” parts and remanufactured units
During discussions at the R90SIG in Spain (2016) it was envisaged that a legislative regime for new and remanufactured callipers could follow similar lines to existing tyre legislation for new and re-treaded tyres (R.108 PC & R.109 CV) which employ common test regimes but different COP procedures
CLEPA was asked to consider the matter based on their members experience

## Slide 4: CLEPA Position
CLEPA members have found serious problems in the replacement market with products offered by some non –OEM suppliers
These problems are with both new “copy” callipers and (supposed) “remanufactured” parts
There are different views within the CLEPA membership as to how best these problems might be addressed
CLEPA recognises that for GRRF to consider any proposal for legislation it is essential to establish if a safety risk of sufficient scale exists
CLEPA members do not have any vehicle accident statistics directly attributed to brake calliper failures - any information from CP’s would be very welcome - but examples of the type of faults that have been found with new “copy” parts and supposed “remanufactured” parts follow

## Slide 5: “Copy” Callipers – problems identified
Problems have been found with “copy” callipers that are associated with the use of poor quality/low strength materials
  Structural failure (carrier) < 700 brake applications of an ISO26965 brake pad test
  Internal component failures (e.g. actuation levers, roller bearings) during early stages (~ 1000 brake applications) of endurance tests
Problems have also been found with ”copy” callipers associated with poor tolerancing/manufacture
  Poor calliper efficiency (< 90%) @ higher pressures
  Excessive load/unload hysteresis effects
  Heavy/uneven actuation component wear

## Slide 6: “Remanufactured” Callipers – problems identified
Continued incorporation of worn/damaged parts that should have been replaced
  e.g. castings/carriers/fasteners/bearings/adjusters
Use of new components of poor quality/low strength
  e.g. fasteners/bearings/shafts/tappets
Poor assembly processes and practices
  e.g. cleaning/sealing/lubrication/testing/traceability