## Slide 1
ETRTO proposal for UN R30 & 64 amendments
Extended Mobility Tyres
Sept 2018 GRBP Supporting material
Informal Document GRB-68-14
Agenda item 19

## Slide 2: WHY TO REGULATE EMT ?
“RF” TYRES rarely adopted, not constituting a representative use case.
Millions of tyres providing flat running mode capability (at least 80 km @ 80 km/h) are on the market and not regulated regarding their flat running mode performance.
“RF” TYRES regulated focusing essentially on flat running mode performance (zero inflation pressure)
“NOISE/WET GRIP/RR” have been regulated afterwards together with other tyre characteristics.
REGULATORY PICTURE
REAL WORLD APPLICATION
WHY TO REGULATE EMT?
To specify a minimum deflated performance requirement that tyres declared as EMT have to meet
to consider EMT as a safety asset for current vehicles and forthcoming autonomous ones.

## Slide 3: WHY NOT JUST TO AMEND RF?
RATIONALE TO INTRODUCE A NEW DEFINITION:
Because RF and EMT have two different structure identification: RF vs. R;
To prevent market confusion, while ensuring a clear regulatory framework.
TEST
MARKING
STRUCTURE
PRODUCT
REQUIREMENT
At least 80 km @ 80 km/h
RF
RUN FLAT
“SNAIL”
ANNEX 7 §3
EMT
RADIAL
“SWIRL”
ANNEX 7 §4
205/55RF16
205/55R16

## Slide 4: RF vs. EMT: REAL WORLD TARGETS & PERFORMANCES EVOLUTION
-38% RR
80 km on vehicle kept
EMT additional capabilities
Rolling resistance improvement Fuel consumption / CO2 reduction.
Weight and stiffness improvement better NVH (comfort, acoustics).
Chassis loads reduction safety enabler (reduced inertia for impact & braking)
-13% Weight
Customers Feedback: Since 2009 more than 7 million vehicles had been sold worldwide fitting EMT, without reported issue on flat running mode performance.
2006  TODAY
ISO 16992:2005 & UN R30 requirement set on limited real world experience
Initial target on vehicle above 200 km
RF tyres focusing more on flat performance than e.g. comfort and rolling resistance
2005-2006
Actual target on vehicle in line with 80 km @ 80 km/h
ISO 16992:2018 with the addition of a more realistic test (reduced load and temperature) following real world experience and better understanding of indoor failure mode compared to the road test.
vs.
Performance evolution RF vs. EMT

## Slide 5: EMT PERFORMANCE EVIDENCE ON VEHICLE
C: medium cars
D: large cars
E: executive cars
F: luxury cars
J: sport utility cars
M: Multi purpose cars
S: Sports cars
ACTUAL EMT ON M1 SEGMENTS = 80 x 80 ON VEHICLE
WIDE RANGE OF TYRE SIZES AND VEHICLE TYPES COVERED TO DEVELOP THE NEW EMT TEST METHOD

## Slide 6: HOW TO REGULATE EMT?
Amendments to implement EMT beside RF
DEFINITION
2.9. "Extended Mobility Tyre (EMT)" describes a tyre with a radial structure allowing the tyre, […] to provide the vehicle with the basic tyre functions at a speed of 80 km/h and a distance of 80 km when operating in flat tyre running mode.
ANNEX 7 - TEST
4. Procedure to assess the "flat tyre running mode" of "extended mobility tyres“
High quality procedure, including test at zero pressure with clear and detailed requirements
MARKING
3.1.15 The symbol below for EMT
3-PILLARS FOR CONSISTENCY IN THE REGULATION & CLEAR REQUIREMENTS SETTING
UN R30
UN R64

## Slide 7: BIG PICTURE OVERVIEW: EMT BESIDE RF
DOES IT WORK?
SIDE ROAD RISK
SOLUTION
Solution
Search the spare tyre
Lift the vehicle
Mount the spare tyre
Put the damaged tyre back in the car
Dismount the damaged/deflated tyre
restart driving
If spare not underinflated
Spare Tyre
Search the emergency wheel
Lift the vehicle
Mount the emergency wheel
Put the damaged tyre back in the car
Dismount the damaged/deflated tyre
restart driving @ limited speed
If not underinflated
Temporary spare
Search the tyre repair kit
Connect the repair kit
Put the tyre repair kit back in the car
Able to use the tyre repair kit???
Remove the tyre repair kit
Restart driving with limited speed if able to use the kit
Tyre repair Kit
„RF“ tyre
EMT
Keep driving with max 80 km/h speed for at least 80 km
Keep driving with max 80 km/h speed for at least 80 km
RF TO BE KEPT BESIDE EMT
(non regulated)

## Slide 8: VISION
It is raining and an L5 full automated vehicle is on the highway fast lane
One tyre has got a puncture,
  the Tyre Pressure Monitoring System detects underinflation
  The ECU is notified by the TPMS
  The ECU is aware the tyre is an EMT
  The vehicle safely reduce the speed, safely moves to the exit line and reaches a maintenance area where the tyre is checked and/or repaired
EMT will be an additional asset for Automated Vehicles

## Slide 9: CONCLUSION and RECOMMENDATIONS
EMT is a safety asset and needs to be regulated to ensure a minimum flat running mode performance.
The proposal while addressing this need is aligned with harmonized regulations regarding road safety and environmental protection (RR, Weight)
The millions of tyres meeting the proposed EMT requirements perform satisfactorily on the market
ETRTO recommends the GRBP to consider for adoption the working documents ECE/TRANS/WP.29/GRVA/2018/6 and ECE/TRANS/WP.29/GRVA/2018/7

## Slide 10
Thank you!