## Slide 1
Information on the 2018 update of “PIEK”
the national regulation in the Netherlands on delivery noise of trucks
Presentation for GRBP September 2018
Introducing informal document GRB-68-10
Under Agenda item 10. “Exchange of information on national and international requirements on noise levels”
Remco Tekstra (PIEK-Keur)
Erik de Graaff (M+P)
Transmitted by the expert from the Netherlands
Informal document GRB-68-28
(68th GRB, 12-14 September 2018,
agenda item 10)

## Slide 2: Why do we share this information with GRB?
Some parties in GRB are using the PIEK measurement method as a test institute
Some parties (truck manufacturers) are applying for a PIEK certificate
Delivery noise is on the long list of GRB and GRB may wish to take note what is going on in the Netherlands

## Slide 3: What is PIEK?
A national regulation in the Netherlands on maximum allowable Peak noise immission levels during loading and unloading of delivery trucks
  Day: no limit
  Evening: limit 65 dB(A)
  Night: limit 60 dB(A)
Problem-owner is the shop/supermarket:
  delivery is forbidden during evening/night, unless noise limits are satisfied
Immision: Evaluation point is closest home around the shop

## Slide 4: What is PIEK?
Huge interest of the branch and widely supported:
  Most supermarkets set requirements towards their transport companies
  Evening/night delivery has major benefits with respect to
  Cost (time, fuel consumption),
  CO2/tail pipe emission,
  Safety
  Liveability of urban centres
In force since 1998, certification-scheme introduced in 2004

## Slide 5: How does PIEK certification work?
Immission levels are translated to 60/65 dB(A) emission levels on 7,5 m
Driveline noise for truck is exempted: Limit for “Quiet Truck” = 72 dB(A)
Measurement methods agreed for a variety of products (trucks, body/coachwork, truck refrigeration units, pallet trucks, dolly’s etc.)
Stichting PIEK-Keur grants certificates; approved products are entered in online register
Approved products are granted night time delivery status
Individual products receive stickers
http://www.piek-international.com/english/

## Slide 6: PIEK products
Stille componenten

## Slide 7: National versus international
PIEK system adopted in Belgium (Flemish law)
Preparations going on in Denmark
Various EU cities have adopted PIEK system on a voluntary base
Recognized and adopted by various international parties
  http://piek.cemafroid.fr
  http://noiseabatementsociety.com/campaigns/nas-piek/
  etc
Many international companies have applied products
  Including most EU truck manufacturers

## Slide 8: What is going to change in the 2018 version?
Procedure update for the whole document
  Clarification of general requirements, like applicable test methods, product family, COP etcetera’s
  Clarification of general requirements on measuring conditions and equipment
Test method update for Quiet Truck
  Clarify and repair ambiguities in the old text
  Update to satisfy the latest stage of technology
  Remove superfluous test methods (e.g. double tested noise sources)
    and keep only the most representative and most demanding method
  Use where possible the ECE R51 systematics and/or test methods
See text proposal in GRB-68-10
Changes are marked in yellow

## Slide 9: What is going to change in the 2018 version? Measurement methods for Quiet Truck
Still in place:
  acceleration 0-20 km/h; but procedure slightly changed
  Compressed air noise; but adopted to ECE R51 procedure
  Reversing alarm and blind spot warning (awaiting progress in GRB IG)
Withdrawn:
  Backwards driving 3 km/h
  Cruise by 20 km/h
  Braking 20-0 km/h
Added:
  Pass by noise conform ECE R51
    @35 km/h, but PIEK mode engaged
    Obliged, but only informative, not normative
  Closing doors
    Obliged, but only informative, not normative

## Slide 10: Procedure and Planning
Current proposal 2018 still to be confirmed by PIEK-Keur board
  After consultation of the committee of experts
  Expected: end of September 2018
New procedures applicable as from January 2019
It remains a national Netherlands procedure and document
  But feedback from any expert or body is always welcome
Future developments in GRBP will be followed closely
  And, if applicable, incorporated in following version of the PIEK protocol

## Slide 11: Questions to GRBP experts (especially truck manufacturers)
Short term:
  If you have any feedback on this 2018 proposal for update, please hand them over to your Netherlands representative in the PIEK-keur expert group
  Deadline: 30 September
Long term:
  Consider introducing delivery noise standards in GRB
  Consider PIEK-keur system as an example or starting point

## Slide 12: Thank you for your attention