## Slide 1
Status report of “Reversing Motion”
in VRU-Proxi Informal Working Group.
JAPAN,
on behalf of
VRU-Proxi Informal Working Group.
Informal document GRSG-115-40
(115th GRSG, 09-12 October 2018,
agenda item 6(a))

## Slide 2
VRU-Proxi Informal Working Group
Working contents
Forward motion
Vehicle turning - Blind Spot Information System (Oct.2018, 115th GRSG)
Vehicle driving straight or taking off from standstill (Apr.2020, 118th GRSG)
Reversing motion
New field of view for behind vehicle (Apri.2019, 116th GRSG)
* Introduction Today
Direct Vision
Evaluation of direct vision around vehicle from driver (Apr. 2021, 120th GRSG)

## Slide 3
Purpose
To provide driver vision for safety of vehicle rear direction when the vehicle moving rearward.
In order to achieve the purpose, " Close-proximity rear" view devices (Class VIII) was added to current R-46.
“ 6.1.2.1.7. Close-proximity rear" view devices (Class VIII)
The contours of the reflecting surface shall be of simple geometric form and its dimensions such that the mirror provides the field of vision specified in paragraph 15.2.4.8. of this Regulation."
“15.2.1.1.1.
Regarding Class VIII devices can be accepted Camera monitor systems (or other devices)."
Scope
All categories of M and N.

## Slide 4
Definitions of Class VIII Field of View
15.2.4.8.1.
The field of vision shall be bounded by the following planes and shall be such that the driver can see at least part of each cylindrical objects with a height of 1,000 mm and a diameter of 300 mm which is located at 6 positions within the boundaries of the field of vision as defined in Figure:
(a) A transverse vertical plane of the outermost point of the rear of the vehicle;
(b) A transverse vertical plane [3,500] mm behind the outermost point of the rear of the vehicle;
(c) Two longitudinal vertical planes parallel to the longitudinal vertical median plane of the outermost point of the side of the vehicle.

## Slide 5
Multimodal approach for Class VIII Field of View
Driver can be perceived Class VIII Field of View by;
Direct vision from newly defined driver’s looking back ocular points
Indirect vision
Combination of mirrors of Class VIII or other Class(es)
Camera monitor system
Obstacle detection systems (e.g. Sonar system)
“15.2.4.8.3.
The driver’s looking back ocular points” means two points located at 96mm longitudinally rearward, 158mm horizontally inside vehicle center and 6mm vertically above from “The driver’s ocular points” described in 12.1.
“15.2.4.8.2.
If the field of vision defined in paragraph 15.2.4.8.1. can be perceived via a combination of devices for indirect vision of other Classes or directly from the driver’s looking back ocular points described in 15.2.4.8.3., it is not mandatory to equip the vehicle with a Class VIII close-proximity rear-view device. In addition, the requirement may be met using a combination of mirrors of Class VIII and other Class(es) or using an obstacle detection system."

## Slide 6
Further discussions
- Style of regulation
Option 1 R46 Amendment
Option 2 New regulation
Option 3 Some parts in R46 Amendment and the other parts in new regulation
Details
For sensor detection, if necessary or not to distinguish VRU and other obstacles
Rear headrest position setting
Suitable rear-end distance, 3.5m or other distance
Scope for application or exception
Transitional provisions

## Slide 7
Schedule
2018
November E-mail and/or Web discussions
December Making draft of Working Document
2019
January 11 Submit Working Document to 116th GRSG
February 5-7 VRU-Proxi 8th meeting at Yokohama
April 2-4 VRU-Proxi 9th meeting at Brussels
April 9-12 116th GRSG

## Slide 8
Thank you for your attentions.