## Slide 1: Dynamic criteria Biorid
Clepa has investigated the industrial feasability of proposed GTR 7 Phase 2 dynamic proposed criteria.
Proposed criteria and limits are :
Transmitted by the expert from CLEPA Informal document GRSP-64-44
(64th GRSP 11-14 December 2018,
agenda item 2)

## Slide 2: Dynamic criteria Biorid
1st investigation : data from JNCAP 2010/12 results at 17.6 km/h.
Clepa has analyzed :
  If seats exceeded the Japanese Biomechanic proposed limits
  If seats exceeded the German Biomechanic proposed limits
  If seats can go into a serial production -> proposed limits – 20 %
  41 data sets were checked for 40 vehicles, 1 vehicle has had 2 seat variants
Transmitted by the expert from CLEPA Informal document GRSP-64-xx
(64th GRSP 11-14 December 2018,
agenda item xx)

## Slide 3: Dynamic criteria Biorid
1st investigation : data from JNCAP 2010/12 results at 17.6 km/h.
Results:
Several vehicles do not meet GTR7 dynamic criteria or would be too borderline to allow an industrialization of such seats.
  Do not meet criteria proposed by Japan : 2 out of 40 cars
  Too borderline to be allowed in serial production for a regulatory use when Japan criteria are used in regulations : 7 out of 40 cars
  Do not meet criteria proposed by Germany : 8 out of 40 cars
  Too borderline to be allowed in serial production for a regulatory use when German criteria are used in regulations : 18 out of 40 cars
  We were not able to determine if such 18 cars fulfilled the backset requirement of GTR7.
Transmitted by the expert from CLEPA Informal document GRSP-64-xx
(64th GRSP 11-14 December 2018,
agenda item xx)

## Slide 4: Dynamic criteria Biorid
Conclusion from data from JNCAP 2010/12 results at 17.6 km/h :
Almost half of the vehicle seats will be eliminated from the market with the german proposal versus 2010/12 vehicles tested by JNCAP
No injury curves are available on Fx- upper and Fx – lower and therefore those criteria shall not be included.
The number of injury criteria can be reduced
Transmitted by the expert from CLEPA Informal document GRSP-64-xx
(64th GRSP 11-14 December 2018,
agenda item xx)

## Slide 5: Dynamic criteria Biorid
2. Dynamic GTR7 phase 2 tests of GOOD EuroNcap seats by Clepa :
Seats A, B, C, D and F have GOOD EuroNcap results, Seat E (1.46 out of 2 points) is near Good EuroNcap limit
3 seats were tested by changing pulse to GTR7 pulse, but maintaining Biorid setup of EuroNcap protocol with HRMD.(marked HRMD)
5 seats were tested by applying GTR7 pulse and GTR7 proposed Biorid set up (marked GTR7)
Torso angle of 25°
Orange : value exceed german proposal
Yellow : value near to regulatory limit (within 20% band)
Transmitted by the expert from CLEPA Informal document GRSP-64-xx
(64th GRSP 11-14 December 2018,
agenda item xx)

## Slide 6: Dynamic criteria Biorid
2. Dynamic GTR7 phase 2 tests of GOOD EuroNcap seats by Clepa :
Results :
    1 of 6 seats did not fulfill German proposal
    the seat not fulfilling german proposal was limit for GOOD EuroNcap rating
    5 of the 6 seats would be too borderline to allow serial production in respect to german proposal
    80 % of tested GOOD EuroNcap seats will not fulfill the requirements for industrial production and GTR7 phase 2 german proposed injury limits.
Transmitted by the expert from CLEPA Informal document GRSP-64-xx
(64th GRSP 11-14 December 2018,
agenda item xx)

## Slide 7: Dynamic criteria Biorid
3. Results of more than 200 tests from seats released in serial production.
Fx+ lower.
A considerable amount of actual seats will not fulfill GTR7 dynamic proposed values of Germany.
Clepa does not understand the statement from Germany that 95% of actual EuroNcap tested head restraints fulfill the values.
Transmitted by the expert from CLEPA Informal document GRSP-64-xx
(64th GRSP 11-14 December 2018,
agenda item xx)

## Slide 8: Dynamic criteria Biorid
2. Dynamic GTR7 phase 2 tests of GOOD EuroNcap seats by Clepa :
Results :
    1 of 6 seats did not fulfill German proposal
    the seat not fulfilling german proposal was limit for GOOD EuroNcap rating
    5 of the 6 seats would be too borderline to allow serial production in respect to german proposal
    80 % of tested GOOD EuroNcap seats will not fulfill the requirements for industrial production and GTR7 phase 2 german proposed injury limits.
Transmitted by the expert from CLEPA Informal document GRSP-64-xx
(64th GRSP 11-14 December 2018,
agenda item xx)

## Slide 9: Repeatability and reproducibility of Biorid
3. Clepa has done 6 repeatability tests of Biorid dummy in 2016 - 2018
  Before and after calibration of Biorid dummy according to latest calibration recommandations from Humanetics, 3 times before and 3 times after calibration.
  The 3 sets of data for 3 calibrations were realized on 6 seats with Good EuroNcap results produced the same day to minimize seat variations with 16 km/h IIWPG pulse.
Results for cv values of the 6 tests and variation of results expressed in +/- 2 sigma :
Transmitted by the expert from CLEPA Informal document GRSP-64-xx
(64th GRSP 11-14 December 2018,
agenda item xx)

## Slide 10: Repeatability and reproducibility of Biorid
Summary of repeatability and reproducibility studies of Humanetics :
  This data was already presented in the GTR7 group under GTR7-16-02-HIS.
Transmitted by the expert from CLEPA Informal document GRSP-64-xx
(64th GRSP 11-14 December 2018,
agenda item xx)

## Slide 11: Repeatability and reproducibility of Biorid
Summary R&R for NIC and calibration corridor :
Humanetics : Repeatability : cv = 9.9% and +/- 2 sigma = +/- 7 m²/s²
Reproducibility : cv = 10.7% and +/- 2 sigma = +/- 7.5 m²/s²
Clepa : Repeatability : : cv = 13.6% and +/- 2 sigma = +/- 3.8 m²/s²
Calibration corridor : none for NIC, but influence by T1 acceleration corridor:
Transmitted by the expert from CLEPA Informal document GRSP-64-xx
(64th GRSP 11-14 December 2018,
agenda item xx)
Transmitted by the expert from CLEPA Informal document GRSP-64-xx
(64th GRSP 11-14 December 2018,
agenda item xx)

## Slide 12: Repeatability and reproducibility of Biorid
Summary R&R for My+ upper and calibration corridor :
Humanetics : Repeatability : cv = 1,7% and +/- 2 sigma = +/- 0.6 Nm
Reproducibility : cv = 5,3% and +/- 2 sigma = +/- 1.6 Nm
Clepa : Repeatability : cv = 15,3% and +/- 2 sigma = +/- 3.8 Nm
Calibration corridor : here or here ?
Transmitted by the expert from CLEPA Informal document GRSP-64-xx
(64th GRSP 11-14 December 2018,
agenda item xx)

## Slide 13: Repeatability and reproducibility of Biorid
Summary R&R for Fx+ lower and calibration corridor :
Humanetics : Repeatability : cv = 3,4% and +/- 2 sigma = +/- 15 N
Reproducibility : cv = 10.5% and +/- 2 sigma = +/- 47 N
Clepa : Repeatability : : cv = 10.7% and +/- 2 sigma = +/- 47 N
Calibration corridor : +/- 150N
Transmitted by the expert from CLEPA Informal document GRSP-64-xx
(64th GRSP 11-14 December 2018,
agenda item xx)

## Slide 14: Dynamic criteria Biorid
Conclusion Repeatability and Reproducibility
Clepa is concerned by R&R issues and calibration corridors of Biorid in addition to needed margin for serial production of seats.
Those variations must be taken into account for the allowed regulatory values.
Allowed variations of the dummy must be added to the injury criteria.
  NIC : 2 sigma of reproducibility of Biorid to be added.
  My+ upper : it is not clear if the right area has been studied for R&R, therefore Clepa proposes to add repeatability values obtained by Clepa.
  Fx+ lower : the corridor of GEN-X test is about +/- 150N and needs to be added.
Transmitted by the expert from CLEPA Informal document GRSP-64-xx
(64th GRSP 11-14 December 2018,
agenda item xx)

## Slide 15: Dynamic criteria Biorid
Conclusion Repeatability and Reproducibility
Results :
Clepa is concerned by R&R issues and calibration corridors of Biorid in addition to needed margin for serial production of seats.
Those variations must be taken into account for the allowed regulatory values.
Allowed variations of the dummy must be added to the injury criteria.
  NIC : 2 sigma of reproducibility of Biorid to be added. 2 sigma = 2 x cv (10.7%) x 23 = 5m²/s²
  My+ upper : it is not clear if the right area has been studied for R&R, therefore proposal to add repeatability values obtained by Clepa = 3.8 Nm
  Fx+ lower : the corridor of GEN-X test is about +/- 150N and needs to be added.
Transmitted by the expert from CLEPA Informal document GRSP-64-xx
(64th GRSP 11-14 December 2018,
agenda item xx)

## Slide 16: Dynamic criteria Biorid
Conclusion :
Clepa does not support the german proposal on injury criteria as not justified by injury risk curves.
Clepa supports the japanese proposal on injury criteria and values, with following changes :
Supression of Fx- upper and Fx- lower as no injury curves have been shown
There is a need for a review of all data for establishement of appropriate injury limits
As example, Clepa believes following limits appropriate :
  NIC : 23 m²/s² + 5m²/s² = 28 m²/s²
  My+ upper : 34 Nm + 3.8 Nm = 37.8 Nm
  Fx+ lower : 640 N + 150N = 790 N
Transmitted by the expert from CLEPA Informal document GRSP-64-xx
(64th GRSP 11-14 December 2018,
agenda item xx)