## Slide 1
C-EDR
Introduction of
Chinese Mandatory National Standard
GB “Automobile Event Data Recorder "
Informal document WP.29-178-27 (178th WP.29, agenda items 2.3)

## Slide 2
contents
DEVELOPMENT PROCESS & STANDARD
FRAMEWORK
2
STANDARD CONTENT
3
STANDARD IMPLEMENTATION
4
BACKGROUND
1

## Slide 3
BACKGROUND
CONTENTS

## Slide 4
CFR 563
Chinese Mandatory Standard
(in the process of approval)
Current EDR Regulations & Standards Around the World
BACKGROUND
1.There are many traffic accidents and complicated situations in China.
2.With the rapid development of intelligent connected vehicles and new energy vehicles, higher requirements are put forward for vehicle safety protection measures. We want to propose requirements for EDR systems that are in line with China’s current and future developments.
3.Support an implementation independent of the airbag system.
4.EDR system should be suitable for the status quo of domestic enterprises.
5.Unified data reading scheme is required.
Main Concern

## Slide 5
DEVELOPMENT PROCESS & STANDARD FRAMEWORK
CONTENTS

## Slide 6
2016.03
Begin
2016.09
2017.09
2018.06
2019.03
Draft
Project approval
Solicit comment
Submit for review
DEVELOPMENT PROCESS
2019.06
Submit for approval

## Slide 7
EDR
Trigger
Threshold
Locking
Condition
Beginning of Event
End Of Event
Data Record
Storage Coverage Mechanism
Power-off Storage
Electronic
Protection
Data Retrieval
Consistency check
Public Needs
Accident Analysis
Defects Recall
Insurance Claims
Acceleration
Delta-V
Braking Status
……
Airbag Status
INPUT
OUTPUT
FRAMEWORK OF EDR STANDARD

## Slide 8
STANDARD CONTENT
CONTENTS

## Slide 9
Step 5
Step 6
Step 7
Step 8
Step 2
Step 1
Step 4
Step 3
C-EDR
Technical Requirements
Appearance and Identification
Manual
Test Methods and Requirements
Type Inspection
Standard Implementation(TBD)
STRUCTURE OF EDR STANDARD
9

## Slide 10
Technical Requirements
Impact Event Requirements
Data Record Requirements
EDR功能要求
EDR Functional Requirements
Data Function Requirements
Data Retrieval Requirements
TECHNICAL RERUIREMENTS

## Slide 11
Trigger Threshold
IMPACT EVENT REQUIREMENTS
Locking Condition
Beginning of Event
End of Impact Event

## Slide 12
1
VERY LOW
2
VERY LOW
2
LOW
3
MEDIUM
4
5
LOW
4
MEDIUM
6
MEDIUM
8
HIGH
10
LOW
MEDIUM
6
MEDIUM
9
HIGH
12
VERY HIGH
15
MEDIUM
4
MEDIUM
8
HIGH
12
VERY HIGH
16
EXTREME
20
MEDIUM
5
HIGH
10
VERY HIGH
15
EXTREME
20
EXTREME
25
3
Level A Data
Element
A
A
B
Level A (17)
Level B (43)
Data that shall be recorded when vehicles are equipped with EDR system.
Relevant data that should be recorded when vehicles with EDR system are equipped with relevant devices or have relevant functions.
DATA RECORD REQUIREMENTS
Time to Maximum
Recorded delta-V
Maximum Recorded
Lateral delta-V
VIN
Service brake
，on or off
Acceleration pedal position%
Lateral delta-V
Maximum Recorded
Lateral delta-V
Vehicle Velocity
Clipping Flag
Revolution per minute
Driver seatbelt status
Power-on cycle
at event
Power-on cycle at retrieving
Complete status of event data record
Time interval from this
event to the last event
ECU hardware number that records EDR data
ECU software number that records EDR data
ECU serial number that records EDR data

## Slide 13
Longitudinal
acceleration
Lateral
acceleration
Lateral
delta-V
Time to Maximum Recorded delta-V，Resultant
Yaw Angle
Velocity
Steering
Angle
Gear
Position
Engine Throttle Position
Brake Pedal
Position
Parking System
Status
Steering Lamp
Status
Occupant Protection
System Warning Status
Tire Pressure Monitoring System
Warning Status
Braking System Warning
Status
Driver’s seat belt pretensioner
Deployment time
Driver’s front airbag
Deployment time （phase I）
Driver’s front airbag
Deployment time
（phase II）
Front-row passenger seat belt pretensioner
Deployment time
Front-row passenger ‘s front airbag suppression status
Front-row passenger ‘s front airbag
Deployment time(phase I)
Front-row passenger ‘s front airbag
Deployment time（phase II）
Front-row passenger’s side airbag
Deployment time
Front-row passenger’s side air curtain
Deployment time
Year
Month
Day
Hour
Minute
Second
Working status and event status
Restraint system
Active system
Time
Level B Data
Element
B
DATA RECORD REQUIREMENTS
Anti-brake system
status
AEB status
Adaptive Cruise
Control system status
Cruise Control
system status
Electronic stability
control system status
Traction control
system status
Driver’s side airbag
Deployment time
Driver’s side air curtain
Deployment time
Front-row passenger
seat belt Status
Tend
Pre-event
synchronization
timing time
Maximum Recorded
Lateral delta-V
Square of Maximum
Recorded Resultant
delta-V
Time to Maximum
Recorded delta-V
lateral
13

## Slide 14
Non-volatile storage medium
At least 3 times of impact event
data.
data before T0 and after T0 to (150±10) ms should be recorded.
DATA RECORD FUNCTION REQUIREMENTS
Power-off storage requirements
Unlocked event data should be overwritten by subsequent un-locked event data, in chronological order.
Locked event data should not be overwritten by data from subsequent events.
For unlocked events, the manufacturer is allowed to set other storage coverage mechanisms.
Storage media and storage frequency requirements
Storage coverage mechanism requirements
14

## Slide 15
1
2
3
4
Unified data retrieval connector
GB/T 34589-2017“Road Vehicles diagnostic connector”
Unified data retrieval protocol
Unified data retrieval ID
0xFA13, 0xFA14 and 0xFA15
Where,
0xFA13 for the most recent event,
0xFA14 for the second event from the bottom,
0xFA15 for the third event from the bottom.
Unified data arrangement
√ Use diagnostic service 0x22“ReadDatabyIdentifier“ in ISO 14229 “Road Vehicles unified diagnostic service " to retrieve EDR data.
√ compatible with CAN bus and k-line.
√ Compatible with functional addressing and physical addressing
√ Compatible with 11-bit and 29-bit CANID
Unified data range, accuracy, resolution and data arrangement order
DATA RETRIEVAL REQUIREMENTS
15

## Slide 16
Test Methods
IMPACT TEST
MEASURE
DRIVER OPERATION DATA TEST
IMPROVE
BENCH TEST
TEST METHODS
16

## Slide 17
Add acceleration and airbag deployment time measurement to the existing mandatory impact test, and compare the results measured in the laboratory and recorded by to verify the accuracy of dynamic data after collision.
Impact Test
Chart: 时间（ms）
Driving Operation Data Test
Enable the vehicle to reach the trigger in any way:
-- hit the vehicle
-- fix the vehicle with the pallet, and hit the pallet
-- physically trigger the EDR
-- input trigger signal to the EDR。
TEST METHODS
17

## Slide 18
The impulse waveform of acceleration is applied to the EDR controller by the shock testing machine to verify the EDR trigger, storage times, coverage mechanism and power off storage requirements.
Bench Test
TEST METHODS
18

## Slide 19
Summary
19
1.This standard is expected to enter into force gradually in China.
2.China would like to contribute our EDR standard development experience to the WP.29 for future development of EDR regulation if it will be developed under 1958 agreement.
3.And China also suggests to adopt this standard into the Compendium of Candidate GTR, if a GTR for EDR is going to be developed by WP.29.
4.China is looking forward to participating the working group for EDR issues. And Chinese delegates would like to further elaborate the details in the IWG level.
For specific discussion please contact Ms. Wu Hanbing by email: wuhanbing@catarc.ac.cn

## Slide 20
THANK YOU！
C-EDR