## Slide 1
Status report
of the
WLTP Informal Working Group
Prepared by WLTP IWG
Informal document GRPE-78-13e
78th GRPE, 10-11 January 2019, agenda item 3(b)

## Slide 2
Content
Request for GRPE Approval
1-1. Amendment 5 of GTR#15
1-2. Amendment 2 of GTR#19
2. Review Overall Progress
3. Status of each TF
4. Outlook for GRPE-79
Seperate presentation:
Transposition into UN R (GRPE-78-14e)

## Slide 3
1. Request for GRPE Approval
Working Categories | Expected Actions reported during 77th GRPE | Request for GRPE Approval
GTR15 Amendment5 (Type I under 23℃) | submit Working Document for approval | ECE/TRANS/WP.29/GRPE/2019/2 Informal Document : GRPE-78-21 Technical report : GRPE-78-03
GTR19 Amendment2 (Evaporative Emission) | submit Working Document for approval | ECE/TRANS/WP.29/GRPE/2019/4 Technical report : GRPE-78-09
Transposition to UNR | submit Informal Document for review | Postponed
Low Temp. Test (Type I under -7℃) | submit Informal Document for review | Postponed

## Slide 4
1-1. Amendment 5 of GTR 15
(Type I test under 23℃)
Working Document : ECE/TRANS/WP.29/GRPE/2019/2
Informal Documents : GRPE-78-21
Main Modifications/Improvements in Working Document
reflection of Round Robin Test for gear shift point determination
make more robust for road load measurement and wind tunnel method
apply Vehicle_M concept to ICE vehicles
Both documents will be merged and submitted for WP.29 review and approval (2019 June session)

## Slide 5
1-1. Amendment 5 of GTR 15
(Type I test under 23℃)
Main Modifications/Improvements in Working Document _cont.
allow alternative procedure in case that practical errors have been identified during interpolation calculation
make it clear REESS voltage measurement during REESS energy change-based correction procedure
exempt the analysis of specific contaminants depending on the production process for hydrogen (fuel cell vehicles)
Main Modifications/Improvements in Informal Document
make “predominant mode” definition more robust (also in line with EU reg.)
allow break during coastdown measurement
[Road load matrix family 3 ton issue]

## Slide 6
1-2. Amendment 2 of GTR#19
(Evaporative Emission Test)
Working Document : ECE/TRANS/WP.29/GRPE/2019/4
Main Modifications/Improvements
allow alternative emission calculation formula (US EPA has been adopting for decades)
improve equipment calibration requirement ( some of equipment are missing)
make family definition more robust (also in line with EU reg.)
make it clear to install aged canister timing for robust procedure
Additional modification without document
Annex 1 Paragraph 3 & 5.1.3.2. : an aged canister → the aged canister

## Slide 7
UNR-WLTP
Low Temp TF
Remaining Open Issues
OBD
2. Overall Progress
Due to contradictory positions on a variety of item, completion of UNR and Low Temp TFs will be delayed by one or two GRPE sessions.
if CPs request
MAC
others
Due to non-urgent CP needs, MAC/other TFs will not be started until CPs provide a clear deadline.
Phase3 activities (limits/fuel/others) are already on
the table as a part of Transposition TF  may be skipped
depend on TF progress

## Slide 8
3. Status of each TF
TF | Status | Next Actions
Transposition to UNR | on going | plan to submit informal document @ 79th GRPE, collaborate with other TFs
Cycle/Gear Shift /Drive Trace Indices(DTI) | on going | Cycle : re-open when HEV system power is available Gear Shift : re-open TF for tool management DTI : outcome will be incorporated into UNR TF
Low Temp. | on going | EC has strong demand to complete by the end of 2019 collaborate with SG EV
Evapo. | COMPLETED | NA (re-open per CP needs)
Durability | PENDING | EU propose to develop as regional basis WLTP IWG holds its decision
COP | on going | outcome will be incorporated into UNR TF
OBD | will re-open | working items and schedule will be reviewed again and clear future actions will be developed
New Open Issues | COMPLETED with a few exemption | CFD : on going under the sub-group 4WD Chassis : outcome will be incorporated into UNR TF

## Slide 9
4. Outlook for 79th GRPE session in May
Working Categories | Expected Actions
GTR15 Amendment6, if ready | submit Informal Document for review
Transposition to UNR including durability and COP | submit Informal Document for review
Mandate | submit Informal Document to request for extension of mandate WLTP IWG for remaining Phase 2 activities and Phase 3 if needed
IWG Meeting | request full 1 day session including Transposition TF request half day session for SG-EV