## Slide 1: IWVTA Ambassador report to GRPE 80
William (Bill) Coleman
January 2020
informal document GRPE-80-14 80th GRPE, 14-17 January 2020
agenda item 11

## Slide 2: Request for Clarifications by IWG-IWVTA
Submitted by the GRPE-IWVTA Ambassador
IWVTA-30-11

## Slide 3: 58A Article 12
4. Notwithstanding that transitional provisions in any version of UN Regulations may have stipulated otherwise, Contracting Parties to this Agreement which are applying UN Regulations may, subject to compliance with the provisions of Article 2, nevertheless issue type approvals pursuant to earlier versions of UN Regulations.
However, subject to paragraph 3 of this Article, Contracting Parties applying a UN Regulation shall not be obliged to accept type approvals issued pursuant to these earlier versions.

## Slide 4: Example 1: UNR 83.01
13. TRANSITIONAL PROVISIONS RELATING TO APPROVED B OR C VEHICLES
13.1 The following provisions shall remain applicable until 31 December 1994 for vehicles newly put into service and type-approved before 1 July 1993:
13.1.1. At the request of the manufacturer, a test equivalent to the type I test for verifying emissions after a cold start may be conducted according to the requirements of paragraphs 13.1.1.1. and 13.1.1.2., for the approval and verification of production of category M1 vehicles equipped with an engine whose capacity is greater than or equal to 1,400 cm3 and fuelled with unleaded petrol or with diesel fuel.
The technical service in this case shall carry out the equivalent test described in annex 4A (EPA cycle) instead of that described in paragraph 5.3.1.
Question: May a Contracting Party still issue approvals to UNR 83.01 based on the EPA cycle? i.e. is this a version of the Regulation?
Answer: No. A version of a Series of Amendments is the valid text (including supplements) at the time of approval.

## Slide 5: Example 2: UNR 83.07
Footnote to table of emissions limits:
(2) Until three years after the dates specified in paragraphs 12.2.1 and 12.2.2 of this Regulation for new type approvals and new vehicles respectively, a particulate number emission limit of 6,0 × 1012 #/km shall apply to PI direct injection vehicles upon the choice of the manufacturer.
Question: May a Contracting Party still issue approvals to UNR 83.07 based on the 6,0 × 1012 #/km limit? i.e. is this a version of the Regulation? (it is based on the dates of a transitional provision but is not contained in it)
Answer: No. A version of a Series of Amendments is the valid text (including supplements) at the time of approval. This will however be resolved by Supplement 9

## Slide 6: Example 3: UNR 83.07
(7) . . . — not later than sixteen months after the dates set out in point 12.2.1, new type approvals shall only be performed with E10 and B7 fuels, — not later than as from dates set out in point 12.2.4, all new vehicles shall be approved with E10 and B7 fuels.
Question: May a Contracting Party still issue approvals to UNR 83.07 based on E5 or B5 fuels? i.e. is this a version of the Regulation?
Answer: No. A version of a Series of Amendments is the valid text (including supplements) at the time of approval. This will however be resolved by Supplement 9

## Slide 7: Other points discussed by IWG-IWVTA Bonn – November 2019

## Slide 8: Unique Identifier
WP.29 decided in June 2019 to ask all GRs to consider the relationship between UI and Approval Numbering/Marking
For Info to GRPE:
  The unique identifier is a means to group Approval numbers from several Regulations into a single marking.
  This is particularly useful for marking of components such as lighting clusters.

## Slide 9: Communication Document (TA Certificate)
Changes to certificate being considered to include „withdrawal of approval“ and „remarks“ and to remove „Extension number“ as this is included in the Approval number
Concerning:2 Approval granted
Approval extended
Approval refused
Approval withdrawn
Production definitively discontinued
of a vehicle type with regard to the emission of gaseous pollutants by the engine pursuant to UN Regulation No. WLTP
Approval No. ……….................................. Extension No. ……………………………
Reason for extension :……………………

## Slide 10: Manufacturer‘s Information Documents
It would appear that GRPE Regulations are exceptional in the ‚58 Agreement (with a few exceptions) as they prescribe a (minimum) format for the M.I.D.
It was reported that most manufacturers use the EU format for other UN Regulation applications (logical)
IWG DETA / IWG IWVTA will consider whether a formalisation of the link is desired.

## Slide 11
Thank you for your attention