## Slide 1
Progress report
of the
WLTP Informal Working Group
Prepared by WLTP IWG
Informal document GRPE-80-24e
80th GRPE, 15-17 January 2020, agenda item 3(b)

## Slide 2
Contents
WLTP IWG Activities
Action Lists during 80th GRPE
Overview of Working Documents
Overview of UNR WLTP
and Major Modifications from GTR15/19
Status of Sub-Groups / Task Forces
Outlook for 81st GRPE

## Slide 3
Since 79th GRPE session
Two (2) face-to face meetings
  Bern (September 25rd – 27th)
  Geneva (Jan 13th)
Fifty-seven (57) Webex meetings of Subgroup and/or TF
Two (2) experts meetings for specific items
As a result,
  Managed to complete Transposition proposal and include new elements
  Managed to keep Low T and OBD on challenging schedule
1. WLTP IWG Activities (1)

## Slide 4
Working Items |  | 2019 | 2020 |  |  |  | 
 |  | 10 | 1 | 3 | 6 |  | 7~
Transposition to UNR | UNR WLTP | WDs 2020/3-4 | IDs 80-38 80-39 |  |  |  | 
 | UNR 83-08 |  |  | WD |  |  | 
GTR#15 | Amd#6 |  | ID | WD | (ID) |  | 
 | Low Temp. |  |  | WD | (ID) |  | 
 | OBD |  |  | WD | (ID) |  | 
GTR#19 | Amd#3 | WD 2020/7 | ID 80-34 80-35 |  |  |  | 
WLTP Organization |  | inform GRPE of future activities⇒ |  |  | ID | New set-up? | 
WD : Working Document
ID : Informal Document
expect to complete most activities by end of mandate
we are here
1. WLTP IWG Activities (2)

## Slide 5
2. Action Lists during 80th GRPE session
Working Items | Expected Actions (informed during 79th session) | Action List
Transposition to UNR including durability, COP and OBD | submit Working Documents for approval | request for approval including informal documents which will be merged into Working documents
GTR19 Amd#3 | NA | 
GTR15 Amd#6 | submit Informal Document for review | request for review (GRPE-80-YY)
Low Temp. |  | 
OBD |  | 

## Slide 6
3. Overview of Working Documents
Due to the inclusion of new elements (e.g. COP, Durability, OBD),
a variety of complicated issue and enthousiastic last mimute text improvement, informal documents were submitted to finalize the working documents.
 | Working documents | Informal documents
UNR WLTP | ECE/TRANS/WP.29/GRPE/2020/3 ECE/TRANS/WP.29/GRPE/2020/4 | GRPE-80-38 and 39 to finalize the Working Documents
GTR19 Amd#3 | ECE/TRANS/WP.29/GRPE/2020/7 | GRPE-80-34 and GRPE-80-35 to bring GTR in line with UNR WLTP

## Slide 7
4. Overview of UNR WLTP (1)
Contents | main sources | 00 series |  | 01 series
 |  | Level 1A | Level 1B | Level 2
1. Scope | GTR15/19 UNR83/101 Japanese Reg. | EU-WLTP | GTR15/19 | cover both Level 1A and 1B area
8. Conformity of production (COP) | EU-WLTP Japanese Reg. | EU-WLTP with slight modification | Japanese Reg. | satisfy both Level 1A and 1B requirement
13 Appendix 5. OBFCM | EU-WLTP | EU-WLTP | NA | EU-WLTP
Annexes Part A. Test report /communication and so on | EU-WLTP Japanese Reg. | ← | ← | ←
for more detail, please refer WLTP-29-05e

## Slide 8
Contents | main sources | 00 series |  | 01 series
 |  | Level 1A | Level 1B | Level 2
Annexes Part B | GTR15_Amd#5 | ← | ← | ←
B3. Reference fuels | GTR15_Amd#5 | limited to EU specification | limited to JPN specification | harmonized
B6a. Ambient Temperature Correction for CO2 | EU-WLTP | EU-WLTP | NA | EU-WLTP
B6b. Speed and distance correction for CO2 | EU-WLTP | EU-WLTP | NA | EU-WLTP
B7/B8. Calculations | GTR15_Amd#5 Japanese Reg. | GTR15_Amend#5 | Japanese Reg. | satisfy both Level 1A and 1B requirement
B8. EVs, FCHVs | GTR15_Amd#5 | ← + OVC-FCHV including interpolation method | GTR15_Amd#5 | ←
4. Overview of UNR WLTP (2)

## Slide 9
Contents | main sources | 00 series |  | 01 series
 |  | Level 1A | Level 1B | Level 2
C3. Type 4 test - Evaporative emissions | GTR19_Amd#2 | ← | ← | ←
C4. Type 5 test – Durability | UNR83 Japanese Reg. | UNR83 with slight modification | Japanese Reg. | UNR83 exclude bench ageing
C4 Appendix4. Special requirements for Hybrid Vehicles | UNR83 | ← | exclude | exclude
C5. On-Board Diagnostics (OBD) | UNR83 Japanese Reg. | ← | ← | ←
In service conformity | EXCLUDE from UNR-WLTP |  |  | 
 |  | taken care by UNR83-08 | NA | taken care by UNR83-08
4. Overview of UNR WLTP (3)

## Slide 10
4. Major Modifications from GTR15
Contents | Brief Description | Applicable to |  | 
 |  | 00 series |  | 01 series
 |  | Level 1A | Level 1B | Level 2
Regional Correction | speed trace and distance correction for ICE only | ✔ | NA | NA
 | ambient temperature correction for CO2 | ✔ | NA | with and without
Post-processing | add fuel efficiency (unit : km/L & km/kg) no utility factor for OVC-HEV | NA | ✔ | both
OBFCM | the devices for monitoring on board the vehicle the consumption of fuel and/or electric energy | ✔ | NA | ✔
Inclusion of OVC-FCHV | same concept as OVC-HEV test procedure | ✔ | NA | NA
Adoption of the interpolation method for FCHVs | same concept as other categories (ICE, HEVs and PEVs) | ✔ | NA | NA
for more detail, please refer WLTP-29-05e_Appendix01

## Slide 11
Contents | Brief Description | Applicable to |  | 
 |  | 00 series |  | 01 series
 |  | Level 1A | Level 1B | Level 2
Scope | modified to "engines fueled with petrol“ from "positive ignition engines“ | ✔ | ✔ | ✔
 | mono-fuel gas vehicle | NA | ✔ | ✔
Puff loss overflow measurement | sampling start time was modified to “5” from “1” min. to ensure accurate measurement when using SHED method | ✔ | ✔ | ✔
4. Major Modifications from GTR19
for more detail, please refer WLTP-29-05e_Appendix01

## Slide 12
5. Status of Task Force / Sub-Group
TF/SG | Status | Next Actions
GTR 15 Amendment | on going | plan to submit Working document @ 81st GRPE taking into account the comments made by India
Transposition to UNR | on going | plan to submit Working document for UNR83-08 @ 81st GRPE
Durability | COMPLETED | 
COP | COMPLETED | 
SG-EV | on going | develop Low Temp. test procedure, then incorporate into Working document
Cycle/Gear Shift | on going | Cycle : re-open when HEV system power is available Gear Shift : plan to complete tool management
Low Temp. | on going | plan to submit Working document @ 81st GRPE with collaboration of SG EV
OBD | on going | plan to submit Working document @ 81st GRPE
New Open Issues | COMPLETED | 

## Slide 13
6. Outlook for 81st GRPE session in June 2020
Working Categories | Expected Actions
UNR83-08 | submit Working Document for approval
GTR15 Amendment6 | submit Working Document for approval
Low Temp. procedure | submit Working Document for approval
OBD | submit Working Document for approval
Future working activities – new set-up WLTP IWG | submit Informal Document to consult with GRPE
IWG Meeting | request one and half day session for IWG meeting including SG-EV