Distr.

GENERAL

TRANS/WP.29/GRRF/2001/12

15 June 2001

ORIGINAL: ENGLISH

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on Brakes and Running Gear (GRRF)

(Fiftieth session, 10 – 12 September 2001,

agenda item 6.6.)

# PROPOSAL FOR DRAFT AMENDMENTS TO REGULATION No. 106

(Agricultural tyres)

Transmitted by the Expert from the

European Tyre and Rim Technical Organization (ETRTO)

Note:	The text reproduced below was prepared by the expert from ETRTO in order to add a new range of Implement tyres.  It is based on the text of a document distributed without a symbol (informal document No. 6) during the forty-ninth session of GRRF (TRANS/WP.29/GRRF/49, para. 71).  In addition, it contains a proposal to provide adequate markings for small tyres.

____________

_____________

Note:	This document is distributed to the Experts on Brakes and Running Gear only.

GE.01-

Insert a new paragraph 3.1.8., to read:

“3.1.8.	the inscriptions ‘LS-2’ or ‘LS-3’ in case of tractor-drive wheel tyres to be fitted to driven axles of forestry tractors”.

Paragraphs 3.1.8. to 3.1.11.(former), renumber as paragraphs 3.1.9. to 3.1.12.

Annex 7, part C, the table, amend to read:

“

| Speed (km/h) | Speed category symbol |  |  |
| --- | --- | --- | --- |
|  | A4 | A6 | A8 | D |  | (1) |
| 10 | + 20 | + 29 | + 40 | + 80 |  | + 58 |
| 15 | + 12 | + 21 | + 33 | + 73 |  | + 35 |
| 20 | [0] | + 14 | + 26 | + 65 |  | + 27 |
| 25 | - 2 | + 7 | + 19 | + 58 |  | + 20 |
| 30 | - 5 | [0] | + 12 | + 51 |  | + 14 |
| 35 |  | - 5 | + 5 | + 44 |  | + 10 |
| 40 |  | - 10 | [0] | + 36 |  | + 6 |
| 45 |  |  | - 5 | + 29 |  | + 2 |
| 50 |  |  | - 10 | + 21 |  | [0] |
| 55 |  |  |  | + 14 |  |  |
| 60 |  |  |  | + 7 |  |  |
| 65 |  |  |  | [0] |  |  |
| 75 |  |  |  | - 9 |  |  |

”

Annex 11, after the pictogram insert a note, to read as follows:

“Note: For tyres having a section height lower or equal to 120 mm, the dimension “9 a” should be “6 a”

________________