Informal document N° 17

(28th GRSP, 27 Nov.- 1 Dec. 2000

agenda item 2.7)

PROPOSAL FOR AMENDMENTS TO ECE R94

(Editorial changes to document TRANS/WP29/GRSP/2000/13)

### AMENDMENTS

Annex 10, para. 1.3.5, amend to read:

"… greater than 100 g. The length between the central horizontal axis of the impactor cylinder and the axis of rotation of the whole pendulum shall be 1250 ( 1 mm. The impact …"

Annex 10, para. 2.3.4, amend to read:

"… with a tolerance of ( 0.5°. Adjust the mount such that the line joining the knee clevis joint and the ankle attachment bolt is horizontal with a tolerance of ( 0.3° with the heel …"

Annex 10, para. 3.3.5, last sentence, amend to read:

"The impactor shall be guided to exclude significant lateral, vertical or rotational movement."

### JUSTIFICATIONS

Document TRANS/WP29/GRSP/2000/13 aims at aligning the current text of ECE R94 to the last amendment of the corresponding Directive (1999/98/EC). Some minor editorial errors should be corrected as above.

____________