Differences between ECE-compliance Buckles and Japan's Proposed Buckles　　　　　　　　　　　　　　　Informal document №8-b

［Document　2］

|  | Buckle/tongue composition | Latch mode | Release mode | Comment |
| --- | --- | --- | --- | --- |
| J A P A N | Tongue A | (1) Normal mode - Only latchable in this mode A front B front (2) Abnormal mode – No latching in all other modes B front A front A reversed B reversed A reversed B reversed | (1) Both tongues are simultaneously released when the buckle button is pressed. | ・Easy belt wearing due to separate latching of tongues ・No latching error due to latching only on normal mode ・One-action release operation |
| E C E |  | （１）Normal mode - Only latchable in this mode Setting together of two tongues Both simultaneously latched in buckle (2)Abnormal mode – No latching in all other modes A front B front B reversed A reversed B reversed A reversed | Both tongues are released in one set when the buckle button is pressed The tongues are separated from each other | ・Difficult to set tongues together in some assemblies ・No latching error due to latching only on normal mode ・Difficult to separate tongues after release in some assemblies (Not suitable for emergency evacuation) |

# Text boxes

×

Tongue B

Buckle

×

Buckle

x

x

x

×

×

×

○

①

①

②

②