| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. RESTRICTED TRANS/WP.29/GRE/2003/9 27 January 2003 ENGLISH Original: ENGLISH ENGLISH AND FRENCH ONLY |
| --- | --- | --- |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on Lighting and Light-Signalling (GRE)

(Fiftieth session, 7-11 April 2003, agenda item 2.2.)

PROPOSAL FOR DRAFT AMENDMENTS TO REGULATION No. 37

(Filament lamps)

Transmitted by the expert from the Working Party "Brussels 1952" (GTB)

Note:	The text reproduced below was prepared by the expert from GTB in order to insert into the Regulation provisions for a new double filament lamp of category HS5 for motorcycles.  The suggested amendments to the Regulation are marked in bold characters.  The text is based upon :

- The text of Revision 3;

- Including (draft) Supplements 21 and 22;

- Including draft Corrigendum 1 to Revision 3;

- Draft proposals to introduce red filament light source (TRANS/WP.29/GRE/2002/36);

- Draft proposals for editorial amendments (TRANS/WP.29/GRE/2002/31);

- Informal document No. 2 distributed during the forty-ninth session of GRE.

_______

__________________

Note:	This document is distributed to the Experts on Lighting and Light-Signalling only.

A.	PROPOSAL

Text of the Regulation,

Annex 1,

List of categories of filament lamps, amend to read:

“...

|  | Category | Sheet number(s) |  |
| --- | --- | --- | --- |

...

|  | HS2 | HS2/1..3 |  |
| --- | --- | --- | --- |
|  | HS5 | HS5/1..4 |  |
|  | R2 | R2/1..3 |  |

...”

List of sheets for filament lamps, amend to read:

“...

|  | Sheet number(s) |  |
| --- | --- | --- |

...

|  | HS2/1..3 |  |
| --- | --- | --- |
|  | HS5/1..4 |  |
|  | P19W/1..3 |  |

...”

New sheets HS5, insert in between sheet HS2/3 and sheet P19W/1 as indicated in the List of sheets above, to read:

(see next pages)

*      *     *

B.	JUSTIFICATION

The proposed draft amendments concern the addition of a new double filament lamp for motorcycles. The proposed introduction of a new harmonized symmetrical beam pattern was the immediate cause to this development.  The proposal also corrects a few editorial errors.

_________________

CATEGORY HS5 	Sheet HS5/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament lamp

FILAMENT LAMP FOR MOTORCYCLES

1/	The reference plane is defined by the three ramp inside surface.

2/	The reference axis is perpendicular to the reference plane and passing through the centre of the 23 mm cap diameter.

3/	Glass bulb and supports shall not exceed the envelope as indicated in figure 1. The envelope is concentric to the reference axis.

4/	Glass bulb shall be optically distortion free within the angles (1 and (2. This requirement applies to the whole bulb circumference within the angles (1 and (2.

5/	The obscuration shall extend at least to angle (3 and shall extend at least to the cylindrical part of the bulb on the whole top circumference.

CATEGORY HS5 	Sheet HS5/2

CATEGORY HS5 	Sheet HS5/3

| Dimensions in mm | Filament lamps of normal production | Standard filament lamp |
| --- | --- | --- |
|  | 12V | 12V |
| e | 26 | 6 / | ( 0.15 |
| lC 7 / | 4.6 |  | ( 0.3 |
| k | 0 |  | ( 0.2 |
| h1, h3 | 0 |  | ( 0.15 |
| h2, h4 | 0 |  | ( 0.20 |
| lR 7 / | 4.6 |  | ( 0.3 |
| j | 0 |  | ( 0.2 |
| g1, g3 | 0 |  | ( 0.30 |
| g2, g4 | 2.5 |  | ( 0.40 |
|  | 50( min. | - | - |
|  | 23( min. | - | - |
|  | 50( min. | - | - |
| Cap P23t in accordance with IEC Publication 60061 (sheet 7004-....-1) |
| ELECTRICAL AND PHOTOMETRIC CHARACTERISTCS |
| Rated values | Voltage | V | 12 | 12 |
|  | Wattage | W | 35 | 30 | 35 | 30 |
| Test voltage | V | 13.2 | 13.2 |
| Objective Values | Wattage | W | 40 max. | 37 max. | 40 max. | 37 max. |
|  | Luminous flux | lm | 620 | 515 |  |  |
|  |  | (% | 15 | 15 |  |  |
| Reference luminous at approximately 12V | 460 lm | 380 lm |

6/	To be checked by means of a “box-system”. Sheet HS5/4.

7/	The positions of the first and the last turn of the filament are defined by the intersections of the outside of the first and the outside of the last light-emitting turn, respectively, with the plane parallel to and 26 mm distant from the reference plane.

CATEGORY HS5 	Sheet HS5/4

Screen projection requirement

This test is used to determine whether a filament lamp complies with the requirements by checking whether:

(a)  the passing-beam filament is correctly positioned relative to the reference axis and the reference plane; and whether

(b)  the driving-beam filament is correctly positioned relative to the passing-beam filament.

Side elevation

| Reference | a | b | c | d | v |
| --- | --- | --- | --- | --- | --- |
| Dimensions | d1+0.6 | d1+0.8 | d2+1.2 | d2+1.6 | 2.5 |

d1 : Diameter of the passing-beam filament

d2 : Diameter of the driving-beam filament

Front elevation

| Reference | h | k |
| --- | --- | --- |
| Dimensions | 6.0 | 0.5 |

The filaments shall lie entirely within the limits shown.

The centre of the filament shall lie within the limits of dimension k.

________________

# Text boxes

//

Dimensions in millimeters

Driving-beam filament

# Passing-beam filament

26.0 to reference plane

a

b

v

d

c

Reference axis

Reference axis

h4

h2

Filament centre

e

g3

g1

j

lR

e

h3

h1

k

lC

g4

g2

Reference axis

#### View A of passing-beam filament

#### View B of driving-beam filament

Top view of passing-beam filament

Top view of driving-beam filament

##### Figure 3

Filament position and dimensions

Filament centre

3 /

Reference axis  2 /

Reference axis  2 /

5 /

4 /







Figure 2  Distortion free area 4 / and black top 5 /

Ø24.5

max

50max

#### Reference plane  1 /

## B

e

#### A

# Figure 1  Main drawing

#### Earth

Driving - beam

#### Passing - beam

26.0 to reference plane

h

//

k    k

Reference axis