ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport 	INF. 32

of Dangerous Goods	Original: ENGLISH

(Seventy-first session,

Geneva, 5-9 November 2001)

Fire-fighting appliances

Transmitted by the Government of Germany

Doc. TRANS/WP.15/2001/29

Report on the operational tests on fire extinguishers
Eynatten and Brussels, 26 October 2001

According to the decision taken at the working-group meeting of ADR-ECE/WP15 of München on 27 and 28/06/2001 fire extinguishers were collected from lorries on 26/10/2001 in the morning and brought to the laboratories of APRAGAZ for testing (in the presence of different members of the WG, see attached list).

It was agreed to take into consideration only conform extinguishers – to the law of each country and with the date of validity or date of next control still valid.

6 German extinguishers identified 1 D to 6 D and 7 Belgian extinguishers identified 1 B to 7 B were collected in the morning on lorries at the border D-B in Eynatten/Lichtenbusch.

These extinguishers were in the afternoon tested in the laboratories of APRAGAZ according EN3-1 : 1996 point 6 “Duration of operation and residual charge” + testing Method according annex A.

The results of the tests are as follows :

# German Extinguishers :

| N° | Nom. charge Powder (*) | Manufacturing date | Validity date | Discharge Time sec. | Residual charge kg |
| --- | --- | --- | --- | --- | --- |
| 1 D | 6 kg Cart | 1992 | 05/2002 | 13 | 0,070 |
| 2 D | 6 kg SP | 04/1974 | 09/2002 | 13 | 0,280 |
| 3 D | 6 kg SP | 1985 | 03/2002 | 20 | 0,040 |
| 4 D | 6 kg Cart | 1986 | 04/2002 | 13 | + 0,280 (overfilled) |
| 5 D | 6 kg Cart | 1992 | 02/2002 | 13 | + 0,110 (overfilled) |
| 6 D | 6 kg Cart | 2000 | 08/2001 | 22 | 0,110 |

# Belgian Extinguishers :

| N° | Nom. charge Powder (*) | Manufacturing date | Validity date | Discharge Time sec. | Residual charge kg |
| --- | --- | --- | --- | --- | --- |
| 1 B | 9 kg Cart | 2000 | 01/2006 | 37 | 0,920 |
| 2 B | 9 kg Cart | 02/1997 | 01/2003 | 18 | 0,400 |
| 3 B | 9 kg Cart | 2000 | 01/2006 | 26 | 0,115 |
| 4 B | 9 kg Cart |  | 01/2003 | not tested, see note below |
| 5 B | 3 kg Cart | 1998 | 01/2004 | 16 | 0,050 |
| 6 B | 9 kg Cart | 2001 | 01/2007 | 40 | 0,870 |
| 7 B | 3 kg Cart | 1997 | 01/2003 | 14 | 0,140 |

(*)	SP = Stored Pressure Extinguisher

Cart = Cartridge type Extinguisher

Extinguisher No. 4 B has not been tested because of lack of conformity with the belgium law (extinguisher was intended for buildings and was damaged by a hole in the main compartment).

Two more belgium extinguishers have not been taken from the lorries as they have been found out to be 12 years old (label showed validity until 2003 but it was manipulated).

#### Conclusion

The results of the operational tests (duration of operation and residual charge) showed some recognizable deviations, but are certified to be in conformity with the requirements of the EN3-1 standard by APRAGAZ.

All the tested extinguishers taken from the German and Belgian lorries worked properly.

Attachment 1

List of Participants

Name	Company

Rasmussen, Soren	IRU, Geneve

van Impe, Patricia	Febetra, Bruxelles

Vandenbergen, Eric	ITR, Bruxelles

Maiworm, Robert	BAG, Köln

Harnack, Michael	bvfa / Gloria

Leplat, Christian	APRAGAZ

Geerwars, Jos	APRAGAZ

Vanderschriek, Mr	APRAGAZ

Laufhütte, Klaus	BMVBW, Germany

Holzhäuser, Jörg	MWVLW, Mainz, Germany

Renard, Claude 	Min. des Communications

____________

# Footnotes

Brussels only