UNITED

NATIONS

Distr.

Economic and Social		GENERAL

Council

TRANS/WP.29/2002/43

12 April 2002

ENGLISH

Original:	ENGLISH and

FRENCH

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

(One-hundred-and-twenty-seventh session,

25-28 June 2002, agenda item 4.2.3.)

DRAFT CORRIGENDUM 3 TO REGULATION No. 13-H

(Harmonization braking)

Transmitted by the Working Party on Brakes and Running Gear (GRRF)

Note:  The text reproduced below was adopted by GRRF at its fifty-first session, and is transmitted for consideration to WP.29 and to AC.1.  It is based on the text reproduced in the session report (TRANS/WP.29/GRRF/51, para. 8).

__________

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

Annex 5, paragraph 3.1.(A), correct to read (footnote 2/ not modified):

"3.1.(A)	For all states of load of the vehicle, the adhesion utilization curve of the rear axle shall not be situated above that for the front axle:  2/

for all braking rates between 0.15 and 0.8:"

____________

# Text boxes

E