Informal document No. GRSG-86-6e

(86th GRSG, 19-23 Pril 2004.

agenda item 10.5.)

The revised text of the Annex 7 of the Consolidated Resolution R.E.3

(document TRANS/WP.29/78/Rev.1/Amend.2)

###### Transmitted by the expert from the Russian federation

| 1. | CATEGORY L – power driven VEHICLES WITH LESS THAN FOUR WHEELS |
| --- | --- |
| 1.1. | Category L1 A two-wheeled vehicle with a maximum design speed of not more than 45 km/h and an engine whose cylinder capacity does not exceed 50 cm3 in the case of the internal combustion type, or maximum continuous rated power is no more than 4 kW in the case of an electric motor. |
| 1.2. | Category L2 A three-wheeled vehicle with a maximum design speed of not more than 45 km/h and an engine whose cylinder capacity does not exceed 50 cm3 if of the spark (positive) ignition type, or maximum net power output does not exceed 4 kW in the case of other internal combustion engines, or maximum continuous rated power does not exceed 4 kW in the case of an electric motor. |
| 1.3. | Category L3 A two-wheeled vehicle without a side-car with an engine having a cylinder capacity of more than 50 cm3 if of the internal combustion type and/or a maximum design speed of more than 45 km/h. |
| 1.4. | Category L4 A two-wheeled vehicle with a side-car with an engine having a cylinder capacity of more than 50 cm3 if of the internal combustion type and/or a maximum design speed of more than 45 km/h. |
| 1.5. | Category L5 A vehicle with three symmetrically arranged wheels fitted with an engine having a cylinder capacity of more than 50 cm3 if of the internal combustion type and/or a maximum design speed of more than 45 km/h. |
| 1.6. | Category L6 A vehicle with four wheels whose unladen mass is not more than 350 kg, not including the mass of the batteries in case of electric vehicles, whose maximum design speed is not more than 45 km/h, and whose engine cylinder capacity does not exceed 50 cm³ for spark (positive) ignition engines, or whose maximum net power output does not exceed 4 kW in the case of other engines 1/ |

| 1.7. | Category L7 A vehicle with four wheels, other than that classified for the category L6, whose unladen mass is not more than 400 kg (550 kg for vehicles intended for carrying goods), not including the mass of batteries in the case of electric vehicles, and whose maximum net engine power does not exceed 15 kW 2/ |
| --- | --- |

Notes:

1/ If a separate ECE Regulation does not stipulate differently, for the purpose of that Regulation such a vehicle shall be considered as of category L2

2/ If a separate ECE Regulation does not stipulate differently, for the purpose of that Regulation such a vehicle shall be considered as of category L5