INF.39

# ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Joint Meeting of the RID Safety Committee and the
Working Party on the Transport of Dangerous Goods
(Geneva, 13 - 23 September 2005, agenda item 3)

Standards

### Comments from Switzerland on Standards listed for discussion at the Standards Working Group

Transmitted by the European Committee for Standardization (CEN)

Standards Working Group of the Joint Meeting ADR/RID

5th meeting, 13-15 September 2005, Geneva

Comments on standards submitted by CEN before the meeting

A. Standards at Stage 2: Submitted for Public Enquiry

Dispatch from CEN dated 13 January 2005

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| PrEN 14638-1 | Transportable gas cylinders – Refillable welded receptacles of a capacity not exceeding 150 litres – Part 1: Welded austenitic stainless steel cylinders made to a design justified by experimental methods | 6.2.2 |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
| CH | 10 | Marking |  | Has to be in accordance with RID/ADR | Remark in RID/ADR |  |  |

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| prEN1442:1998 rev 2005 | Transportable refillable welded steel gas cylinders for liquefied petroleum gas (LPG) - Design and construction | 6.2.2 |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
| CH | Whole Standard |  |  | There is already a new standard for welded steel cylinders mentioned in RID/ADR (EN 13322-1:2003). This standard is therefore unnecessary and the present EN 1442:1998 could be removed! |  |  |
| CH | Annex A | Table A1-.1 |  | If you put the gas name „Butane“ somewhere in the ADR marking area, this may be confusing. If the test pressure of 15 bar is a problem for the owner then it should clearly be stated above or below the ADR/RID marking „FOR UN 1011/1095 BUTANE ONLY“. But this marking shall not conflict with the required marks | See decision to EN1442:1198:prA” in INF. 32 Annex 2 (Sept. 2004) |  |  |
| CH | 5.1.3 | Test pressure |  | The calculation pressure shall at least be the test pressure as recommended in RID/ADR P200 |  |  |  |
| CH | 9.8.5 | Weld repairs |  | Cylinders originally heat treated have to be heat treated again after weld repair |  |  |  |
| CH | 10 | Marking |  | Marking has to be in accordance with RID/ADR | Remark: Exclude clause 10 |  |  |

Dispatch from CEN dated July 2005

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| prEN ISO 23667 | Packaging - Transport packaging for dangerous goods – Rigid plastics and plastics composite IBC’s - Compatibility testing |  |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
| CH | Annex C | Table C.1 |  | As this table is part of RID/ADR and may be changed at some time it can only be, as stated, for information only | Remark: Table C.1 to be excluded in RID/ADR |  |  |
| Decision of the Standards Working Group: | Accepted: □ Refused: □ | Comments: |

B. Standards at Stage 3: Submitted for Final Voting

Dispatch from CEN dated 21 January 2005

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| prEN 1968 A1 | Periodic inspection and testing of seamless steel gas cylinders | 6.2.2 |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
| CH |  |  |  | -- |  |  |  |
| Decision of the Standards Working Group: | Accepted: □ Refused: □ | Comments: |

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| prEN 13530-2/A1 | Cryogenic vessels – Large transportable vacuum insulated vessels - Part 2: Design, fabrication, inspection and testing. |  |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
| CH |  |  |  | -- |  |  |  |
| Decision of the Standards Working Group: | Accepted: □ Refused: □ | Comments: |

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| prEN ISO 7866 | Gas cylinders - Refillable seamless aluminium alloy gas cylinders – Design, construction and testing |  |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
| CH |  |  |  | -- |  |  |  |
| Decision of the Standards Working Group: | Accepted: □ Refused: □ | Comments: |

Dispatch from CEN dated 7 March 2005

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| prEN ISO 16103 | Packaging - Transport packaging for dangerous goods – Recycled plastics compatibility material |  |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
| CH |  |  |  | -- |  |  |  |
| Decision of the Standards Working Group: | Accepted: □ Refused: □ | Comments: |

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| prEN 1439 rev | Transportable refillable welded and brazed steel Liquefied Petroleum Gas (LPG) cylinders - Procedure for checking before, during and after filling |  |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
| Only the version 2004-10 was available, the actual version is 2005-05!! |  |  |  |  |
| CH | 3.5 |  |  | Protected cylinders are not cylinders in accordance with RID/ADR, this type of cylinders has already been discussed in the joint meeting and has been rejected. | Remark in RID/ADR where the Standard is placed |  |  |
| CH | Annex A | Table A.1 |  | It is not visible which area shall be used for RID/ADR cylinders | Remark: for RID/ADR only Area I is applicable |  |  |
| Decision of the Standards Working Group: | Accepted: □ Refused: □ | Comments: |

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| EN 12863:2002/prA1 | Transportable gas cylinders - Periodic inspection and maintenance of dissolved acetylene cylinders. |  |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
| CH |  |  |  | -- |  |  |  |
| Decision of the Standards Working Group: | Accepted: □ Refused: □ | Comments: |

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| EN13365:2002/prA1 | Transportable gas cylinder - Cylinder bundles for permanent and liquefied gases (excluding acetylene) - Inspection at time of filling |  |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
| CH |  |  |  | -- |  |  |  |
| Decision of the Standards Working Group: | Accepted: □ Refused: □ | Comments: |

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| prEN 14763 | Transportable refillable composite cylinders for liquefied petroleum gas (LPG) - Procedure for checking before, during and after filling |  |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
| CH | General remark to standards concerning tests on LPG cylinders: Concerning rejection criteria in the tables where additional test decide about rejection: As long as there are no tests carried out, every cylinder with a defect has to be rejected and scrapped. It can not be the job of a filling station or a testing body to arrange these tests. These standards are therefore not suitable for the inspection and test personell! Standards affected: prEN14763, prEN 14767, prEN 14913, prEN 14914 |  |  |
| CH | 3.14 | Periodic inspection |  | For periodic inspection the type approval and the standard used for type approval have to be considered not prEN 14427 in general | Remark: 3.14 not to use in RID/ADR |  |  |
| CH | 4.2 b) |  |  | A relief valve is not mandatory for all type of cylinders (see also 4.4 c)) | Remark: Exclude this point from RID/ADR |  |  |
| CH | Annex A | Table A.1 |  | It is not visible which area shall be used for RID/ADR cylinders | Remark: for RID/ADR only Area I is applicable |  |  |
| Decision of the Standards Working Group: | Accepted: □ Refused: □ | Comments: |

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| prEN 14794 | Transportable refillable aluminium cylinders for liquefied petroleum gas (LPG) - Procedure for checking before, during and after filling |  |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
| CH | Annex A | Table A.1 |  | It is not visible which area shall be used for RID/ADR cylinders | Remark: for RID/ADR only Area I is applicable |  |  |
| CH | 3.3 | Periodic inspection |  | For periodic inspection the type approval and the standard used for type approval have to be considered not prEN 14427 in general | Remark: 3.3 not to use in RID/ADR |  |  |
| Decision of the Standards Working Group: | Accepted: □ Refused: □ | Comments: |

Dispatch from CEN dated 11 April 2005

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| prEN 14767 | Transportable refillable composite cylinders for liquefied petroleum gas (LPG) - Periodic requalification |  |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
|  | CH: General remark to standards concerning tests on LPG cylinders: Concerning rejection criteria in the tables where additional test decide about rejection: As long as there are no tests carried out, every cylinder with a defect has to be rejected and scrapped. It can not be the job of a filling station or a testing body to arrange these tests. These standards are therefore not suitable for the inspection and test personell! Standards affected: prEN14763, prEN 14767, prEN 14913, prEN 14914 |  |  |
| CH | Annex A | Inspection interval |  | Inspection interval and requirements for extension to be decided by competent authority | Remark: Annex A to be excluded from RID/ADR |  |  |
| CH | 3.3 | Periodic inspection |  | For periodic inspection the type approval and the standard used for type approval have to be considered not prEN 14427 in general | Remark: 3.3 not to use in RID/ADR |  |  |
| CH | 5 | Periodic inspection |  | The inspection procedures have to be in accordance with RID/ADR. For the periodic inspection according to RID/ADR a hydraulic test has to be applied at test pressure. It could be replaced by a pneumatic test pressure but not by other tests. A leak test a low pressure cannot replace the pressure test. | Remark: Inspection in accordance with RID/ADR |  |  |
| CH | 7.4 | Marking |  | Marking in accordance with RID/ADR | prEN 14894 not to be used |  |  |
| Decision of the Standards Working Group: | Accepted: □ Refused: □ | Comments: |

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| EN ISO 10156-2 | Gas cylinders – Gases and gas mixtures –Part 2: Determination of oxidising ability of toxic and corrosive gases and gas mixtures |  |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
| CH | All | EN ISO 10156-2 has already been published! (August 2005) ISO 10156 Gases and gas mixtures-Determination of fire potential and oxidizing ability for the selection of cylinder valve outlets | ISO 10156-2 to be placed in RID/ADR 2.2.2.1.5 ISO 10156 to be placed in RID/ADR 6.2.2 either for materials or for closures |  |  |
| Decision of the Standards Working Group: | Accepted: □ Refused: □ | Comments: |

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| prEN ISO 11114-4 | Transportable gas cylinders - Compatibility of cylinder and valve materials with gas contents - Part 4: Test methods for selecting metallic materials resistant to hydrogen embrittlement | 6.2.2 |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
| CH |  |  |  | -- |  |  |  |
| Decision of the Standards Working Group: | Accepted: □ Refused: □ | Comments: |

Dispatch from CEN dated 9 May 2005

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| prEN 1440: 1996 REVIEW | Transportable refillable welded and brazed steel Liquefied Petroleum Gas (LPG) cylinders - Periodic inspection |  |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
| CH | Whole Standard |  |  | There is already a standard for the periodic inspection of welded steel cylinders mentioned in RID/ADR (EN 1803) this standard is therefore unnecessary. |  |  |
| CH | 1 | “This European Standard specifies inspection intervals,….” |  | The inspection interval is specified by RID/ADR | Remark: Inspection intervals in accordance with RID/ADR |  |  |
| CH | 3.5 |  |  | Protected cylinders are not cylinders in accordance with RID/ADR, this type of cylinders has already been discussed in the joint meeting and has been rejected. | Remark in RID/ADR where the Standard is placed |  |  |
| CH | 4 | Interval |  | The general interval in accordance to RID/ADR is 10 Years, 15 years is the exemption | Remark |  |  |
| CH | 4 / 5 | The inspection Procedures to be applied shall be selected from the alternatives given in clause 5 |  | The inspection procedures have to be in accordance with RID/ADR. For the periodic inspection according to RID/ADR a hydraulic test has to be applied at test pressure. It could be replaced by a pneumatic test pressure but not by other tests. A leak test a low pressure cannot replace the pressure test. | Remark: Inspection in accordance with RID/ADR |  |  |
| CH | 5.2 | External Visual Inspection |  | Checking the marking is also a part of the visual inspection in accordance with RID/ADR | amend |  |  |
| CH | 5.3.2.4 Note | Welding or repairing should be carried out in accordance with the manufacturers requirements |  | Repair procedures have to be as agreed with the competent authority. |  |  |  |
| CH | 7.4 | Marking |  | The marking has to be in accordance with RID/ADR |  |  |  |
| Decision of the Standards Working Group: | Accepted: □ Refused: □ | Comments: |

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| EN12252:2000/prREV | Equipping of Liquefied Petroleum Gases (LPG) road tankers |  |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
|  | 9.2.6 | Leak test |  | “If the Tank is in gas service the leak proofness test shall be not less than 20% of the test pressure the LPG vapour pressure” The meaning of this sentence is not clear; ADR requires at any time 20% of the test pressure for leakproofness test. (6.8.3.4.9) | Ammend sentence to: ..or the LPG vapour pressure if higher |  |  |
|  | Annex A: | A.1 |  | “The pressure valve shall be set to the design pressure of the tank, see EN12493” This isa deviation to ADR which requires: “These valves shall be capable of opening automatically under a pressure between 0.9 and 1.0 times the test pressure of the tank to which they are fitted” These pressures are different | Remark Annex A to be exluded from ADR |  |  |
|  |  | A.2 |  | Examples Note: The calculations are based on a set pressure of 17 bar/gauge ADR requires: ”These valves shall be capable of opening automatically under a pressure between 0.9 and 1.0 times the test pressure of the tank to which they are fitted” ( 6.8.3.2.9 Test Pressure (Table 4.3.3.2.5 In ADR, the test pressure of these tanks can be 27 bars; the setting of the safety valve shall therefore be 24.3 bars |  |  |  |
| Decision of the Standards Working Group: | Accepted: □ Refused: □ | Comments: |

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| prEN 14795 | Transportable refillable aluminium cylinders for Liquefied Petroleum Gas (LPG) - Periodic inspection |  |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
| CH | 5.1 |  |  | Reconditioning procedures have to be as agreed with the competent authority. |  |  |  |
| CH | 5.1 |  |  | The inspection procedures have to be in accordance with RID/ADR. For the periodic inspection according to RID/ADR a hydraulic test has to be applied at test pressure. It could be replaced by a pneumatic test pressure but by the agreement of the testing and certifying body. | Remark: Inspection in accordance with RID/ADR |  |  |
| CH | 7.4 | Marking |  | Marking in accordance with RID/ADR | prEN 14894 not to be used |  |  |
| Decision of the Standards Working Group: | Accepted: □ Refused: □ | Comments: |

Dispatch from CEN dated July 2005

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| EN 13322-1:2003/ prA1 | Transportable gas cylinders - Refillable welded steel gas cylinders - Design and construction - Part 1: Carbon steel |  |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
| CH |  |  |  | -- |  |  |  |
| Decision of the Standards Working Group: | Accepted: □ Refused: □ | Comments: |

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| prEN ISO10297 | Transportable gas cylinders – Cylinder valves – Specification and type testing |  |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
| CH |  |  |  | prEN ISO 10297 has been published! |  |  |  |
| CH | 7 | Marking |  | The working or test pressure should also be marked |  |  |  |
| Decision of the Standards Working Group: | Accepted: □ Refused: □ | Comments: |

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| prEN 14912 | LPG equipment and accessories – Inspection and maintenance of LPG cylinder valves at time of periodic inspection of cylinders |  |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
| CH | All |  |  | As with EN 14189 there is already a Standard for the periodic inspection of valves in RDID/ADR ther is no need for a additional on. |  |  |
| Decision of the Standards Working Group: | Accepted: □ Refused: □ | Comments: |

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| prEN 14913 | Transportable refillable welded steel cylinders for Liquefied Petroleum Gas (LPG) – Alternative design and construction - Procedure for checking before, during and after filling |  |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
| CH | All |  |  | It is not clear why there has to be an additional standard for these cylinders as there is no difference for the inspection. A filer will not be able to distinguish between cylinders manufactured to different standards. This standard should therefore not be mentioned in RID/ADR. |  |  |
|  | CH: General remark to standards concerning tests on LPG cylinders: Concerning rejection criteria in the tables where additional test decide about rejection: As long as there are no tests carried out, every cylinder with a defect has to be rejected and scrapped. It can not be the job of a filling station or a testing body to arrange these tests. These standards are therefore not suitable for the inspection and test personell! Standards affected: prEN14763, prEN 14767, prEN 14913, prEN 14914 |  |  |
| CH | Annex A | Table A.1 |  | It is not visible which area shall be used for RID/ADR cylinders | Remark: for RID/ADR only Area I is applicable |  |  |
| Decision of the Standards Working Group: | Accepted: □ Refused: □ | Comments: |

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| prEN 14914 | Transportable refillable welded steel cylinders for Liquefied Petroleum Gas (LPG) – Alternative design and construction - Periodic inspection |  |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
| CH |  |  |  | It is not clear why there has to be an additional standard for these cylinders as there is no difference for the inspection. This standard should therefore not be mentioned in RID/ADR |  |  |
|  | CH: General remark to standards concerning tests on LPG cylinders: Concerning rejection criteria in the tables where additional test decide about rejection: As long as there are no tests carried out, every cylinder with a defect has to be rejected and scrapped. It can not be the job of a filling station or a testing body to arrange these tests. These standards are therefore not suitable for the inspection and test personell! Standards affected: prEN14763, prEN 14767, prEN 14913, prEN 14914 |  |  |
| CH | 5.1 |  |  | The inspection procedures have to be in accordance with RID/ADR. For the periodic inspection according to RID/ADR a hydraulic test has to be applied at test pressure. It could be replaced by a pneumatic test pressure with the agreement of the testing and certifying body. Internal inspection is mandatory. | Remark: Inspection in accordance with RID/ADR |  |  |
| CH | Annex A | Inspection interval |  | Inspection interval and requirements for extension to be decided by competent authority | Remark: Annex A to be excluded from RID/ADR |  |  |
| CH | 7.4 | Marking |  | Marking in accordance with RID/ADR | prEN 14894 not to be used |  |  |
| Decision of the Standards Working Group: | Accepted: □ Refused: □ | Comments: |

| Reference | Title of document | Where to refer in ADR/RID | Applicable sub-sections and paragraphs |
| --- | --- | --- | --- |
| EN 14427:2004 prA1 | Transportable composite cylinders for LPG – Design and construction |  |  |
| Comments from members of the Joint Meeting: |
| Country | Clause No./ | Paragraph/ Figure/Table/Note (e.g. Table 1) | Type of comment (Editorial/ Technical) | Comment (justification for change) | Proposed change | Comment from CEN Consultant | Comment from WG Standards |
| CH |  |  |  | Remark by the CE Consultant must be followed | This remark has to be stated in RID/ADR otherwise A1 has to be cancelled for RID/ADR |  |  |
| Decision of the Standards Working Group: | Accepted: □ Refused: □ | Comments: |

# Text boxes

INF.39

page 2

INF.39

page 3

INF.39

page 4

INF.39

page 5

INF.39

page 5

INF.39

page 6

INF.39

page 7

INF.39

page 8

INF.39

page 9

INF.39

page 10

INF.39

page 11

INF.39

page 12

INF.39

page 13

INF.39

page 14

INF.39

page 15

INF.39

page 16

INF.39

page 17

INF.39

page 18

INF.39

Page 19

INF.39

page 20

INF.39

page 21

INF.39

page 22

INF.39

page 23