| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL TRANS/WP.29/GRSP/2005/16 26 September 2005 Original: ENGLISH ENGLISH AND FRENCH ONLY |
| --- | --- | --- |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on Passive Safety (GRSP)

(Thirty-eighth session, 6-9 December 2005,

agenda item B.1.3.)

#### PROPOSAL FOR DRAFT AMENDMENTS TO REGULATION No. 16

(Safety belts)

Transmitted by the expert from France

Note: The text reproduced below was prepared by the expert from France in order to reduce the risks of interference of the tongue of the unbuckled belt with the interior components and the vehicle doors and to improve the grip of the tongue to buckle the belt.   It is based on a document distributed without a symbol (informal document No. GRSP-37-13) during the thirty-seventh session (TRANS/WP.29/GRSP/37, para. 15). The amendments to the current text of the Regulation are marked in bold characters.  The deleted text is indicated as strikethrough.

________________

Note: This document is distributed to the Experts on Passive Safety only.

A.	PROPOSAL

Paragraph 8.2.2.5., amend to read:

"8.2.2.5. 	The technical service shall verify that, with the buckle tongue engaged in the buckle and no occupant in the seat: "

Paragraph 8.2.2.5.2., amend to read:

"8.2.2.5.2. 	in the case of three-point belts, a tension of at least 50 N can be established in the lap section of the belt by external application of tension in the diagonal section of the belt, when positioned:

- on a 10-year manikin as specified in Annex 8, Appendix 1 to Regulation No. 44 and set in accordance with Annex 17, Appendix 4 to the present Regulation;

- and on the fixture specified in Annex 17, Appendix 1, figure 1 to the present Regulation for the seats that enable the installation of a child restraint device of universal category."

Annex 17, insert a new Appendix 4 to read:

"Annex 17 – Appendix 4

INSTALLATION OF 10-YEAR MANIKIN

-	Adjust the seat to its fully rearward position.

-	Adjust the seat height in accordance with the manufacturer’s specifications. In the absence of any specification, adjust the seat to the lowest position.

-	Adjust the seat back angle to the manufacturer's design position. In the absence of any specification, an angle of 25 degrees from the vertical, or the nearest fixed position of the seat back, should be used.

-	Set the shoulder anchorage to the lowest position.

-	Set the manikin on the seat ensuring that the pelvis is in contact with the seat back.

-	The longitudinal plan passing by the manikin centre line will be on the apparent centre line of the seating position."

B.	JUSTIFICATION

The 50 N tension was introduced so as to guarantee the free sliding motion of the lap section of the belt in the tongue to ensure the restraint of universal child restraint systems and the restraint of any passenger of 10 years old and more.  The introduction in 1999, with the supplement 8 of the series 4 of amendments of Regulation No. 16, of a fixture to check the compatibility of safety belts with child restraint systems of "universal category", no longer justifies the verification of the tension of the lap section without an occupant.  Therefore, it is proposed to check this 50 N tension with the manikin that corresponds to the lowest limit of use of the belt and with the fixture for the seats that enable the installation of a child restraint system of “universal” category.  This amendment aims at reducing the risks of interference of the tongue of the unbuckled belt with the interior components and the vehicle doors and at improving the grip of the tongue to buckle the belt.

- - - - -