| UNITED NATIONS | E |
| --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2006/19 19 December 2005 ENGLISH Original: ENGLISH and FRENCH |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

(One-hundred-and-thirty-eighth session, 7-10 March 2006,

agenda item 4.2.24.)

#### PROPOSAL FOR SUPPLEMENT 6 TO REGULATION No. 112

(Headlamps emitting an asymmetrical passing beam)

Transmitted by the Working Party on Lighting and Light-Signalling (GRE)

Note:  The text reproduced below was adopted by GRE at its fifty-fifth session, and is transmitted for consideration to WP.29 and to AC.1 (TRANS/WP.29/GRE/55, para. 52).  It is based on document TRANS/WP.29/GRE/2005/32, not amended.

Paragraph 6.2.9., amend to read:

"6.2.9.	The requirements in paragraph 6.2.5. above shall also apply to headlamps designed to provide bend lighting and/or that include the additional light source referred to in paragraph 6.2.10.2.  In the case of a headlamp designed to provide bend lighting its alignment may be changed, provided that the axis of the beam is not displaced vertically by more than 0.2 °."

- - - - -