| UNITED NATIONS | E |
| --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/GRRF/2007/11 10 July 2007 Original: ENGLISH ENGLISH AND FRENCH ONLY |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

Working Party on Brakes and Running Gear

Sixty-second session

Geneva, 25-28 September 2007

Item 6. of the provisional agenda

REGULATION No. 89 (Speed limitation device)

#### Proposal for a draft corrigendum to Regulation No. 89

Submitted by the expert from France

#### The text reproduced below was prepared by the expert from France to correct the current text of Regulation No. 89.  It is based on a document without a symbol (informal document No. GRRF-61-21), distributed during the sixty-first GRRF session (see report ECE/TRANS/WP.29/GRRF/61, para. 45).

The modifications to the current text of the Regulation are marked in bold characters.

A.	PROPOSAL

Annex 5, paragraph 1.1.4.2.2.3., correct to read:

"1.1.4.2.2.3.	the stabilized speed conditions specified in 1.4.2.3. paragraph 1.1.4.2.3. shall be attained within 10 s of first reaching Vstab;"

Annex 6, paragraph 1.5.4.1.1.3., correct to read:

"1.5.4.1.1.3.	the stabilized speed conditions specified in 1.5.4.1.1. paragraph 1.5.4.1.2. shall be attained within 10 s of first reaching Vstab;"

B.	JUSTIFICATION

Both amendments concern the correction of editorial mistakes:

1.	In the first case, the paragraph 1.4.2.3. does not exist at all.  The stabilized speed conditions are specified in paragraph 1.1.4.2.3.

2.	The second case is analogous to the first one:  Even if the mentioned paragraph 1.5.4.1.1. exists, the reference is not correct.  The stabilized speed conditions are specified in paragraph 1.5.4.1.2.

- - - - -