| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2009/129/Corr.2 6 October 2009 ENGLISH ONLY |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-forty-ninth session

Geneva, 10-13 November 2009

Item 4.2.38 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for the 02 series of amendments to Regulation No. 64

(Temporary-use spare wheels/tyres)

Submitted by the Working Party on Brakes and Running Gear (/

Corrigendum

The text reproduced below is the result of discussions by the Working Party on Brakes and Running Gear (GRRF) at its sixty-sixth session.  It refers to document ECE/TRANS/WP.29/2009/129 and was drafted by the chairman of GRRF.  It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

Annex 5

Paragraph 1.5., correct to read:

"1.5.	Accuracy of pressure measurement equipment

Pressure measurement equipment to be used for the tests contained in this annex shall be accurate to at least +/- 3kPa."

Paragraph 2.1., correct to read:

"2.1.	…..and tyre positions. All pressure measurements shall be carried out using the same test equipment."

Paragraphs 2.5.1. and 2.5.2., correct to read:

"2.5.1.	Procedure for the puncture test to verify the requirements of  paragraph 5.3.2. to this Regulation

Deflate one of the vehicle's tyres within 5 minutes of measuring the warm pressure as described in paragraph 2.4.3. above, until it is at Pwarm -20 per cent, or it is at a minimum pressure of 150 kPa, whichever is higher, namely Ptest. Following a stabilisation period of between 2 and 5 minutes the pressure Ptest shall be rechecked and adjusted if necessary.

2.5.2.	Procedure for the diffusion test to verify the requirements of  paragraph 5.3.3. to this Regulation

Deflate all four tyres within 5 minutes of measuring the warm pressure as described in paragraph 2.4.3. above, until the deflated tyres are at Pwarm – 20 per cent plus a further deflation of 7 kPa, namely Ptest. Following a stabilisation period of between 2 and 5 minutes the pressure Ptest shall be rechecked and adjusted if necessary."

Delete paragraph 2.5.3.

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.