| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/GRE/2009/12 16 January 2009 Original: ENGLISH ENGLISH AND FRENCH ONLY |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

Working Party on Lighting and Light-Signalling

Sixty-first session

Geneva, 30 March - 3 April 2009

Item 3(a) of the provisional agenda

REGULATION No. 37

(Filament lamps)

Proposal for Supplement 34 to the 03 series of amendments

Proposal for Corrigendum 1 to Revision 5 to Regulation No. 37

Submitted by the expert from the Working Party "Brussels 1952" (/

The text reproduced below was prepared by the expert from the Working Party "Brussels 1952" (GTB) in order to amend data on light source categories PS19W, PSY19W, PSR19W, PS24W, PSX24W, PSY24W and PSR24W.  The proposal is based on the current text of the Regulation including draft Supplement 32 to the 03 series of amendments.  The modifications to the current text of Regulation No. 37 are marked in bold characters.

A. 	PROPOSAL

Annex 1, Sheet P19W/2, footnote 4, amend to read:

"4/	For categories PS19W, PSY19W and PSR19W, dimensions may be checked with O-ring removed to assure the correct mounting during testing."

Annex 1, Sheet P24W/2, footnote 4, amend to read:

"4/	For categories PS24W, PSX24W, PSY24W and PSR24W, dimensions may be checked with O-ring removed to assure the correct mounting during testing."

B. 	JUSTIFICATION

The removal of the O-ring is to ascertain correct mounting of the light source during testing. However, for some test equipment it is preferred to keep the O-ring at its place.

- - - - -

# Footnotes

(/  In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.