| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/GRE/2009/61 14 July 2009 Original: ENGLISH ENGLISH AND FRENCH ONLY |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

Working Party on Lighting and Light-Signalling

Sixty-second session

Geneva, 6 - 9 October 2009

Item 3 of the provisional agenda

REGULATION No. 37

(Filament lamps)

Proposal for Supplement 35 to the 03 series of amendments to Regulation No. 37 (/

Submitted by the expert from the Working Party "Brussels 1952"

The text reproduced below was prepared by the expert from the Working Party "Brussels 1952" (GTB) in order to introduce into Regulation No. 37 the provisions for new categories of filament light sources PW13W, PW16W, PWY16W, PWR16W, PW19W, PWY19W, PWR19W, PW24W, PWY24W, and PWR24W.  The modifications to the existing text of the Regulation, including draft Supplement 34 to the 03 series of amendments, are marked in bold characters.

A. 	PROPOSAL

Annex 1,

The list of categories of filament lamps and their sheets, amend to read:

"

| Group 2: |  |  |  |
| --- | --- | --- | --- |
| Only for use in signalling lamps, cornering lamps, reversing lamps and rear registration plate lamps: |
|  | Category |  | Sheet number(s) |  |
|  | C5W |  | C5W/1 |  |

...

| … |  |  |  |  |
| --- | --- | --- | --- | --- |
|  | PSY24W |  | PSY24W/1 to 3 |  |
|  | PW13W |  | P13W/1 to 3 |  |
|  | PW16W |  | PC16W/1 to 3 |  |
|  | PWR16W |  | PC16W/1 to 3 |  |
|  | PWY16W |  | PC16W/1 to 3 |  |
|  | PW19W |  | P19W/1 to 3 |  |
|  | PWR19W |  | P19W/1 to 3 |  |
|  | PWY19W |  | P19W/1 to 3 |  |
|  | PW24W |  | P24W/1 to 3 |  |
|  | PWR24W |  | P24W/1 to 3 |  |
|  | PWY24W |  | P24W/1 to 3 |  |
|  | PY19W |  | PY19W/1 to 3 |  |
| … |  |  |  |  |

"

Sheets P13W/1 to P13W/3 (existing), replace by the new sheets P13W/1 to P13W/3, to read (see below):

Sheets PC16W/1 to PC16W/3 (existing), replace by the new sheets PC16W/1 to PC16W/3, to read (see below):

Sheets P19W/1 to P19W/3 (existing), replace by the new sheets P19W/1 to P19W/3, to read (see below):

Sheets P24W/1 to P24W/3 (existing), replace by the new sheets P24W/1 to P24W/3, to read (see below):

Sheet P13W/1

CATEGORIES P13W and PW13W

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament lamp

1/	The reference plane is defined by the meeting points of the cap-holder fit.

2/	No actual filament diameter restrictions apply but the objective is d max. = 1.0 mm.

3/	No opaque parts other than filament turns shall be located in the shaded area indicated in Figure 2. This applies to the rotational body within the angles (1 + (2.

Sheet P13W/2

CATEGORIES P13W and PW13W

| Dimensions in mm | Filament lamps of normal production | Standard filament lamp |
| --- | --- | --- |
| e 5/ | P13W | 25.0 4/ | 25.0 ( 0.25 |
|  | PW13W | 19.25 4/ | 19.25( 0.25 |
| f 5/ | 4.3 4/ | 4.3 ( 0.25 |
| (1 6/ | 30.0° min. | 30.0° min. |
| (2 6/ | 58.0° min. | 58.0° min. |
| P13W Cap PG18.5d-1 PW13W Cap WP3.3x14.5-7 | in accordance with IEC Publication 60061 (sheet 7004-147-1) in accordance with IEC Publication 60061 (sheet 7004-xxx-x) |
| ELECTRICAL AND PHOTOMETRIC CHARACTERISTICS |
| Rated values | Voltage | V | 12 | 12 |
|  | Wattage | W | 13 | 13 |
| Test voltage | V | 13.5 | 13.5 |
| Objective values | Wattage | W | 19 max. | 19 max. |
|  | Luminous flux | lm | 250 |  |
|  |  | ( | +15% / –20% |  |
| Reference luminous flux at approximately 13.5V | 250 lm |

4/	To be checked by means of a "Box-System"; sheet P13W/3.

5/	The ends of the filament are defined as the points where, when the viewing direction is perpendicular to the plane through the filament lead-in wires, the projection of the outside of the end turns crosses the filament axis.

6/	No part of the cap beyond the reference plane shall interfere with angle (2 as shown in Figure 1 on sheet P13W/1. The bulb shall be optically distortion free within the angles (1+ (2.
These requirements apply to the whole bulb circumference.

Sheet P13W/3

CATEGORIES P13W and PW13W

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament lamp complies with the requirements.

|  | p | q | u1,u2 | r,s | t,v |
| --- | --- | --- | --- | --- | --- |
| Filament lamps of normal production | 1.7 | 1.9 | 0.3 | 2.6 | 0.9 |
| Standard filament lamps | 1.5 | 1.7 | 0.25 | 2.45 | 0.6 |

The filament position is checked in two mutually perpendicular planes, one of them being the plane through the lead-in wires.

The ends of the filament as defined on sheet P13W/2, note 4/, shall lie between Z1 and Z2 and between the lines Z3 and Z4.

The filament shall lie entirely within the limits shown.

Sheet PC16W/1

CATEGORIES PC16W, PCY16W, PCR16W, PW16W, PWY16W and PWR16W

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament lamp

1/	The reference plane is defined by the meeting points of the cap-holder fit.

2/	No actual filament diameter restrictions apply but the objective is d max. = 1.1 mm.

3/	The light emitted from normal production lamps shall be white for category PC16W and PW16W; amber for category PCY16W and PWY16W; red for category PCR16W and PWR16W. 
(see also note 7/).

Sheet PC16W/2

CATEGORIES PC16W, PCY16W, PCR16W, PW16W, PWY16W and PWR16W

| Dimensions in mm | Filament lamps of normal production | Standard filament lamp |
| --- | --- | --- |
|  | min. | nom. | max. | 7/ |
| e 4/ 5/ | PC16W PCY16W PCR16W |  | 18.5 |  | 18.5 |
|  | PW16W PWY16W PWR16W |  | 17.1 |  | 17.1 |
| f 4/ 5/ |  | 4.0 |  | 4.0 ( 0.2 |
| α 6/ | 54° |  |  | 54° min. |
| PC16W Cap PU20d-1 PCY16W Cap PU20d-2 PCR16W Cap PU20d-7 | in accordance with IEC Publication 60061 (sheet 7004-157-1) |
| PW16W Cap WP3.3x14.5-8 PWY16W Cap WP3.3x14.5-9 PWR16W Cap WP3.3x14.5-10 | in accordance with IEC Publication 60061 (sheet 7004-XXX-X) |
| ELECTRICAL AND PHOTOMETRIC CHARACTERISTICS |
| Rated values | Volts | 12 | 12 |
|  | Watts | 16 | 16 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts |  | 17 max. | 17 max. |
|  | Luminousflux | PC16W PW16W | 300 ( 15 % |  |
|  |  | PCY16W PWY16W | 180 ( 20 % |  |
|  |  | PCR16W PWR16W | 70 ( 20 % |  |
| Reference luminous flux at approximately | 13.5 V | White: 300 lm Amber: 180 lm Red: 70 lm |

4/	The filament position is checked by means of a "Box-System"; sheet PC16W/3.

5/	The ends of the filament are defined as the points where, when the viewing direction is perpendicular to the plane through the filament lead-in wires as showed in the drawing on sheet PC16W/1, the projection of the outside of the end turns crosses the filament axis.

6/	No part of the cap beyond the reference plane shall interfere with angle (. The bulb shall be optically distortion free within the angle 2( + 180°.

7/	The light emitted from standard filament lamps shall be white for category PC16W and PW16W; white or amber for category PCY16W and PWY16W; white or red for category PCR16W and PWR16W.

Sheet PC16W/3

CATEGORIES PC16W, PCY16W, PCR16W, PW16W, PWY16W and PWR16W

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament lamp complies with the requirements.

| PC16W, PCY16W, PCR16W | a1 | a2 | b1, b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- |
| Filament lamps of normal production | 2.9 | 3.9 | 0.5 | 5.2 | 3.8 |
| Standard filament lamps | 1.5 | 1.7 | 0.25 | 4.7 | 3.8 |

| PW16W, PWY16W and PWR16W | a1 | a2 | b1, b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- |
| Filament lamps of normal production | 2.5 | 2.5 | 0.4 | 5.2 | 3.8 |
| Standard filament lamps | 1.5 | 1.7 | 0.25 | 4.7 | 3.8 |

The filament position is checked in two mutually perpendicular planes, one of them being the plane through the lead-in wires.

The ends of the filament as defined on sheet PC16W/2, note 5/, shall lie between Z1 and Z2 and between the lines Z3 and Z4.

The filament shall lie entirely within the limits shown.

Sheet P19W/1

CATEGORIES P19W, PY19W, PR19W, PS19W, PSY19W, PSR19W, PW19W, PWY19W and PWR19W

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament lamp

1/	The reference plane is defined by the meeting points of the cap-holder fit.

2/	No actual filament diameter restrictions apply but the objective is d max. = 1.1 mm.

3/	The light emitted from normal production lamps shall be white for categories P19W, PS19W and PW19W; amber for categories PY19W, PSY19W and PWY19W; red for categories PR19W, PSR19W and PWR19W. (see also note 8/).

Sheet P19W/2

CATEGORIES P19W, PY19W, PR19W, PS19W, PSY19W, PSR19W, PW19W, PWY19W and PWR19W

| Dimensions in mm 4/ | Filament lamps of normal production | Standard filament lamp |
| --- | --- | --- |
|  | min. | nom. | max. | 8/ |
| e 5/ 6/ | P19W, PS19W, PY19W, PSY19W, PR19W, PSR19W |  | 24.0 |  | 24.0 |
|  | PW19W PWY19W PWR19W |  | 18.1 |  | 18.1 |
| f 5/ 6/ |  | 4.0 |  | 4.0 ( 0.2 |
| α 7/ | 58° |  |  | 58° min. |
| P19W Cap PGU20-1 PY19W Cap PGU20-2 PR19W Cap PGU20-5 PS19W Cap PG20-1 PSY19W Cap PG20-2 PSR19W Cap PG20-5 | in accordance with IEC Publication 60061 (sheet 7004-127-2) |
| PW19W Cap WP3.3x14.5-1 PWY19W Cap WP3.3x14.5-2 PWR19W Cap WP3.3x14.5-5 | in accordance with IEC Publication 60061 (sheet 7004-xxx-x) |
| ELECTRICAL AND PHOTOMETRIC CHARACTERISTICS |
| Rated values | Volts | 12 | 12 |
|  | Watts | 19 | 19 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts |  | 20 max. | 20 max. |
|  | Luminous flux | P19W PS19W PW19W | 350 ( 15 % |  |
|  |  | PY19W PSY19W PWY19W | 215 ( 20 % |  |
|  |  | PR19W PSR19W PWR19W | 80 ( 20 % |  |
| Reference luminous flux at approximately 13.5 V | White: 350 lm Amber: 215 lm Red: 80 lm |

4/	For categories PS19W, PSY19W and PSR19W, dimensions shall be checked with O-ring removed.

5/	The filament position is checked by means of a "Box-System"; sheet P19W/3.

6/	The ends of the filament are defined as the points where, when the viewing direction is perpendicular to the plane through the filament lead-in wires as showed in the drawing on sheet P19W/1, the projection of the outside of the end turns crosses the filament axis.

7/	No part of the cap beyond the reference plane shall interfere with angle (. The bulb shall be optically distortion free within the angle 2( + 180°.

8/	The light emitted from standard filament lamps shall be white for categories P19W, PS19W and PW19W; white or amber for categories PY19W, PSY19W and PWY19W; white or red for categories PR19W, PSR19W and PWR19W.

Sheet P19W/3

CATEGORIES P19W, PY19W, PR19W, PS19W, PSY19W, PSR19W, PW19W, PWY19W and PWR19W

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament lamp complies with the requirements.

| P19W, PY19W, PR19W, PS19W, PSY19W, PSR19W | a1 | a2 | b1, b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- |
| Filament lamps of normal production | 2.9 | 3.9 | 0.5 | 5.2 | 3.8 |
| Standard filament lamps | 1.5 | 1.7 | 0.25 | 4.7 | 3.8 |

| PW19W, PWY19W and PWR19W | a1 | a2 | b1, b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- |
| Filament lamps of normal production | 2.5 | 2.5 | 0.4 | 5.2 | 3.8 |
| Standard filament lamps | 1.5 | 1.7 | 0.25 | 4.7 | 3.8 |

The filament position is checked in two mutually perpendicular planes, one of them being the plane through the lead-in wires.

The ends of the filament as defined on sheet P19W/2, note 6/, shall lie between Z1 and Z2 and between the lines Z3 and Z4.

The filament shall lie entirely within the limits shown.

Sheet P24W/1

CATEGORIES P24W, PX24W, PY24W, PR24W, PS24W, PSX24W, PSY24W, PSR24W, PW24W, PWY24W and PWR24W

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament lamp

1/	The reference plane is defined by the meeting points of the cap-holder fit.

2/	No actual filament diameter restrictions apply but the objective is d max. = 1.1 mm.

3/	The light emitted from normal production lamps shall be white for categories P24W, PX24W, PS24W, PSX24W and PW24W; amber for categories PY24W, PSY24W and PWY24W; red for categories PR24W, PSR24W and PWR24W.  (See also note 8/)

Sheet P24W/2

CATEGORIES P24W, PX24W, PY24W, PR24W, PS24W, PSX24W, PSY24W, PSR24W, PW24W, PWY24W and PWR24W

| Dimensions in mm 4/ | Filament lamps of normal production | Standard filament lamp |
| --- | --- | --- |
|  | min. | nom. | max. | 8/ |
| e 5/ 6/ | P24W, PY24W, PR24W, PS24W, PSY24W, PSR24W, PX24W, PSX24W |  | 24.0 |  | 24.0 |
|  | PW24W, PWY24W, PWR24W |  | 18.1 |  | 18.1 |
| f 5/,6/ | P24W, PY24W, PR24W, PS24W, PSY24W, PSR24W, PW24W, PWY24W, PWR24W |  | 4.0 |  | 4.0 |
|  | PX24W, PSX24W |  | 4.2 |  | 4.2 |
| ( 7/ | 58.0 ° |  |  | 58.0° min. |
| P24W Cap PGU20-3 PX24W Cap PGU20-7 PY24W Cap PGU20-4 PR24W Cap PGU20-6 PS24W Cap PG20-3 PSX24W Cap PG20-7 PSY24W Cap PG20-4 PSR24W Cap PG20-6 | in accordance with IEC Publication 60061 (sheet 7004-127-2) |
| PW24W Cap WP3.3x14.5-3 PWY24W Cap WP3.3x14.5-4 PWR24W Cap WP3.3x14.5-6 | in accordance with IEC Publication 60061 (sheet 7004-XXX-X) |
| ELECTRICAL AND PHOTOMETRIC CHARACTERISTICS |
| Rated values | Volts | 12 | 12 |
|  | Watts | 24 | 24 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts |  | 25 max. | 25 max. |
|  | Luminous Flux | P24W PS24W PW24W | 500 +10/-20 % |  |
|  |  | PX24W PSX24W | 500 +10/-15 % |  |
|  |  | PY24W PSY24W PWY24W | 300 +15/-25 % |  |
|  |  | PR24W PSR24W PWR24W | 115 +15/-25 % |  |
| Reference luminous flux at approximately | 12 V | White: 345 lm |
|  | 13.2 V | White: 465 lm |
|  | 13.5 V | White: 500 lm Amber: 300 lm Red: 115 lm |

4/	For categories PS24W, PSX24W, PSY24W and PSR24W, dimensions shall be checked with O-ring removed.

5/	The filament position is checked by means of a “box-system”; sheet P24W/3.

6/	The ends of the filament are defined as the points where, when the viewing direction is perpendicular to the plane through the filament lead-in wires as showed in the drawing on sheet P24W/1, the projection of the outside of the end turns crosses the filament axis.

7/	No part of the cap beyond the reference plane shall interfere with angle (. The bulb shall be optically distortion free within the angle 2( + 180°.

8/	The light emitted from standard filament lamps shall be white for categories P24W, PX24W, PS24W, PSX24W and PW24W; white or amber for categories PY24W, PSY24W and PWY24W; white or red for categories PR24W, PSR24W and PWR24W.

Sheet P24W/3

CATEGORIES P24W, PX24W, PY24W, PR24W, PS24W, PSX24W, PSY24W, PSR24W, PW24W, PWY24W and PWR24W

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament lamp complies with the requirements.

| P24W, PY24W, PR24W, PS24W, PSY24W, PSR24W | a1 | a2 | b1, b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- |
| Filament lamps of normal production | 2.9 | 3.9 | 0.5 | 5.2 | 3.8 |
| Standard filament lamps | 1.5 | 1.7 | 0.25 | 4.7 | 3.8 |

| PW24W, PWY24W, PWR24W | a1 | a2 | b1, b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- |
| Filament lamps of normal production | 2.5 | 2.5 | 0.4 | 5.0 | 3.8 |
| Standard filament lamps | 1.5 | 1.7 | 0.25 | 4.7 | 3.8 |

| PX24W, PSX24W | a1 | a2 | b1, b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- |
| Filament lamps of normal production | 1.9 | 1.9 | 0.35 | 5.0 | 4.0 |
| Standard filament lamps | 1.5 | 1.5 | 0.25 | 4.7 | 4.0 |

The filament position is checked in two mutually perpendicular planes, one of them being the plane through the lead-in wires.

The ends of the filament as defined on sheet P24W/2, note 6/, shall lie between Z1 and Z2 and between the lines Z3 and Z4.

The filament shall lie entirely within the limits shown.

B. JUSTIFICATION

Carmakers and set makers expressed the need for:

(a)	A simpler connectivity / mounting solution of the existing categories for light signalling of P13W and families Pxx16W, Pxx19W and Pxx24W;

(b)	Other interfaces than those specified so far by Regulation No. 37;

(c)	A simpler and more flexible cap/interface to enable carmaker/setmakers  in-house connector standards.

(d)	Accurate signalling light sources.

This proposal is to satisfy those needs.

These are all versions based on existing light source categories but with another (plastic wedge base) cap that is being standardized by IEC. As the cap will be mainly used with an adapter, the tolerances have been tightened to compensate for tolerances in the adapter.

OR

EXISTING		NEW

APPLICATION:

ETCETERA

- - - - - -

# Footnotes

(/  In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.

# Text boxes

##### Figure 3 – Main drawing PW13W

Ø16.6 max. max

Reference plane

##### Enlarged centre of View B

##### 40°

##### Figure 2 – Metal free zone 3/

##### Reference axis

##### Figure 1 – Main drawing P13W





##### Ø 16.6 max

##### 44.0 max

##### Reference plane 1/

##### Reference axis

##### e

##### f

##### 2/

##### View B

##### View A

##### e

##### 37.0 max

α1

α2

##### f

##### r

##### s

##### Reference axis

##### t

##### v

##### z4

##### z3

##### z2

##### z1

p

q

##### u1

##### u2

##### e

##### View A

PC16W, PCY16W, PCR16W

Reference plane 1/

e

28 max

Ø16.6 max. max

f



Reference axis

3/

2/

Reference axis

e

f

37.0 max

Ø16.6 max. max

α

PW16W, PWY16W, PWR16W

Reference plane

e

P19W, PY19W, PR19W,

PS19W, PSY19W, PSR19W

37 max

e

f

Reference axis

PW19W, PWY19W, PWR19W

Ø18.5 max. max

Reference plane

Reference plane

α

e

P24W,

PX24W,

PY24W, PR24W,

PS24W,

PSX24W,

PSY24W, PSR24W

Reference plane

37 max

PW24W, PWY24W, PWR24W

Reference axis

e

f

Ø18.5 max. max

α

e