|  | United Nations | ST/SG/AC.10/C.4/2010/6 |
| --- | --- | --- |
|  | Secretariat | Distr.: General 29 July 2010 English Original: English and French |

Committee of Experts on the Transport of Dangerous Goods
and on the Globally Harmonized System of Classification
and Labelling of Chemicals

Sub-Committee of Experts on the Globally Harmonized
System of Classification and Labelling of Chemicals

Twentieth session

Geneva, 7–9 December 2010

Item 2 (e) of the provisional agenda

Updating of the third revised edition of the Globally Harmonized System
of Classification and Labelling of Chemicals (GHS) – Miscellaneous proposals

Draft amendments to the third revised edition of the GHS adopted in principle by the Sub-Committee at its nineteenth session

Note by the secretariat

I. 	Background

1.	At its nineteenth session, the Sub-Committee examined several informal documents containing proposals for amendment to the third revised edition of the GHS. Noting that the amendment proposals were circulated as informal documents, the Sub-Committee agreed to adopt them in principle, pending their submission to the twentieth session in an official document for final endorsement (refer to the report of the Sub-Committee on its nineteenth session, document ST/SG/AC.10/C.4/38, paragraph 9).

2.	The proposed amendments to the third revised edition of the GHS, as adopted in principle by the Sub-Committee at its nineteenth session, are reproduced hereafter.

II. 	Draft amendments to the third revised edition of the GHS adopted in principle by the Sub-Committee at its nineteenth session

Chapter 2.1

2.1.2.1 (f)	Delete “detonating”

(Reference document: ST/SG/AC.10/C.4/38, paragraph 12)

Chapter 2.2

2.2.4.2	 and 2.2.5 (heading)	Replace “ISO 10156:1996” with “ISO 10156:2010”

(Reference document: ST/SG/AC.10/C.4/38, paragraphs 8 and 9)

Chapter 2.3

2.3.2.2 	In the note, replace “extremely flammable (Category 1)” with “flammable aerosols, Category 1”

(Reference document: ST/SG/AC.10/C.4/38, paragraph 10)

Chapter 2.4

2.4.1 		In the note, replace “ISO 10156:1996 or 10156-2:2005” with “ISO 10156:2010”

(Reference document: ST/SG/AC.10/C.4/38, paragraphs 8 and 9)

2.4.4.1		Replace “ISO 10156:1996” with “ISO 10156:2010” and delete “and ISO 10156-2:2005 “Gas cylinders, Gases and gas mixtures. Part 2: Determination of oxidizing ability of toxic and corrosive gases and gas mixtures”

(Reference document: ST/SG/AC.10/C.4/38, paragraphs 8 and 9)

2.4.4.2 	Replace with the following:

“2.4.4.2	Guidance

Example of the classification of an oxidizing gas mixture by calculation according to ISO 10156:2010.

The classification method described in ISO 10156 uses the criterion that a gas mixture should be considered as more oxidising than air if the oxidising power of the gas mixture is higher than 0.235 (23.5%).

The oxidizing power (OP) is calculated as follows:

Where:

xi	= 	molar fraction of the i:th oxidising gas in the mixture;

Ci	= 	coefficient of oxygen equivalency of the i:th oxidising gas in the mixture;

Kk	= 	coefficient of equivalency of the inert gas k compared to nitrogen;

Bk	=  	molar fraction of the k:th inert gas in the mixture;

= 	total number of oxidising gases in the mixture;

=  	total number of inert gases in the mixture;

Example mixture: 	9%(O2) + 16%(N2O) + 75%(He)

Calculation steps

Step 1:

Ascertain the coefficient of oxygen equivalency (Ci) for the oxidising gases in the mixture and the nitrogen equivalency factors (Kk) for the non-flammable, non-oxidising gases.

Ci (N2O)	=  0.6 (nitrous oxide)

Ci (O2)	= 1 (oxygen)

Kk (He)	= 0.9 (helium)

Step 2:

Calculate the oxidising power of the gas mixture

20.1 < 23.5

Therefore the mixture is not considered as an oxidising gas”.

(Reference document: ST/SG/AC.10/C.4/38, paragraphs 8 and 9)

Chapter 2.5

2.5.1		In the definition of gases under pressure, insert “at 20°C” after “or more”

(Reference document: ST/SG/AC.10/C.4/38, paragraphs 23 and 24)

2.5.2		In the introductory sentence before table 2.5.1, replace “Gases” with “Gases under pressure”.

(Reference document: ST/SG/AC.10/C.4/38, paragraphs 23 and 24)

2.5.4.1		Replace with the following:

“2.5.4.1	Decision logic

Classification can be made according to decision logic 2.5

Decision logic 2.5 for gases under pressure

”

(Reference document: ST/SG/AC.10/C.4/38, paragraphs 23 and 24)

# Footnotes

In accordance with the report of the Sub-Committee of experts on its nineteenth session (see ST/SG/AC.10/C.4/38, paragraphs 8–10, 12, 23 and 24).

# Text boxes

Yes

Yes

(High pressure)

Liquefied gas

Warning

Yes

Yes

Is the gas partially liquid 
at temperatures above – 50°C?

Yes

Yes

Yes

No

Not classified as a gas under pressure

Is the gas contained in a receptacle at a pressure of 200 kPa (gauge) or more at 20°C, 
or is the gas liquefied or liquefied and refrigerated?

No

The substance or mixture is a gas

Is the gas dissolved in a liquid phase solvent?

Is its critical temperature between –50 °C and +65 (C?

Compressed gas

Warning

Refrigerated 
liquefied gas

Warning

(Low pressure)

Liquefied gas

Warning

No

Is the gas entirely in gaseous state at –50 (C

No

Is the gas partially liquid because of its low temperature?

Is its critical temperature above +65 °C?

No

Dissolved gas

Warning