| UN/SCEGHS/20/INF.16 UN/SCETDG/38/INF.20 |
| --- |
| Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals 24 November 2010 |
| Sub-Committee of Experts on the Transport of Dangerous Goods | Sub-Committee of Experts on the Globally Harmonized System of Classification and Labelling of Chemicals |
| Thirty-eight session | Twentieth session |
| Geneva, 29 November–7 December 2010 Item 11 of the provisional agenda Issues relating to the Globally Harmonized System of Classification and Labelling of Chemicals (GHS) | Geneva, 7–9 December 2010 Item 2 (a) of the provisional agenda Updating of the third revised edition of the Globally Harmonized System of Classification and Labelling of Chemicals (GHS): Physical hazards |

Amendment to the tables with concentration limits for chemically unstable gases in ST/SG/AC.10/C.3/2010/70 – ST/SG/AC.10/C.4/2010/10

Transmitted by the expert from Germany on behalf of the informal working group

Introduction

1.	As indicated in Table 3x.1 in document ST/SG/AC.10/C.3/2010/70 – ST/SG/AC.10/C.4/2010/10 the specific concentration limit for ethylene oxide is supposed to be amended before the December meeting.

2.	In addition, in Table 3x.2 one further value can be added for mixtures of acetylene and methane.

3.	The amended values of the tables are given in the following proposal. Changes compared to the tables in document ST/SG/AC.10/C.3/2010/70 – ST/SG/AC.10/C.4/2010/10 are in red and underlined.

Proposal

4.	Replace the row for ethylene oxide in Table 3x.1 in document ST/SG/AC.10/C.3/2010/70 – ST/SG/AC.10/C.4/2010/10 by the following:

Table 3x.1: 	Information about gases with regard to their chemical instability and concentration limits for their mixtures below which the mixtures are not classified as chemically unstable

| Information about the pure gas | Information about its mixtures |
| --- | --- |
| Chemical Name | Molecular formula | CAS No | UN No | Classification | Specific concentration limit (see Notes 1 and 2) |
| Ethylene oxide | C2H4O | 75-21-8 | 1040 | Chem. Unst. Cat. 1 | 15 mole% for mixtures containing rare gases 30 mole% for other mixtures |

5.	Replace the row for a 3 mole% concentration limit of acetylene in Table 3x.2 in document ST/SG/AC.10/C.3/2010/70 – ST/SG/AC.10/C.4/2010/10 by the following:

Table 3x.2: 	Specific concentration limits for binary mixtures with acetylene. These concentration limits may also be applied to butyne-1 (ethylacetylene), propadiene and propyne

| Concentration limit for acetylene in mol % | Maximum (filling) pressure in bar for a mixture with |
| --- | --- |
|  | N2 | CO2 | NH3 | H2 | CH4 | C3H8 | C2H4 |
| 3.0 | 200.0 |  |  |  | 200.0 |  |  |